## Slide 1: Impact of Acknowledgements on Application Performance in 4G LTE Networks
Master’s Thesis Presentation
Brett Levasseur
Advisors
Mark Claypool, Robert Kinicki
Reader
Emanuel Agu

## Slide 2: Network Growth
Worldwide Mobile networks in 2013
  ½ billion mobile devices added
  77% of this growth from smartphones
  Mobile data traffic grew 81%
  Mobile video traffic 51% of all mobile data
4G in 2013
  2.9% of all connections
  Account for 30% of all mobile traffic
  Predicted to be ½ of all connections in 2018
[Cisco 13]

## Slide 3: 4G Long Term Evolution (LTE)
Long Term Evolution (LTE) – Standard created by the 3rd Generation Partnership Project
  Deployed globally
  All packet switched network
  High throughput and QoS considerations
  Provides wireless retransmissions of lost data

## Slide 4: Wireless Loss and LTE
LTE responds to poor signal quality by decreasing throughput
  Retransmissions
LTE has multiple configuration parameters for wireless retransmissions
  E.g. 1 or 2 layers of retransmissions
Network providers may not choose optimum settings
Application developers have no knowledge on LTE retransmissions

## Slide 5: General Problem Statement
How do LTE retransmissions impact application performance?
What LTE retransmissions settings impact application performance?
Which LTE retransmission policies are preferred in different wireless loss conditions?

## Slide 6: Outline
Introduction
Background
  LTE
  ns-3
Related Work
Approach
Results
Conclusion

## Slide 7: LTE Network
Packet Delivery Network Gateway (PGW)
  Connects LTE network to IP networks
Serving Gateway (SGW)
  Route packets to and from wireless access points
Enhanced Node B (eNodeB)
  Wireless access point
User Equipment (UE)
  End user devices

## Slide 8: LTE Network Layers
LTE wireless network has 6 layers (not all shown)
PHY – RLC layers carry user and network control data
LTE transmits collections of Physical Resource Blocks (PRB)s in transport blocks
Application
TCP
UDP
IP
RLC
MAC
PHY

## Slide 9: Channel Quality Indictor (CQI)
UEs send CQI to notify received signal quality
  Maps to modulation and encoding schemes (MCS)
  MCS and PRBs determine transport block size

## Slide 10: LTE Retransmissions: MAC
  Hybrid Automatic Request Reply (HARQ)
Data sent at time n, arrives at time n
3ms taken to check if data arrived with errors
n+4 ACK/NACK sent back
n+8 if NACK, data can be retransmitted
  Up to 3 retransmissions for downlink traffic
[Dahlman 11]
1ms TTI

## Slide 11: LTE Retransmissions: RLC
Unacknowledged Mode (UM) receive window
  VR(UR) – Lower bound
  VR(UH) – Highest received SN + 1
  VR(UX) – Reordering SN
Acknowledged Mode (AM) receive window
  VR(R) – Lower bound
  VR(H) – Highest received SN + 1
  VR(X) – Reordering SN
  VR(MS) – Highest SN to ACK
  VR(MR) – Upper bound

## Slide 12: RLC UM
Receiving window used for reordering PDUs
Out of order PDU trigger timer t-Reordering
0
1
2
3
4
5
6
VR(UR),VR(UH)
0
1
2
3
4
5
6
VR(UR)
VR(UX),VR(UH)

## Slide 13: Timer t-Reordering UM
Timer runs when PDUs arrive out of order
Gives MAC layer chance to recover lost data
Expiration moves VR(UR) up to first SN >= VR(UX) that is not received
Tradeoffs
  Small timer, MAC retransmissions lost
  Large timer, keeps lower bound of window stalled
0
1
2
3
4
5
6
VR(UR)
VR(UX),VR(UH)
0
1
2
3
4
5
6
VR(UR),VR(UH)
LOST
0
1
2
3
4
5
6
VR(UR),VR(UH)
Recovered

## Slide 14: RLC AM
Receiving window used for reordering and ACK/NACK messaging
0
1
2
3
4
5
6
VR(R),VR(H),VR(MS)
0
1
2
3
4
5
6
VR(R),VR(MS)
VR(X),VR(H)

## Slide 15: Timer t-Reordering AM
Gives MAC layer time before NACKing
t-Reordering starts when SN 5 arrives
  ACK = 3
While running SN 4 arrives
  ACK = 3
When timer expires VR(MS) is updated
  ACK = 6, NACK = 3
Tradeoffs
  Small timer, NACK data that MAC can recover
  Large timer, stalls NACKs
0
1
2
3
4
5
6
VR(R),VR(MS)
VR(X),VR(H)
0
1
2
3
4
5
6
VR(H),VR(MS)
0
1
2
3
4
5
6
VR(X),VR(H)
VR(R),VR(MS)
VR(R)

## Slide 16: RLC AM STATUS
Control message for sending ACKs/NACKs between UEs and eNodeBs
Sender polls for STATUS messages
[LTE RLC]

## Slide 17: Timer t-StatusProhibit
Receiver side timer
  Stops receiver from sending STATUS messages
  Timer started when STATUS message sent
  All poll requests collapsed to one STATUS sent when timer expires
Trade off
  Small timer could send many STATUS messages
  Large timer delays sending ACKs and NACKs

## Slide 18: Outline
Introduction
Background
  LTE
  ns-3
Related Work
Approach
Results
Conclusion

## Slide 19: ns-3
Open source packet level network simulator
Successor to ns-2
Funded by National Science Foundation and the Planete group at INRIA Sophia Antipolis
2009 - 2012 ns-3 downloaded 50,792 times
As of version 3.16 there were 113 listed authors and 25 maintainers
[ns-3]
[ns-3 stats]

## Slide 20: LTE-EPC Network Simulator Module
LTE/EPC Network Simulator (LENA)
Developed Centre Tecnologic de Telecomunicacions de Catalunya
Allows simulations with LTE networks in ns-3
  Part of the main ns-3 branch
Still under active development
[Baldo 11]

## Slide 21: Outline
Introduction
Background
  LTE
  ns-3
Related Work
Approach
Results
Conclusion

## Slide 22: Related Work
Applications Used
  Böhmer et al. – Mobile apps mostly used for communication
  Huang et al. – Majority of data over LTE uses TCP
HARQ
  Kawser et al. – Limit MAC retransmissions to 3 or less
RLC AM
  Makidis – Examined TCP with RLC AM
[Böhmer 11]
[Huang 13]
[Makidis 07]
[Kawser 12]

## Slide 23: Outline
Introduction
Background
  LTE
  ns-3
Related Work
Approach
Results
Conclusion

## Slide 24: Specific Problem Statement
How do MAC and RLC layer retransmission impact VoIP, FTP, Video
  Delay/Loss/Throughput sensitive
How does adjusting RLC timer settings impact retransmissions and application performance
When is it better to use RLC AM or UM with varying loss rates at physical layer

## Slide 25: ns-3 LTE Modifications
LTE module for ns-3 did not support NACKs in AM STATUS message
Joined discussion forum to implement NACKs
  Worked with LTE module developers and others
  Provided code for (de-)serializing NACKs to developers
  Discussed specifics of AM receive window for NACKs with developers
  Helped LTE model developers test changes
[ns-3 Forum]

## Slide 26: Simulator Additions
Confirmed NACK read/write works
Modified how NACKs are selected
  Found and corrected errors on when AM window variables were updated
  Tests show AM recovers all lost PDUs

## Slide 27: Simulating VoIP
ns-3 example code for application that sends data at a specified rate
Use G.711 encoding format to define size of packets and sending rate
  160 bytes data, 12 bytes RTP header, 8 bytes UDP header, 20 bytes IP header
  Sending rate 64Kbps or about 1 packet every 20ms
Mean Opinion Score (MOS) used as performance metric
  1 – 5 point scale, 1 worst, 5 best
  Calculated from delay and loss using E-Model
[ITU G.711]
[E-Model]

## Slide 28: Simulating FTP
ns-3 bulk send application
  Transmits as much data as possible over TCP
  Default ns-3 congestion control algorithm is NewReno
Throughput used as performance metric

## Slide 29: Simulating MPEG
ns-3 MPEG trace file application
  Reads a file of MPEG frame sizes and times to transmit
  Sends frames in UDP packets
Compatible video trace files from the Telecommunication Network Group at Technische Universität Berlin
Selected video of soccer match
Frame rate used as performance metric
[MPEG Trace]

## Slide 30: Simulation Network
Server sends data to UE
Wireless link bottleneck
UE stationary
No obstructions or noise sources
UE positioned so it would request CQI 8

## Slide 31: CQI Choice
Wrote Android application to log requested CQI value on LTE networks
Collected data over 1 week from Feb – March 2014
Average CQI requested was 8

## Slide 32: Wireless Loss
LTE simulator allows fading trace files to impose SINR
  File is a matrix of TTI, PRB number and SINR
If fading trace SINR is too high any data in that PRB sent in that TTI is lost
Gilbert-Elliot model used to set which TTIs have loss
  Bursty Loss

## Slide 33: Wireless Loss Cont
Creating fading loss file
  Run previous equations for state transitions
  Run Gilbert model

## Slide 34: RLC Settings
Test adjusting t-Reordering and t-StatusProhibit timers
Settings suggested in LTE specification
Subset of these suggested values are used for testing
t-Reordering | 0 ms, 5, 10, 15, 20, 25, 30, 35, 40, 45, 50, 55, 60, 65, 70, 75, 80, 85, 90, 95, 100, 110, 120, 130, 140, 150, 160, 170, 180, 190, 200
t-StatusProhibit | 0 ms, 5, 10, 15, 20, 25, 30, 35, 40, 45, 50, 55, 60, 65, 70, 75, 80, 85, 90, 95 100, 105, 110, 115, 120, 125, 130, 135, 140, 145, 150, 155, 160, 165, 170, 175, 180, 185, 190, 195, 200, 205, 210, 215, 220, 225, 230, 235, 240, 245, 250, 300, 350, 400, 450, 500
[LTE RRC]

## Slide 35: Outline
Introduction
Background
  LTE
  ns-3
Related Work
Approach
Results
Conclusion

## Slide 36: VoIP t-Reordering
Adjusting t-Reordering has little impact on delay
  AM experiences more delay but not by much
AM
UM

## Slide 37: VoIP t-Reordering
Adjusting t-Reordering has little impact on MOS
  Worst MOS is still good across all settings
Fix t-Reordering = 30ms
AM
UM

## Slide 38: VoIP t-StatusProhibit
Adjusting t-StatusProhibit has greater impact
Lower values for timer better than higher in general
Fix t-StatusProhibit = 50ms

## Slide 39: VoIP AM vs UM
Adjusted loss percent
VoIP over AM outperforms VoIP over UM until 20% loss
  Same for both Atlantic and Pacific test

## Slide 40: FTP t-Reordering
AM outperforms UM across t-Reordering
Large error ranges due to TCP RTO
Fix t-Reordering = 50ms
AM
UM

## Slide 41: FTP t-StatusProhibit
Lower values for t-StatusProhibit are better
Large error ranges from TCP RTOs
Fix t-StatusProhibit = 75ms

## Slide 42: FTP AM vs UM
FTP over AM has higher average throughput than FTP over UM
UM briefly better at 10% loss but has higher error range
  Input gap lengths up to 30 for 5 – 25% and up to 100 for 30 – 50%

## Slide 43: MPEG t-Reordering
Adjusting t-Reordering has little impact on frame rate
  Exception is additional frames recovered in UM
Fix t-Reordering = 30ms
AM
UM

## Slide 44: MPEG t-StatusProhibit
Lower values for t-StatusProhibit produce less variation
  Large error ranges from RLC retransmissions
Fix t-StatusProhibit = 75ms

## Slide 45: MPEG AM vs UM
AM – Higher average frame rate
UM – Lower average frame rate

## Slide 46: MPEG AM vs UM
AM – Out of order frames delayed by retransmissions
UM – Lower average delay but more frames lost

## Slide 47: Conclusion
Added RLC AM NACKs to ns-3 LTE simulator
VoIP over AM has higher MOS until 20% loss
  5 – 20% loss rate AM avg 4.26, UM avg 4.15
  25 – 35% loss rate AM avg 1.82, UM avg 3.7
FTP over AM has higher average throughput
  AM average throughput 1.21Mb/s, UM 0.83 Mb/s
Video over AM has higher delay, UM lower average frame rate
  AM avg 25 frames per sec, UM avg 21
  UM frame delay avg 29 ms, AM avg 95 ms

## Slide 48: Future Work
Video simulations with TCP
Test with other RLC layer settings
  t-PollRetransmit timer
  PollPDU and pollByte
Add support for RLC AM maximum retransmission radio link layer failure

## Slide 49: Questions
Impact of Acknowledgements on Application Performance in 4G LTE Networks
Master’s Thesis Presentation
Brett Levasseur
Advisors
Mark Claypool, Robert Kinicki
Reader
Emanuel Agu

## Slide 50: References
[LTE RLC] 3GPP. 3rd Generation Partnership Project; Technical Specification Group Radio Access Network; Evolved Universal Terrestrial Radio Access (E-UTRA); Radio Link Control (RLC) protocol specification (Release 8). Technical Specification 36.322v8.0.0, 3GPP, December 2007. http://www.3gpp.org/ftp/Specs/html-info/36322.htm.
[LTE RRC] 3GPP. 3rd Generation Partnership Project; Technical Specification Group Radio Access Network; Evolved Universal Terrestrial Radio Access (E-UTRA); Radio Resource Control (RRC) Protocol specication (Release 8). Technical Specication 36.331v8.10.0, 3GPP, march 2008. http://www.3gpp.org/ftp/Specs/html-info/36331.htm.
[Cisco 13] Cisco. Cisco Visual Networking Index: Global Mobile Data Traffic Forecast Update, 2013-2018. Technical report, Cisco, 2014. http://www.cisco.com/en/US/solutions/collateral/ns341/ns525/ns537/ns705/ns827/white paper c11-520862.pdf
[Dahlman 11] Erik Dahlman, Stefan Parkvall, and Johan Skold. 4G LTE/LTE-Advanced for Mobile Broadband. Academic Press, Oxford, 2011.
[Zyren 07] Jim Zyren. Overveiw of the 3GPP Long Term Evolution Physical Layer. Technical report, Freescale Semiconductor, 07 2007.
[ns-3] https://www.nsnam.org/
[ns-3 stats] https://www.nsnam.org/overview/statistics/
[Baldo 11] Nicola Baldo, Marco Miozzo, Manuel Requena-Esteso, and Jaume Nin-Guerrero. An open source product-oriented lte network simulator based on ns-3. In Proceedings of the 14th ACM International Conference on Modeling, Analysis and Simulation of Wireless and Mobile Systems, MSWiM '11, pages 293{298, New York, NY, USA, 2011. ACM.
[ITU G.711] International Telecommunication Union. Pulse Code Movulation (PCM) of Vlice Frequencies. Technical Specification G.711, ITU-T, November 1988. https://www.itu.int/rec/dologin pub.asp?lang=e&id=T-REC-G.711-198811-I!!PDFE& type=items.
[MPEG Trace] http://www-tkn.ee.tu-berlin.de/research/trace/trace.html
[Gordo 10] N Gordo and A Daniel. Evaluating video quality degradation from data packet losses in an lte environment, 2010.
[Verizon] Verizon. IP Lagency Sstatistics, April 2014. http://www.verizonenterprise.com/about/network/latency/.

## Slide 51: References Cont
[ns-3 Forum] https://groups.google.com/forum/#!topic/ns-3-users/CEfmMX3IRBw
[E-Model] Leandro Carvalho, Edjair Mota, Regeane Aguiar, Ana F Lima, Jose Neuman de Souza, and Anderson Barreto. An E-model implementation for speech quality evaluation in VoIP systems. In Proceedings of the 10th IEEE Symposium on Computers and Communications, volume 154. IEEE Computer Society, 2005.
[Böhmer 11] Matthias Böhmer, Brent Hecht, Johannes Schoning, Antonio Kruger, and Gernot Bauer. Falling asleep with angry birds, facebook and kindle: a large scale study on mobile application usage. In Proceedings of the 13th International Conference on Human Computer Interaction with Mobile Devices and Services, pages 47{56. ACM, 2011.
[Huang 13] Junxian Huang, Feng Qian, Yihua Guo, Yuanyuan Zhou, Qiang Xu, Z. Morley Mao, Subhabrata Sen, and Oliver Spatscheck. An In-depth Study of LTE: Eect of Network Protocol and Application Behavior on Performance. In Proceedings of the ACM SIG-COMM 2013 Conference on SIGCOMM, SIGCOMM '13, pages 363{374, New York, NY, USA, 2013. ACM.
[Makidis 07] Michael Makidis. Implementing and evaluating the RLC/AM protocol of the 3GPP specification. Master's thesis, Athens University of Economics and Business, 2007.
[Kawser 12] T. Mohammad Kawser, Nax Imtiaz Bin Hamid, Nayeemul Hasan, M. Shah Alam, and M. Musqur Rahman. Limiting HARQ Retransmissions in Downlink for Poor Radio Link in LTE. International Journal of Information and Electronics Engineering, 2012.

## Slide 52: Backup Slides

## Slide 53: MPEG t-Reordering
Video over UM outperforms video over AM across t-Reordering
Fix t-Reordering = 30ms
AM
UM

## Slide 54: MPEG t-StatusProhibit
Lower values for t-StatusProhibit are better
Large error ranges from RLC retransmissions
Fix t-StatusProhibit = 75ms

## Slide 55: Loss Shape
30% loss performs better for AM than 25%

## Slide 56: Gilbert-Elliot Model
Two state machine for loss
  X = 0 no loss
  X = 1 loss
Transition probabilities define when to change states

## Slide 57: Transitions
Gordo et al. shows how to take input of loss gaps and determine state transitions
  Ok – # of burst losses of length k
  a - # of TTIs
  d - # of lost TTIs
[Gordo 10]

## Slide 58: HARQ
MAC layer fixes blocks with known errors

## Slide 59: RLC UM
Maintains transmission & reception buffers
Segmentation & concatenation of RLC SDUs
Reorder of PDUs
Retransmissions still occur in MAC layer

## Slide 60: RLC AM
Maintains transmission, retransmission & reception buffers
Segmentation & concatenation of RLC SDUs
Reorder of PDUs
Sliding window for PDUs sent/received
Max retransmission threshold

## Slide 61: Simulation Settings
Physical
  Tx Power
  Noise
  Mobility
RLC
  AM
  UM
Applications
  Protocols
  App types

## Slide 62: Traffic Separation & Frame Structure
Time Division Duplexing (TDD)
Frequency Division Duplexing (FDD)
Generic Frame Structure for FDD
Notes: LTE Frames are 10 msec in duration. They are divided into 10 sub-frames, each of 1 msec. Each sub-frame is divided into two slots of 0.5 msec. Slots have either 6 or 7 OFDM symbols, depending on the cycle prefix used.
Symbol = waveform so symbol rate is waveform changes per unit of time.
A symbol can have 1 or more bits.

## Slide 63: Downlink Multiplexing
Orthogonal Frequency Division Multiple Access (OFDMA)
  User allocated Physical Resource Blocks (PRBs) or subcarriers for predetermined time
  Total subcarriers depends on bandwidth
Bandwidth (MHz) | 1.4 | 3.0 | 5.0 |  | 10.0 | 15.0 | 20.0
Subcarrier bandwidth (kHz) | 15 |  |  |  |  |  | 
PRB bandwidth (kHz) | 180 |  |  |  |  |  | 
# of available PRBs | 6 | 15 |  | 25 | 50 | 75 | 100
Notes: Orthogonal Frequency Division Multiple Access (OFDMA) downlink
PRB allocation is handled by scheduling function at eNodeB
LTE frame is 10 msec in duration, divided into 10 subframes of 1 msec and each subframe is divided into 2 slots of 0.5 msec. Slots have 6 to 7 OFDM symbols
OFDM supports
QPSK (4QAM) = 2 bits per symbol
16QAM = 4 bits per symbol
64QAM = 6 bits per symbol

## Slide 64: Downlink Resource Grid
PRB 0
PRB 0
PRB 1
PRB 1
PRB X
PRB X
Frequency
Time
1 ms
0.5 ms
Slot 1
Slot 2
12 sub
carriers
Notes: Instead of PHY preamble special reference symbols are embedded in the PRB (physical resource block)
Each box is one OFDM symbol on one subcarrier
  PRB uses 12 consecutive subcarriers per slot (0.5 msec)
  MIMO apps have one resource grid per transmitting antenna

## Slide 65: Transport Block Size
TB
TB
TB
TB
TB
TB
TB
TB
TB
TB
1 Frame (10 msec)
1 Transport Block (1 msec)
PRB
PRB
…
1 – 100 possible PRBs per slot depending on available frequencies
Depending on modulation and number of PRBs the total size of 1 Transport Block can be from:
16 – 75,376 bits
PRB
PRB
…
Slot (0.5msec)

## Slide 66: SDUs & PDUs
Notes: Service Data Units (SDUs)
Protocol Data Units (PDUs)
These terms can be misleading if you do not realize that the MAC, RLC and PDCP layers have their own PDUs and SDUs. One layers SDU is the higher layers PDU and one layers PDU is the lower layers SDU.
PDCP – One to one mapping of SDUs to PDUs
RLC – SUDs are stuffed into PDUs or PDUs are padded for single SDUs depending on SDU and Transport Block size
MAC – One to one mapping of SDUs to PDUs

## Slide 67: LTE
Long Term Evolution – Standard of wireless communication of high-speed data for mobile equipment
ITU lowered original 4G criteria for LTE and WIMAX
Standard Organization | 3GPP
Uplink Speed (theoretical) | 50 Mbit/s
Downlink Speed (theoretical) | 100 Mbit/s
Bandwidth Range | 1.4 MHz – 20 MHz
Based On | GSM/EDGE and UMTS/HSPA
Notes: ITU = International Telecommunication Union
3GPP = 3rd Generation Partnership Project

## Slide 68: Multipath Handling
Orthogonal Frequency Division Multiplexing (OFDM)
  Transmits data in parallel streams
  Symbol preceded by cyclic prefix (CP)
  Overlap of multiple paths occur in the CP
Notes: Orthogonal Frequency Division Multiplexing (OFDM)
OFDM systems break the available bandwidth into many narrower sub-carriers and transmit the data in parallel streams. Each subcarrier is modulated using varying levels of QAM modulation, e.g. QPSK, QAM, 64QAM or possibly higher orders depending on signal quality. Each OFDM symbol is therefore a linear combination of the instantaneous signals on each of the subcarriers in the channel.