## Slide 1: Impact of Acknowledgements on Application Performance in 4G LTE Networks
Brett Levasseur
Mark Claypool, Robert Kinicki
ICNC 2015
2/16/2015

## Slide 2: Network Growth
Worldwide Mobile networks in 2013
  ½ billion mobile devices added
  77% of this growth from smartphones
  Mobile data traffic grew 81%
  Mobile video traffic 51% of all mobile data
4G in 2013
  2.9% of all connections
  Account for 30% of all mobile traffic
  Predicted to be ½ of all connections in 2018
[Cisco 13]

## Slide 3: General Problem Statement
LTE responds to poor signal quality by decreasing throughput
LTE has multiple configuration parameters for wireless retransmissions
How do LTE retransmissions impact application performance?
What LTE retransmissions settings impact application performance?
Which LTE retransmission policies are preferred in different wireless loss conditions?

## Slide 4: Outline
Introduction
Background
Approach
Results
Conclusion

## Slide 5: LTE Retransmissions: MAC
[Dahlman 11]
1ms TTI
Hybrid Automatic Request Reply (HARQ)
Data sent at time n, arrives at time n
3ms taken to check if data arrived with errors
n+4 ACK/NACK sent back
n+8 if NACK, data can be retransmitted
  Up to 3 retransmissions for downlink traffic

## Slide 6: LTE Retransmissions: RLC
Unacknowledged Mode
  No retransmissions
  Timer t-Reordering – wait before handing data up a layer for MAC layer to try recovery
Acknowledged Mode
  Retransmissions
  Timer t-Reordering – wait before requesting retransmission
  Timer t-StatusProhibit – wait before sending RLC ACK/NACK message

## Slide 7: ns-3
Open source packet level network simulator
Successor to ns-2
Funded by National Science Foundation and the Planete group at INRIA Sophia Antipolis
2009 - 2012 ns-3 downloaded 50,792 times
LTE/EPC Network Simulator (LENA)
Developed Centre Tecnologic de Telecomunicacions de Catalunya
[ns-3]
[ns-3 stats]
[Baldo 11]

## Slide 8: Related Work
Applications used in mobile networks
  Böhmer et al. – Mobile apps mostly used for communication
  Huang et al. – Majority of data over LTE uses TCP
HARQ
  Kawser et al. – Found that MAC retransmissions could be limited to 3 or less as allowing more in poor signal quality conditions did not improve reception
RLC AM
  Makidis – Examined TCP with RLC AM for VoIP and FTP but did not examine UM or MAC layer retransmissions

## Slide 9: Outline
Introduction
Background
Approach
Results
Conclusion

## Slide 10: Specific Problem Statement
How do MAC and RLC layer retransmission impact VoIP, FTP, Video
  Delay/Loss/Throughput sensitive
How does adjusting RLC timer settings impact retransmissions and application performance
When is it better to use RLC AM or UM with varying loss rates at physical layer

## Slide 11: ns-3 LTE Modifications
LTE module for ns-3 did not support NACKs in AM STATUS message
Joined discussion forum to implement NACKs
  Worked with LTE module developers and others
  Provided code for (de-)serializing NACKs to developers
  Discussed specifics of AM receive window for NACKs with developers
  Helped LTE model developers test changes
[ns-3 Forum]

## Slide 12: Simulation Network
Server sends data to UE
Wireless link bottleneck
UE stationary
No obstructions or noise sources
UE positioned so it would request CQI 8

## Slide 13: Outline
Introduction
Background
  LTE
  ns-3
Related Work
Approach
Results
Conclusion

## Slide 14: VoIP t-Reordering
Adjusting t-Reordering has little impact on delay
  AM experiences more delay but not by much
AM
UM

## Slide 15: VoIP t-Reordering
Adjusting t-Reordering has little impact on MOS
  Worst MOS is still good across all settings
Fix t-Reordering = 30ms
AM
UM

## Slide 16: VoIP t-StatusProhibit
Adjusting t-StatusProhibit has greater impact
Lower values for timer better than higher in general
Fix t-StatusProhibit = 50ms
AM
AM

## Slide 17: VoIP AM vs UM
Adjusted loss percent
VoIP over AM outperforms VoIP over UM until 20% loss
  Same for both Atlantic and Pacific test

## Slide 18: FTP t-Reordering
AM outperforms UM across t-Reordering
Large error ranges due to TCP RTO
Fix t-Reordering = 50ms
AM
UM

## Slide 19: FTP t-StatusProhibit
Lower values for t-StatusProhibit are better
Large error ranges from TCP RTOs
Fix t-StatusProhibit = 75ms
AM

## Slide 20: FTP AM vs UM
FTP over AM has higher average throughput than FTP over UM
UM briefly better at 10% loss but has higher error range
  Input gap lengths up to 30 for 5 – 25% and up to 100 for 30 – 50%

## Slide 21: Conclusion
Added RLC AM NACKs to ns-3 LTE simulator
VoIP over AM has higher MOS until 20% loss
  5 – 20% loss rate AM avg 4.26, UM avg 4.15
  25 – 35% loss rate AM avg 1.82, UM avg 3.7
FTP over AM has higher average throughput
  AM average throughput 1.21Mb/s, UM 0.83 Mb/s

## Slide 22: Future Work
Video simulations with TCP
Test with other RLC layer settings
  t-PollRetransmit timer
  PollPDU and pollByte
Add support for RLC AM maximum retransmission radio link layer failure

## Slide 23: Questions
Brett Levasseur
Mark Claypool, Robert Kinicki
ICNC 2015
Impact of Acknowledgements on Application Performance in 4G LTE Networks

## Slide 24: References
[Baldo 11] Nicola Baldo, Marco Miozzo, Manuel Requena-Esteso, and Jaume Nin-Guerrero. An open source product-oriented lte network simulator based on ns-3. In Proceedings of the 14th ACM International Conference on Modeling, Analysis and Simulation of Wireless and Mobile Systems, MSWiM '11, pages 293{298, New York, NY, USA, 2011. ACM.
[Böhmer 11] Matthias Böhmer, Brent Hecht, Johannes Schöning, Antonio Krüger, and Gernot Bauer. Falling asleep with angry birds, facebook and kindle: a large scale study on mobile application usage. In Proceedings of the 13th International Conference on Human Computer Interaction with Mobile Devices and Services, pages 47-56. ACM, 2011.
[Cisco 13] Cisco. Cisco Visual Networking Index: Global Mobile Data Traffic Forecast Update, 2013-2018. Technical report, Cisco, 2014. http://www.cisco.com/en/US/solutions/collateral/ns341/ns525/ns537/ns705/ns827/white paper c11-520862.pdf
[Dahlman 11] Erik Dahlman, Stefan Parkvall, and Johan Sköld. 4G LTE/LTE-Advanced for Mobile Broadband. Academic Press, Oxford, 2011.
[E-Model] Leandro Carvalho, Edjair Mota, Regeane Aguiar, Ana F Lima, Jose Neuman de Souza, and Anderson Barreto. An E-model implementation for speech quality evaluation in VoIP systems. In Proceedings of the 10th IEEE Symposium on Computers and Communications, volume 154. IEEE Computer Society, 2005.
[Huang 13] Junxian Huang, Feng Qian, Yihua Guo, Yuanyuan Zhou, Qiang Xu, Z. Morley Mao, Subhabrata Sen, and Oliver Spatscheck. An In-depth Study of LTE: Eect of Network Protocol and Application Behavior on Performance. In Proceedings of the ACM SIG-COMM 2013 Conference on SIGCOMM, SIGCOMM '13, pages 363{374, New York, NY, USA, 2013. ACM.
[ITU G.711] International Telecommunication Union. Pulse Code Modulation (PCM) of Vlice Frequencies. Technical Specification G.711, ITU-T, November 1988. https://www.itu.int/rec/dologin pub.asp?lang=e&id=T-REC-G.711-198811-I!!PDFE& type=items.
[Kawser 12] T. Mohammad Kawser, Nax Imtiaz Bin Hamid, Nayeemul Hasan, M. Shah Alam, and M. Musqur Rahman. Limiting HARQ Retransmissions in Downlink for Poor Radio Link in LTE. International Journal of Information and Electronics Engineering, 2012.

## Slide 25: References Cont
[LTE RLC] 3GPP. 3rd Generation Partnership Project; Technical Specification Group Radio Access Network; Evolved Universal Terrestrial Radio Access (E-UTRA); Radio Link Control (RLC) protocol specification (Release 8). Technical Specification 36.322v8.0.0, 3GPP, December 2007. http://www.3gpp.org/ftp/Specs/html-info/36322.htm.
[LTE RRC] 3GPP. 3rd Generation Partnership Project; Technical Specification Group Radio Access Network; Evolved Universal Terrestrial Radio Access (E-UTRA); Radio Resource Control (RRC) Protocol specification (Release 8). Technical Specification 36.331v8.10.0, 3GPP, march 2008. http://www.3gpp.org/ftp/Specs/html-info/36331.htm.
[Makidis 07] Michael Makidis. Implementing and evaluating the RLC/AM protocol of the 3GPP specification. Master's thesis, Athens University of Economics and Business, 2007.
[ns-3] https://www.nsnam.org/
[ns-3 Forum] https://groups.google.com/forum/#!topic/ns-3-users/CEfmMX3IRBw
[ns-3 stats] https://www.nsnam.org/overview/statistics/
[Verizon] Verizon. IP Latency Statistics, April 2014. http://www.verizonenterprise.com/about/network/latency/.
[Zyren 07] Jim Zyren. Overveiw of the 3GPP Long Term Evolution Physical Layer. Technical report, Freescale Semiconductor, 07 2007.

## Slide 26: Backup Slides

## Slide 27: CQI Choice
Wrote Android application to log requested CQI value on LTE networks
Collected data over 1 week from Feb – March 2014
Collected in multiple locations

## Slide 28: CQI Choice Cont.
Cumulative distribution of data
Collected 5,070 data points
Average CQI requested was 8

## Slide 29: Wireless Loss Cont
Creating fading loss file
  Use goal % loss and set of input gap lengths to find state transition probabilities
  Run Gilbert model

## Slide 30: Simulating VoIP
ns-3 example code for application that sends data at a specified rate
Use G.711 encoding format to define size of packets and sending rate
  160 bytes data, 12 bytes RTP header, 8 bytes UDP header, 20 bytes IP header
  Sending rate 64Kbps or about 1 packet every 20ms
Mean Opinion Score (MOS) used as performance metric
  1 – 5 point scale, 1 worst, 5 best
  Calculated from delay and loss using E-Model
[ITU G.711]
[E-Model]

## Slide 31: Simulating FTP
ns-3 bulk send application
  Transmits as much data as possible over TCP
  Default ns-3 congestion control algorithm is NewReno
Throughput used as performance metric

## Slide 32: RLC UM
Receiving window used for reordering PDUs
Out of order PDU trigger timer t-Reordering
0
1
2
3
4
5
6
VR(UR),VR(UH)
0
1
2
3
4
5
6
VR(UR)
VR(UX),VR(UH)

## Slide 33: Timer t-Reordering UM
Timer runs when PDUs arrive out of order
Gives MAC layer chance to recover lost data
Expiration moves VR(UR) up to first SN >= VR(UX) that is not received
Tradeoffs
  Small timer, MAC retransmissions lost
  Large timer, keeps lower bound of window stalled
0
1
2
3
4
5
6
VR(UR)
VR(UX),VR(UH)
0
1
2
3
4
5
6
VR(UR),VR(UH)
LOST
0
1
2
3
4
5
6
VR(UR),VR(UH)
Recovered

## Slide 34: RLC AM
Receiving window used for reordering and ACK/NACK messaging
0
1
2
3
4
5
6
VR(R),VR(H),VR(MS)
0
1
2
3
4
5
6
VR(R),VR(MS)
VR(X),VR(H)

## Slide 35: Timer t-Reordering AM
Gives MAC layer time before NACKing
t-Reordering starts when SN 5 arrives
  ACK = 3
While running SN 4 arrives
  ACK = 3
When timer expires VR(MS) is updated
  ACK = 6, NACK = 3
Tradeoffs
  Small timer, NACK data that MAC can recover
  Large timer, stalls NACKs
0
1
2
3
4
5
6
VR(R),VR(MS)
VR(X),VR(H)
0
1
2
3
4
5
6
VR(H),VR(MS)
0
1
2
3
4
5
6
VR(X),VR(H)
VR(R),VR(MS)
VR(R)

## Slide 36: Gilbert-Elliot Model
Two state machine for loss
  X = 0 no loss
  X = 1 loss
Transition probabilities define when to change states

## Slide 37: Transitions
Gordo et al. shows how to take input of loss gaps and determine state transitions
  Ok – # of burst losses of length k
  a - # of TTIs
  d - # of lost TTIs
[Gordo 10]

## Slide 38: LTE Network Layers
LTE wireless network has 6 layers (not all shown)
PHY – RLC layers carry user and network control data
LTE transmits collections of Physical Resource Blocks (PRB)s in Transport Blocks (TB)
  A TB is the packet sent through the PHY layer
  One TB can have multiple PRBs
  Each PRB takes up some radio spectrum and time frame
Application
TCP
UDP
IP
RLC
MAC
PHY