## Slide 1: Measurements Comparing TCP Cubic and TCP BBR over a Satellite Network
Jae Chung
Saahil Claypool, Mark Claypool
Notes: Saahil Claypool, Jae Chung, and Mark Claypool. Measurements Comparing TCP Cubic and TCP BBR over a Satellite Network, In Proceedings of the IEEE Consumer Communications & Networking Conference (CCNC), Virtual Conference, January 9-12, 2021.
Online at: http://www.cs.wpi.edu/~claypool/papers/bbr-cubic-sat/

## Slide 2: Introduction (1 of 2)
Satellites provide global networking
  “Always on” connectivity for remote locations, during disasters [SIA20]
  Bitrates increasing (20x recently)
Challenge is latency  about 300 ms min. one-way for geosynchronous
300 ms

## Slide 3: Introduction (2 of 2)
Latency impacts TCP bitrates
  One window of packets each RTT
  Window size depends upon congestion control algorithm
  TCP Cubic – most Internet bytes, servers
  TCP BBR – newcomer, Google servers
Few published studies of TCP over satellite network
  Mostly simulation or emulation
This paper  TCP Cubic & TCP BBR over satellite network

## Slide 4: Outline
Introduction (done)
Background (next)
Methodology
Results
Conclusions

## Slide 5: TCP Inflight Data
BDP
BDP + Queue
RTT
x
x
x
Delivery Rate
x
x
x
Inflight
BBR
Cubic
Cubic
BBR

## Slide 6: TCP over Time
inflight
BBR
[CCGY17]
inflight
Time
Cubic
Slow Start
Congestion
Avoidance
Start-up
Probe BW
Probe RTT
[HRX08]

## Slide 7: Outline
Introduction (done)
Background (done)
Methodology (next)
Results
Conclusions

## Slide 8: Methodology
Baseline
  UDP Ping
Bulk-download
  iperf
[RFC 5166]
  Throughput
  Round-trip time
  Retransmissions (loss)
144 Mb/s
Servers
Client
Notes: Client Intel i7-1065G7 CPU @ 1.30GHz and 32 GB RAM
Servers Intel Ken E312xx CPUs @ 2.5 GHz and 32 GB RAM
Servers and client run Ubuntu 18.04.4 LTS, Linux kernel v4.15.0
Servers connect to WPI LAN via Gb/s Ethernet.
WPI campus connected to Internet via several 10 Gb/s, throttled to 1 Gb/s.
Viasat terminal to Ka-band outdoor antenna (RF amplifier, up/down converter, reflector and feed) through Viasat 2 satellite to Ka-band gateways links
Service plan peak data rate of 144 Mb/s
Gateway does per-client queue management for traffic
  Queue up to 36 MBytes (about 2 seconds)
  Active Queue Management (AQM) randomly drops 25% when queue over 18 MBytes

## Slide 9: Outline
Introduction (done)
Background (done)
Methodology (done)
Results (next)
  Baseline
  Steady State
  Start-up
Conclusions

## Slide 10: Baseline
Loss: 0.05%
  77% are single packet
  Largest 11 packets (2.2 seconds)

## Slide 11: Steady State – Throughput
BBR
BBR
Cubic
Cubic

## Slide 12: Steady State – Throughput
Independent, 2-tailed t test (α = 0.5)  statistically significant
  t(158) = 4.4
  p < .0001
Large effect size (d = 0.7)
Cubic
BBR

## Slide 13: Start-up

## Slide 14: Start-up
Independent, 2-tailed t test (α = 0.5) for mean start-up throughput  statistically significant
  t(158) = 31.9
  p < .0001
Very large effect size (d = 5)
Cubic
BBR

## Slide 15: Conclusion
Baseline consistent RTT 600ms, low loss
Steady-state: BBR a bit lower throughput than Cubic
  From BBR “probe RTT” state
Start-up: BBR 50% faster than Cubic

## Slide 16: Future Work
Multiple Flows
  e.g., BBR and Cubic together
Other Protocols
  e.g., PCC, Hybla, QUIC
Performance Enhancing Proxy (PEP)
Other applications
  e.g., Web browsing, streaming video

## Slide 17: Measurements Comparing TCP Cubic and TCP BBR over a Satellite Network
Jae Chung
Saahil Claypool, Mark Claypool
Thank-you!
Notes: Saahil Claypool, Jae Chung, and Mark Claypool. Measurements Comparing TCP Cubic and TCP BBR over a Satellite Network, In Proceedings of the IEEE Consumer Communications & Networking Conference (CCNC), Virtual Conference, January 9-12, 2021.
Online at: http://www.cs.wpi.edu/~claypool/papers/bbr-cubic-sat/

## Slide 18: References
[BCDA99] C. Barakat, N. Chaher, W. Dabbous, and E. Altman, “Improving TCP/IP over Geostationary Satellite Links,” in Proceedings of GLOBECOM, Rio de Janeireo, Brazil, Dec. 1999.
[CCGY17] N. Cardwell and Y. Cheng and C. S. Gunn and S. H. Yeganeh and Van Jacobson, “BBR: Congestion-based Congestion Control,” Communications of the ACM, no. 2, pp. 58–66, Jan. 2017.
[HRX08] S. Ha, I. Rhee, and L. Xu, “CUBIC: A New TCP-Friendly High-Speed TCP Variant,” ACM SIGOPS OS Review, vol. 42, no. 5, 2008.
[OTI11] H. Obata, K. Tamehiro, and K. Ishida, “Experimental Evaluation of TCP-STAR for Satellite Internet over WINDS,” in Proceedings of Autonomous Decentralized Systems, Tokyo, Japan, Mar. 2011.
[RFC 5166] S. Floyd, “Metrics for the Evaluation of Congestion Control Mechanisms,” Internet Requests for Comments RFC 5166, March 2008.
[SIA20] S. I. Association, “Introduction to the Satellite Industry,” Online presentation: https://tinyurl.com/y5m7z77e, 2020.
[WZL+18] Y. Wang, K. Zhao, W. Li, J. Fraire, Z. Sun, and Y. Fang, “Performance Evaluation of QUIC with BBR in Satellite Internet,” in Proceedings of IEEE Wireless for Space and Extreme Environments (WiSEE), Huntsville, AL, USA, Dec. 2018.

## Slide 19: Extra Slides

## Slide 20: Steady State – RTT
Cubic
BBR

## Slide 21: Steady State – Loss