## Slide 1: Who is the King of the Hill? Traffic Analysis over a 4G Network
Feng Li, Xiaoxiao Jiang, Jae Chung, and Mark Claypool
Verizon Labs and Worcester Polytechnic Institute (WPI)

## Slide 2: Introduction
-- Low latency and high link capacity of LTE
-- Significant growth in number and variety of mobile applications
-- Performance-enhancing proxies (PEPs) are introduced by many carriers
-- TLS/SSL make it hard to identify content type and choose traffic shaping strategies
-- To provide enhanced QoS services, carriers need better understanding of breakdown of application traffic

## Slide 3: Outline
-- Introduction
-- Methodology
-- Network Protocol Breakdown
-- Flow Statistics Analysis
-- Mobile Applications
-- Conclusions

## Slide 4: Methodology
-- Tier-1 wireless carrier in south-central U.S.
-- Mirror traffic from UE pool with over 5000 users
-- 2 consecutive days, November 7-8, 2016
-- 7 hours, 9am-4pm
-- Total 85 GB data, 2.5 million flows
Note: no subscribers’ IDs, geographic locations, device types nor mobile numbers

## Slide 5: Network Protocol Breakdown
-- 64% flows IPv4 compared to 36% IPv6
-- IPv6 volume slightly larger than IPv4
-- Mean IPv6 TCP flows is 81 KB, while Mean TCP IPv4 is 11 KB
-- HTTP-family still dominates mobile: 70% of traffic volume
-- Only 30% traffic unencrypted HTTP

## Slide 6: Flow Statistics
-- Characteristics important for LTE network: duration, volume, rate (throughput), RTT
-- Most flows less than 2s
-- 11% TCP flows and 0.5% UDP flows longer than 1 minute
-- Most flows small
-- High volume UDP flows contributed by QUIC

## Slide 7: Flow Statistics
-- Applications with req/resp may never send enough data to fill pipe
-- Focus on elephant flow instead of numerous small flows
-- Median TCP initial RTT is 79ms
-- Large TCP initial RTTs may be from retransmission of SYN/SYN-ACK or backward compatible 2G/3G devices
-- Time efficiency of DNS caching is confirmed
Notes: -- 90% of TCP flows have rates less than 285 Kbps down and 60 Kbps up, while 90% of UDP flows have rates less than 815 Kbps down and 379 Kbps up
TCP, 3-way handshank
UDP from DNS request-response pairs

## Slide 8: Mobile Applications
-- Analyze applications through SNI, Hostname, reverse DNS
-- Able to classify 88% of the traffic (by volume)
-- Focus on well-know content providers
-- Goal: recognize video flows

## Slide 9: Top Content Providers
-- Top 5 Content Providers
-- Google include YouTube is largest content provider
-- QUIC constitute 25% of YouTube’s overall traffic
-- Instagram constitutes about half of all FaceBook traffic
-- Apple traffic consist of variety of different services
Notes: Most of goolge’s traffic is protected by TSL/SSL, and mainly over IPv6
Instagram is mainly over HTTP, similar to Google, FB has migrate much of its traffic to IPv6
Most of Apple traffic is over IPv4

## Slide 10: Top Mobile Applications
-- Top 10 mobile apps/servers
-- These top 10 applications account for 46% of total traffic
-- Video and Social apps most popular
-- Snapchat only application using QUIC besides Google

## Slide 11: YouTube Traffic
-- 22% of total observed traffic
-- HTTPS and QUIC, hard to infer application types even with DPI
-- Classify HTTPS based YouTube flow through SNI
-- Classify QUIC based YouTube flow through reverse DNS
-- QUIC YouTube and QUIC misc

## Slide 12: YouTube Flows Analysis
-- Flow duration not good differentiator for video flows
-- Ytimg flow even longer duration
-- Googlevideo.com and QUIC (YouTube) larger than others
-- Duration and volume come too late for detecting video

## Slide 13: YouTube Flows Analysis
-- Throughput of googlevideo.com and QUIC (YouTube) highest
-- Throughput may be good for identifying video
-- 60% googlevideo.com and 25% QUIC (youtube) have payload of 1000+ bytes
-- Packet length may good for identifying video

## Slide 14: Conclusions
Approach:
-- Detailed snapshot of current commercial mobile network
-- Cross-layer traffic analysis from tier-1 wireless network
Findings:
-- High volumes of IPv6 and HTTPs suggest renewed focus on traffic classification
-- QUIC comprises 60% of UDP traffic and warrants special attention
-- Google, Facebook and Apple top 3 content providers
-- YouTube alone accounts for over 20% of total traffic

## Slide 15: Thanks! Questions?