## Slide 1: Comparison of TCP Congestion Control over a Satellite Network
Jae Chung
Saahil Claypool, Mark Claypool
Notes: Saahil Claypool, Jae Chung, and Mark Claypool. Measurements Comparing TCP Cubic and TCP BBR over a Satellite Network, In Proceedings of the IEEE Consumer Communications & Networking Conference (CCNC), Virtual Conference, January 9-12, 2021.
Online at: http://www.cs.wpi.edu/~claypool/papers/bbr-cubic-sat/

## Slide 2: Introduction (1 of 2)
Satellites provide global networking
  “Always on” connectivity for remote locations, during disasters
  Bitrates increasing (20x recently)
Challenge is latency  about 300 ms min. one-way for geosynchronous
300 ms

## Slide 3: Introduction (2 of 2)
Latency impacts TCP bitrates
  One window of packets each RTT
  Window size depends upon congestion control algorithm
  TCP Cubic – loss-based
  TCP BBR – BDP-based
  TCP PCC – utility function-based
  TCP Hybla – satellite optimized
Few published studies of TCP over satellite network
  Mostly simulation or emulation
This paper  TCP over satellite netwrk

## Slide 4: Outline
Introduction (done)
Methodology (next)
Results
Conclusions

## Slide 5: Methodology
Baseline
  UDP Ping
Bulk-download
  iperf
[RFC 5166]
  Throughput
  Round-trip time
  Retransmissions (loss)
144 Mb/s
Servers
Client
Notes: Client Intel i7-1065G7 CPU @ 1.30GHz and 32 GB RAM
Servers Intel Ken E312xx CPUs @ 2.5 GHz and 32 GB RAM
Servers and client run Ubuntu 18.04.4 LTS, Linux kernel v4.15.0
Servers connect to WPI LAN via Gb/s Ethernet.
WPI campus connected to Internet via several 10 Gb/s, throttled to 1 Gb/s.
Viasat terminal to Ka-band outdoor antenna (RF amplifier, up/down converter, reflector and feed) through Viasat 2 satellite to Ka-band gateways links
Service plan peak data rate of 144 Mb/s
Gateway does per-client queue management for traffic
  Queue up to 36 MBytes (about 2 seconds)
  Active Queue Management (AQM) randomly drops 25% when queue over 18 MBytes

## Slide 6: Outline
Introduction (done)
Methodology (done)
Results (next)
  Baseline
  Steady State
  Start-up
Conclusions

## Slide 7: Baseline
Loss: 0.05%
  77% are single packet
  Largest 11 packets (2.2 seconds)

## Slide 8: Steady State – Throughput
BBR
Cubic
Hybla
PCC
median

## Slide 9: Steady State – Throughput
BBR
Hybla
PCC
Large
BBR
Cubic
Hybla
PCC
780
821
958
685
RTT (ms)
Tput (Mb/s)

## Slide 10: Start-up

## Slide 11: Start-up
BBR
Hybla
PCC
Very Large
BBR
Cubic
Hybla
PCC
917
757
799
806
RTT
(ms)
Tput
(ms)

## Slide 12: Power
BBR
Cubic
Hybla
PCC

## Slide 13: Conclusion
Baseline consistent RTT 600ms, low loss
Steady state:
  Medians similar
  Mean – BBR, PCC lowest
Start-up:
  Hybla fastest
  BBR, PCC next
  Cubic slowest
Power:
  PCC – steady state
  Hybla – start-up

## Slide 14: Future Work
Multiple Flows
  e.g., BBR and Cubic together
TCP settings and Protocols
  e.g., RTT0, QUIC
Performance Enhancing Proxy (PEP)
Other applications
  e.g., Web browsing, streaming video

## Slide 15: Comparison of TCP Congestion Control over a Satellite Network
Jae Chung
Saahil Claypool, Mark Claypool
Notes: Saahil Claypool, Jae Chung, and Mark Claypool. Measurements Comparing TCP Cubic and TCP BBR over a Satellite Network, In Proceedings of the IEEE Consumer Communications & Networking Conference (CCNC), Virtual Conference, January 9-12, 2021.
Online at: http://www.cs.wpi.edu/~claypool/papers/bbr-cubic-sat/