## Slide 1: Project 1 Speech Detection
Due: Sunday, February 1st, 11:59pm

## Slide 2: Outline
Motivation
Problem Statement
Details
Hints
Grading
Turn in

## Slide 3: Motivation
Speech recognition detects word boundaries in raw audio data
“Silence
Is
Golden”

## Slide 4: Motivation
Recognizing silence can reduce:
  Network bandwidth
  Processing load
Easy in sound proof room, with digitized tape
  Measure energy level in digitized voice
What about elsewhere?

## Slide 5: Speech in the Presence of Noise
Speech corrupted by additive background noise at decreasing SNRs.
Clean SNR = 5 dB SNR = -5 dB
[RGS07]
Notes: J. Ramírez, J. M. Górriz, J. C. Segura, “Voice Activity Detection. Fundamentals and Speech Recognition System Robustness”. Robust Speech Recognition and Understanding. pp. 1-22, Ed.: M. Grimm and K. Kroschel, I-TECH Education and Publishing, 2007. ISBN: 978-3-902613-08-0

## Slide 6: Speech in the Presence of Noise
Energy (dB)
[RGS07]
Notes: J. Ramírez, J. M. Górriz, J. C. Segura, “Voice Activity Detection. Fundamentals and Speech Recognition System Robustness”. Robust Speech Recognition and Understanding. pp. 1-22, Ed.: M. Grimm and K. Kroschel, I-TECH Education and Publishing, 2007. ISBN: 978-3-902613-08-0

## Slide 7: Research Problem
Noisy rooms with background noise make some edges difficult
“Five”

## Slide 8: Research Problem
Computer audio often for interactive applications
  Voice commands
  Teleconferencing (Voice over IP or VoIP)
Needs to be done in ‘real-time’

## Slide 9: Project
Implementation in Linux or Windows (or Cygwin)
Implement end-point algorithm by Rabiner and Sambur [RS75]
  (Paper for class, next)
Embed in “record” utility – data from microphone
Build “play” utility for testing – data to speakers
Basis for VoIP
  (Project 2)

## Slide 10: Details - Record
Voice-quality:
  8000 samples/second
  8 bits per sample
  One channel
Record sound, write files:
  sound.data: audio data (from 0 and 255)  can graph
  sound.raw: raw audio data with all sound  can play
  speech.raw: raw audio data without silence  can play
  energy.data: energy, one row per frame  can graph
  zero.data: zero crossings, one row per frame  can graph
Other features allowed

## Slide 11: Details - Play
Plays sound file
Repeat until file empty
E.g.,
  play sound.raw
  play speech.raw
Other features allowed

## Slide 12: Sound in Windows
Microsoft Visual C++
  See Web page for hints
Use sound device  WAVEFORMATEX struct:
  wFormatTag: set to WAVE_FORMAT_PCM
  nChannels, nSamplesPerSec, wBitsPerSample: set to voice quality audio settings
  nBlockAlign: set to number of channels times number of bytes per sample
  nAvgBytesPerSec: set to number of samples per second times the nBlockAlign value
  cbSize: set this to zero

## Slide 13: Sound in Windows
waveInOpen()
  a device handle (HWAVEIN)
  device number (may be 1, depends upon PC)
  WAVEFORMATEX variable
  a callback function
    gets invoked when sound device has a sample of audio

## Slide 14: Sound in Windows
Sound device needs buffers to fill
Type LPWAVEHDR
  lpData: for raw data samples
  dwBufferLength: set to nBlockAlign times length (in bytes) of sound chunk you want
waveInAddBuffer() to give buffer to sound device
  Give it device
  Buffer (LPWAVEHDR)
  Size of variable
When callback invoked, buffer (lpData) has raw data to analyze
  Must give it another via waveInAddBuffer() again

## Slide 15: Sound in Windows
Useful header files:
    #include <windows.h>
    #include <stdio.h>
    #include <stdlib.h>
    #include <mmsystem.h>
    #include <winbase.h>
    #include <memory.h>
    #include <string.h>
    #include <signal.h>
    extern "C"
Useful data types:
HWAVEOUT
  writing audio device
HWAVEIN
  reading audio device
WAVEFORMATEX
  sound format structure
LPWAVEHDR
  buffer
MMRESULT
  Return type from wave system calls
Online documentation from Visual C++ for more information (Visual Studio  Samples)

## Slide 16: Sound in Linux
Two primary methods: Open Sound System (OSS) or Advanced Linux Sound Architecture (ALSA)
ALSA part of kernel, v2.4+
  Phonon, Xine, Gstreamer, PulseAudio, Jack, even OSS all interface with it
OSS “legacy” but broader than Linux
How it works: Linux audio explained

## Slide 17: Linux – OSS
Can do in Windows!  Cygwin
  Unix-like environment and command-line interface for Microsoft Windows (http://www.cygwin.com/)
Audio device just like file (POSIX):
  /dev/dsp
  open("/dev/dsp", O_RDWR)
Recording and Playing by:
  read() to record
  write() to play

## Slide 18: OSS – Sound Parameters
Use ioctl() to change sound card parameters
E.g., to change sample size to 8 bits:
  fd = open("/dev/dsp", O_RDWR);
  arg = 8;
  ioctl(fd, SOUND_PCM_WRITE_BITS, &arg);
Remember to error check all system calls!

## Slide 19: OSS – Sound Parameters
The parameters of interest are:
  SOUND_PCM_WRITE_BITS
    number of bits per sample
  SOUND_PCM_WRITE_CHANNELS
    mono or stereo
  SOUND_PCM_WRITE_RATE
    sample/playback rate

## Slide 20: OSS Compatibility Mode
Has not been in the Linux kernel since v2.4
But there is OSS compatibility mode
Try: aoss name_of_program_using_oss
  E.g., aoss record
Or have snd_pcm_oss kernel module loaded

## Slide 21: Linux – ALSA
Samples at given time for all channels is called a frame
If stream is non-interleaved, each channel is stored in separate buffer
If stream is interleaved, the samples are mixed together in single buffer
A period contains multiple samples (frames)
Only needed audio include is:
#include <alsa/asoundlib.h>
When compiling, -lasound needed to link in libasound library

## Slide 22: ALSA – Open Device
Open with snd_pcm_open()
snd_pcm_t *handle;
/* open playback device (e.g. speakers default) */
snd_pcm_open(&handle, "default", SND_PCM_STREAM_PLAYBACK, 0);
/* open record device (e.g. microphone default) */
snd_pcm_open(&handle, "default", SND_PCM_STREAM_CAPTURE, 0);
When done, close with snd_pcm_close()

## Slide 23: ALSA – Write/Read
Done by snd_pcm_writei() and snd_pcm_read(), respectively:
/* write to audio device */
snd_pcm_writei(handle, buffer, frames);
/* read from audio device */
snd_pcm_readi(handle, buffer, frames);
[Tra04] J. Tranter. Introduction to Sound Programming with ALSA, Linux Journal, Issue #126, October, 2004.

## Slide 24: Program Template (Linux)
open sound device
set sound device parameters
record silence
set algorithm parameters
while (1)
  record sound
  compute algorithm stuff
  detect speech
  write data to file
  write sound to file
  if speech, write speech to file

## Slide 25: Questions
When done, brief answers (in answers.txt)
What might happen to the speech detection algorithm in a situation where the background noise changes a lot over the audio session?
What are some cases where you might want the silence to remain in a recorded audio stream?
Accurate detecting the beginning of speech might be easier with a large sample size (i.e., capturing more of the audio before computing energy and zero crossings). Why might this be a bad idea for some audio applications?
Do you think the algorithm is language (e.g., English versus Spanish) specific? Why or why not?

## Slide 26: Hand In
Online turnin (see Web page)
Turn in:
  Code
  Makefile/Project file
  Answers
Zip/Tar up in one file
Via email

## Slide 27: Grading
25% basic recording of sound
25% basic playback of sound
20% speech detection
10% adjustment of thresholds
10% proper file output (sound, speech, data)
10% answers to questions
Rubric on Webpage