## Slide 1: CARA: Collision-Aware Rate Adaptation for IEEE 802.11 WLANs
Presented by
Eric Wang

## Slide 2: Outline
Introduction
Related Work
Preliminaries
CARA
Performance Evaluation
Conclusion and Future Work

## Slide 3: Basic CSMA/CA

## Slide 4: Introduction
802.11 no rate adaption scheme
Most open-loop adaption schemes don’t consider collision
  Malfunction when collisions happen
CARA
  Combines RTS/CTS exchange with CCA
  Collision vs. channel errors
  No change to current 802.11 standard

## Slide 5: Outline
Introduction
Related Work
Preliminaries
CARA
Performance Evaluation
Conclusion and Future Work

## Slide 6: Related Work
Rate adaption scheme classifications:
  Closed-loop
    Receiver feedback of desired rate by RTS/CTS
    Transmitter adapts rate accordingly
    Costly! Waste of bandwidth.
  Open-loop
    Further classified into two categories

## Slide 7: Open-loop rate adaption
Subcategory 1
  Decides transmission rate by local channel est.
    eg. ACK frame receptions
    Usually good performance as closed-loop
    Extra implementation efforts.
Subcategory 2
  Make use of local ACK information.
    Simple implementation

## Slide 8: Rate adaption Scheme issues
When to increase
  Transmitter adaptively changes rate over time
When to decrease
  Open-loop scheme malfunctions during collision
  No differentiate between collision and channel errors
  Thus, decrease over-aggressively.

## Slide 9: Preliminaries
CSMA/CA
  DCF, PCF
  CCA
RTS/CTS exchange
  Useful in highly-contending WLAN
ARF
  Timing function and missing ACK frame
CARA

## Slide 10: Outline
Introduction
Related Work
Preliminaries
CARA
Performance Evaluation
Conclusion and Future Work

## Slide 11: CARA
Adopts two methods to differentiate collisions from channel errors:
  RTS probing (mandatory)
  CCA detection (optional)

## Slide 12: Identifying collision via RTS probing
RTS probing is mandatory
  Assume transmission error negligible
    Small size, robust transmission rate
    Failure of RTS transmission indicates collision
  After RTS/CTS exchange
    Data transmission error caused by channel errors
    No misinterpretation
    Overhead of adding RTS/CTS is large
  RTS probing: enables RTS/CTS exchange only when transmission failure of data frames happens

## Slide 13: State Transition Diagram

## Slide 14: State Transition Diagram

## Slide 15: RTS probing mechanism
Data frame transmitted without RTS/CTS
If transmission failed, activate RTS/CTS exchange for next transmission. If retransmission failed, lower transmission rate
If transmission successful, stays at same rate and send next data frame without RTS/CTS

## Slide 16: ARF vs. RTS probing

## Slide 17: Identifying Collision via CCA Detection

## Slide 18: CCA detection
Case 1 & 3: CCA not helping
  Because CCA cannot be sure whether collision happened
  RTS Probing is launched later.
Case 2: CCA helping
  no need to activate RTS/CTS exchange.
  Collision detected!
  Retransmit the data.

## Slide 19: Outline
Introduction
Related Work
Preliminaries
CARA
Performance Evaluation
Conclusion and Future Work

## Slide 20: ns-2 simulation details
20dBm transmit power
Static stations; 1500 octet MAC payload
BER vs SNR curves measured in AWGN (Additive White Gaussian Noise) environment without fading.
Set background noise to -96dBm
Simulate indoor settings
Use Ricean fading model for multi-path fading time-varying wireless conditions.

## Slide 21: Results for One-to-One topology
One station continuously
transmitting to another.
X :Physical distance (meters)
Y :Throughput (Mbps)

## Slide 22: Results for Star Topology with varing number of contending stations
Various number of
contending stations
are evenly placed on
a circle around AP
within 10 meters.
Two reasons for ARF
ill behavior:
Collision vs. channel errors
Performance anomaly

## Slide 23: Results for Line Topology with random data frame sizes and random station positions
Performance gap
becomes larger:
CCA becomes more
helpful.

## Slide 24: Results for random topologies with time-varying wireless channel
50 different scenarios
When 10 stations
contend
Random locations
Random data size
CARA 1 > CARA 2 ?
CCA succeeds but
failed to transmit
data, delaying
adaptation.

## Slide 25: Averaged result with various contending stations

## Slide 26: Results for random topologies with time-varying wireless channel

## Slide 27: Transmission rate adaptation over time

## Slide 28: Summary
RTS probing is very efficient in differentiating collisions from channel errors.
  Why CARA outperforms ARF
CARA-2 with CCA detection outperforms CARA-1 when data transmission durations are different among contending stations.
Collision aware rate adaptation scheme are needed due to bad performance of ARF.

## Slide 29: Outline
Introduction
Related Work
Preliminaries
CARA
Performance Evaluation
Conclusion and Future Work

## Slide 30: Conclusion
CARA is more likely to make correct rate adaptation decisions than ARF.
CARA requires no change to the 802.11 standard (unlike RBAR).
CARA significantly outperforms ARF in all simulated multiple contending environments.

## Slide 31: Future work
Look at changes to the increase rate algorithm [CARA-RI].
Study optimization of operational CARA parameters.
Address possibility of hidden terminal detection [CARA-HD].
Built a working CARA prototype using MadWIFI driver.