## Slide 1: TCP Sliding Windows, Flow Control, and Congestion Control
Lecture material taken from
“Computer Networks A Systems Approach”, Fourth Ed.,Peterson and Davie,
Morgan Kaufmann, 2007.

## Slide 2: Sliding Windows Outline
Generic Sliding Windows
Receiver Response Choices
Introduction to TCP Sliding Windows
  Flow control and buffers
  Advertised window
  Congestion control

## Slide 3: Sliding Windows
Normally a data link layer concept.
Our interest is understanding the TCP mechanism at the transport layer.
Each frame is assigned a sequence number: SeqNum.
The sender maintains three variables: send window size (SWS), last ACK received (LAR), and last Frame sent (LFS).

## Slide 4: Sender Variables
SWS :: the upper bound on the number of outstanding frames (not ACKed) the sender can transmit.
LAR :: the sequence number of the last ACK received.
LFS :: the sequence number of the last frame sent.

## Slide 5: Sender Invariant
LFS – LAR ≤ SWS
LAR
LFS
≤ SWS

## Slide 6: Sender Window
An arriving ACK  LAR moves right 1
 sender can send one more frame.
Associate a timer with each frame the sender transmits.
Sender retransmits the frame if the timer times out.
Sender buffer :: up to SWS frames.

## Slide 7: Receiver Variables
Receiver window size (RWS) :: the upper bound on the number of out-of-order frames the receiver is willing to accept.
Largest acceptable frame (LAF) :: the sequence number of the largest acceptable frame.
Last frame received (LFR) :: the sequence number of the last frame received.

## Slide 8: Receiver Invariant
LAF – LFR ≤ RWS
LFR
LAF
≤ RWS

## Slide 9: Receiver Window
When a frame arrives with SeqNum:
  If (SeqNum ≤ LFR or SeqNum > LAF)
  the frame is discarded because it is outside the window.
  If (LFR < SeqNum ≤ LAF)
  the frame is accepted.

## Slide 10: Receiver ACK Decisions
SeqNumToAck :: largest sequence number not yet ACKed such that all frames ≤ SeqNumToAck have been received.
Receiver ACKs receipt of SeqNumToAck
  and sets
  LFR = SeqNumToAck
  LAF = LFR + RWS
  SeqNumToAck is adjusted appropriately!

## Slide 11
ACK sequence number indicates the last frame successfully received.
- OR -
2. ACK sequence number indicates the next frame the receiver expects to receive.
Both of these can be strictly individual ACKs or represent cumulative ACKing.
Cumulative ACKs is the most common technique.
Generic ACK Choices

## Slide 12
Use a duplicate ACK.
2. Use a selective ACK [SACK].
3. Use a negative ACK [NACK] .
Generic Responses to a Lost Packet or Frame

## Slide 13: TCP Sliding Windows
In practice, the TCP implementation switches from packet pointers to byte pointers.
Guarantees reliable delivery of data.
Ensures data delivered in order.
Enforces flow control between sender and receiver.
The idea is: the sender does not overrun the receiver’s buffer.

## Slide 14
Application process
Write
bytes
TCP
Send buffer
Segment
Segment
Segment
Transmit segments
Application process
Read
bytes
TCP
Receive buffer
■ ■ ■
Figure 5.3 TCP Managing a Byte Stream
P&D slide

## Slide 15: Figure 5.8 Relationship between TCP Send Buffer and TCP Receive Buffer
P&D slide

## Slide 16: Receiver’s Advertised Window
The big difference in TCP is that the size of the sliding window size at the TCP receiver is not fixed.
The receiver advertises an adjustable window size (AdvertisedWindow field in TCP header).
Sender is limited to having no more than AdvertisedWindow bytes of unACKed data at any time.

## Slide 17: Figure 5.4 TCP Header Format
P&D slide

## Slide 18: Figure 5.5 Simplified TCP
P&D slide

## Slide 19: TCP Flow Control
The discussion is similar to the previous sliding window mechanism except we add the complexity of sending and receiving application processes that are filling and emptying their local buffers.
Also we introduce the complexity that buffers are of finite size without worrying about where the buffers are stored.
        MaxSendBuffer
        MaxRcvBuffer

## Slide 20: TCP Flow Control
The receiver throttles the sender by advertising a window size no larger than the amount it can buffer.
On TCP receiver side:
LastByteRcvd - LastByteRead ≤ MaxRcvBuffer
to avoid buffer overflow!

## Slide 21: TCP Flow Control
TCP receiver advertises:
AdvertisedWindow = MaxRcvBuffer -
(LastByteRcvd - LastByteRead)
i.e., the amount of free space available in the receiver’s buffer.

## Slide 22
The TCP sender must adhere to the AdvertisedWindow from the receiver such that
LastByteSent – LastByteAcked ≤ AdvertisedWindow
or use EffectiveWindow
EffectiveWindow = AdvertisedWindow – (LastByteSent – LastByteAcked)
TCP Flow Control

## Slide 23
Sender Flow Control Rules:
EffectiveWindow > 0 for sender to send more data.
LastByteWritten – LastByteAcked ≤ MaxSendBuffer
equality here  send buffer is full!!
 TCP sender process must block the sender application.
TCP Flow Control

## Slide 24: TCP Congestion Control
CongestionWindow :: a variable held by the TCP source for each connection.
TCP is modified such that the maximum number of bytes of unacknowledged data allowed is the minimum of CongestionWindow and AdvertisedWindow.
MaxWindow :: min (CongestionWindow , AdvertisedWindow)

## Slide 25: TCP Congestion Control
Finally, we have that
EffectiveWindow = MaxWindow – (LastByteSent – LastByteAcked)
The idea :: the source’s effective window can be no faster than the slowest of the network (i.e., its core routers) or the destination Host.
The TCP source receives implicit and/or explicit indications of congestion by which to reduce the size of CongestionWindow.

## Slide 26: Sliding Windows Summary
Generic Sliding Windows
Receiver Response Choices
Introduction to TCP Sliding Windows
  Flow control and buffers
  Advertised window
  Congestion control