## Slide 1: Tuning RED for Web Traffic
Mikkel Christiansen, Kevin Jeffay,
David Ott, Donelson Smith
UNC, Chapel Hill
SIGCOMM 2000, Stockholm
subsequently
IEEE/ACM Transactions on Networking
Vol. 9 , No. 3 (June 2001) pp 249 – 264.
presented by Bob Kinicki

## Slide 2: Tuning RED Outline
Introduction
Background and Related Work
Experimental Methodology
  Web-like Traffic Generation
Experiment Calibrations and Procedures
FIFO and RED Results
Conclusions

## Slide 3: Introduction
RFC2309 recommends Active Queue Management [AQM] for Internet congestion avoidance.
RED, the best known AQM technique, has not been studied much for Web traffic, the dominant subset of TCP connections on the Internet in 2000.
The authors use response time, a user-centric performance metric, to study short-lived TCP connections that model HTTP 1.0.

## Slide 4: Introduction
They model HTTP request-response pairs in a lab environment that simulates a large collection of browsing users.
Artificial delays are added to a small lab testbed to approximate coast-to-coast US round trip times (RTT’s).
The paper focuses on studying RED tuning parameters.
The basis of comparison is the effect of RED vs. Drop Tail FIFO on response time for HTTP 1.0.

## Slide 5: Background and Related Work
The authors review RED parameters ( avg, qlen, minth, maxth, wq , maxp) and point to Sally Floyd’s modified guidelines.
RED is effective in preventing congestion collapse when TCP windows are configured to exceed network storage capacity.
Claim by Villamizar and Song: The bottleneck router queue size should be 1-2 times the bandwidth-delay product.
RED issues (shortcomings) were studied through alternatives: BLUE, Adaptive RED, BRED, FRED, SRED, and Cisco’s WRED.
  e.g. FRED shows that RED does not promote fair sharing of link bandwidth between TCP flows with long RTTs or small windows and RED does not provide protection from non-adaptive flows (e.g, UDP flows).

## Slide 6: Background and Related Work
ECN was not considered in this paper.
The big deal - Most of the previous studies used small number of sources except the BLUE paper with 1000-4000 Parento on-off sources (but BLUE uses ECN).
Previous tuning results include:
  optimal maxp is dependent on the number of flows.
  router queue length stabilizes around maxth for a large number of flows.

## Slide 7: Background and Related Work
Previous analytic and simulation modeling at INRIA results:
  TCP goodput does not improve significantly with RED and this effect is independent of the number of flows.
  RED has lower mean queueing delay but much higher delay variance.
Conclusion – research pieces missing include: Web-like traffic and worst-case studies where there are dynamically changing number of TCP flows with highly variable lifetimes.

## Slide 8: Experimental Methodology

## Slide 9: Experimental Methodology
{These researchers used careful, meticulous, experimental techniques that are excellent.}
They use FreeBSD 2.2.8, ALTQ version 1.2 extensions, and dummynet to build a lab configuration that emulates full-duplex Web traffic through two routers separating Web request generators {browser machines} from Web servers.
They emulate RTT’s uniformly selected from 7-137 ms. range derived from measured data (mean 79 ms.).
FreeBSD default TCP window size of 16KB was used.
A modified version of tcpdump is used to collect TCP/IP headers.

## Slide 10: Web-like Traffic Generation
The synthetic HTTP traffic for the experiments is based on Mah’s Web browsing model [1995 data] that include:
  HTTP request length in bytes
  HTTP reply length in bytes
  The number of embedded (file) references per page
  The time between retrieval of two successive pages (user think time)
  The number of consecutive pages requested from a server.

## Slide 11: Web-like Traffic Generation
The empirical distributions for all these elements were used in synthetic-traffic generators they built.
The client-side request-generation program emulates behavioral elements of Web browsing.
Important parameters include the size of server requests, the number of browser users (several hundred!!) each instance of the program represents and the user think time.
A new TCP connection is made for each request/response pair (HTTP 1.0).
Another parameter: number of concurrent TCP connections per browser user {to mimic browser behavior}.

## Slide 12: Experiment Calibrations and Procedures
They needed to insure that the congested link between routers was the primary bottleneck on the end-to-end path.
They needed to guarantee that the offered load on the testbed network could be predictably controlled using the number of emulated browser users as a parameter to the traffic generator.
To simplify analysis, the number of emulated users remains fixed throughout one experiment.

## Slide 13: Experimental Methodology
Monitoring tools:
  At router interface collect: router queue size mean and variance, max queue size, min queue size sampled every 3 ms.
  The machine connected to hubs forming links to routers uses a modified version of tcpdump to produce log of link throughput.
  end-to-end measurements done on end-systems (e.g., response times).

## Slide 14: Experimental Calibrations and Procedures
Figure 3 and 4 show desired linear increases that imply no fundamental resource limitations. Note – these runs use a 100 Mbps link.
The authors were concerned about exceeding the 64 socket descriptor limitation on one FreeBSD process. This limit was never encountered due to long user think times.
3500 [100%] 3750 [110%]

## Slide 15: Experimental Calibrations and Procedures
Figures 5 and 6 show the highly bursty nature of requests by 3500 users during one second intervals.

## Slide 16: Experimental Procedures
After initializing and configuring the test-bed, the server-side processes were started followed by the browser processes.
Each browser emulated an equal number of users chosen to place load on network that represent 50, 70, 80, 90, 98 or 110 percent of 10 Mbps capacity.
Each experiments ran for 90 minutes with the first 20 minutes discarded to eliminate startup and stabilization effects.

## Slide 17: Experiment Calibrations and Procedures
Best-case
performance
Unstable
Start up
Behavior

## Slide 18: Experimental Procedures
Figure 8 represents the best-case performance for 3500 browsers generating request/response pairs in an unconstrained network.
Since responses from the servers are much larger than requests to server, only the effects on the IP output queue carrying traffic from servers to browsers is reported (All other queues are FIFO with queue size of 50 elements).
They measure: end-to-end response times, percent of IP packets dropped at the bottlenecked link, mean queue size and throughput achieved on the link.

## Slide 19: FIFO Results [Drop Tail]
FIFO tests run to establish a baseline.
* For the critical FIFO parameter, queue size, the consensus is roughly 2-4 times the bandwidth-delay product (bdp).
  mean min RTT = 79 ms.
  10 Mbps congested link => 96 K bytes (bdp)
  measured IP datagrams approx. 1 K bytes  190 - 380 elements in FIFO queue to be within guidelines.

## Slide 20: FIFO Results
poor
performance
tradeoff

## Slide 21: Appendix B

## Slide 22: FIFO Results
In Figure 9 a queue size of from 120 to 190 is a reasonable choice (1.25- 2 bdp) especially when one considers the tradeoffs for response time without significant loss in link utilization or high drops.
At 98% (Figure 9c), one can see the tradeoff of using a queue length of 120. Namely, longer response times for shorter objects, but shorter response times for longer objects.

## Slide 23: FIFO Results

## Slide 24: Figure 10 FIFO Results
At loads below 80% capacity, there is no significant change in response time as a function of load.
Response time degrades sharply when offered load exceeds link capacity.

## Slide 25: RED Experimental Goals
Determine the RED parameter settings that provide good performance for Web traffic.
  Additionally review the RED parameter guidelines.
Another objective is to examine the tradeoffs in RED tuning parameter choices.
The FIFO results show complex tradeoffs between response times for short responses and response times for longer responses.

## Slide 26: RED Results

## Slide 27: Figure 11 RED Results
The queue size was set to 480 to eliminate physical queue length (qlen) as a factor.
The figure shows the effect of varying loads on response time distributions.
(minth , maxth) set to (30, 90)
The interesting range for varying RED parameters for optimization is between 90-110% load levels where performance decreases significantly.

## Slide 28: RED Results
bad choice

## Slide 29: Figure 12 RED Results
The goal is to study minth , maxth choices
  The Floyd recommended choice (5, 15) yields bad performance at 90% load and poor performance at 98% load.
(30, 90) or (60, 180) are the best choices!
The authors prefer (30, 90) at 98% load.
After Figure 13, authors conclude that (30, 90) provides the best ‘balance’ for response time performance.

## Slide 30
RED Results
The effect of varying minth is small at 90% load.

## Slide 31
RED Results

## Slide 32: Figure 14 RED Results
maxp = 0.25 has negative impact on performance – too many packets are dropped. Generally, changes in wq and maxp mainly impact longer flows (the back part of the CDF).
There is no evidence to use values other than recommended wq = 1/512 and maxp = 0.10

## Slide 33: RED Results
120 is a good choice for queue length at 90% and 110% load.

## Slide 34: RED Results

## Slide 35: Best RED Parameter Summary

## Slide 36: RED Results

## Slide 37: Figures 15 and 16 RED Results
RED can be tuned to yield “best settings” for a given load percentage.
At high loads, near saturation, there is a significant downside potential for choosing “bad” parameter settings
bottom line result- RED tuning is not easy!

## Slide 38: RED Response Time Analysis
This section added when paper went to journal.
Detailed analysis of retransmission patterns for various TCP segments (e.g., SYN, FIN)
This section reinforces the complexity of understanding the effects of RED for HTTP traffic.

## Slide 39: RED Response Time Analysis

## Slide 40: FIFO versus RED
The only ‘distinct’ improvement for RED is at 98% load where careful tuning improves response times for shorter responses.

## Slide 41: Conclusions
Contrary to expectations, there is little improvement in response times for RED for offered loads up to 90%.
At loads approaching link saturation, RED can be carefully tuned to provide better response times.
Above 90%, load response times are more sensitive to RED settings with a greater downside potential of choosing bad parameter settings.
There seems to be no advantage to deploying RED on links carrying only Web traffic.
Question: Why these results for these experiments?