## Slide 1: An In-depth Study of LTE: Effect of Network Protocol and Application Behavior on Performance
Authors: Junxian Huang, Feng Qian, Yihua Guo, Yuanyuan Zhou, Qiang Xu, Z. Morley Mao, Subhabrata Sen, Oliver Spatscheck
CS577
Brett Levasseur

## Slide 2: Outline
Introduction
LTE Data And Local Testbed
LTE Network Characteristics
Abnormal TCP Behavior
Bandwidth Estimation
Network Applications in LTE
Conclusions
Questions

## Slide 3: Introduction
Previously observed LTE network characteristics
  Higher bandwidths
  Lower RTT
  TCP underutilizes links
This work examines
  Measurements from real LTE network
  TCP bandwidth estimation algorithm
  Power management

## Slide 4: LTE Network
UE – User Equipment
RAN – Radio Access Network
CN – Core Network
Monitor – Author’s data collection point
PEP – Performance Enhancing Proxy

## Slide 5: LTE Network
PEP – Not part of normal CN
  Intercepts TCP traffic on ports 80 and 8080
Splits end to end TCP connection to two
  UE to PEP
  PEP to server
Performs compression and caching
Internet
RAN
PGW
SGW
MME
HSS
[Dahlman]

## Slide 6: LTE Data
Covered 22 eNBs in a US city
Collection from 10/12/2012 - 10/22/2012
Collected
  IP and transport headers
  64 bit timestamps per packet
  HTTP headers
  3.8 billion packets
  2.9 TB of traffic (324 GB of headers)

## Slide 7: Local Test Bed
UE
  Samsung Galaxy S III
  Android 4.0.4 / Linux Kernel 3.0.8
Server
  2GB RAM / 2.4 GHz Intel Core 2 CPU
  Ubuntu 12.04 / Linux Kernel 3.2.0-36-generic
  TCP CUBIC
Measured TCP throughput and RTT
Used two different LTE networks

## Slide 8: Outline
Introduction
LTE Data And Local Testbed
LTE Network Characteristics
Abnormal TCP Behavior
Bandwidth Estimation
Network Applications in LTE
Conclusions
Questions

## Slide 9: Measurements
Majority of traffic is TCP
Majority of the remainder is UDP
TCP Flows (95.3 %) | HTTP (80/8080) 50.1%
 | HTTPS (443) 42.1%
TCP Bytes (97.2%) | HTTP (80/8080) 76.6%
 | HTTPS (443) 14.8%

## Slide 10: TCP Flow Size

## Slide 11: TCP Flow Size
UL Flows | 90%, less than 2.9 KB | 
 | 10.9% have no uplink | 
 | Top 0.1% (by payload) account for 63.9% of total bytes | 
 | 73.6% of the top flows are images | 
DL Flows | 90%, less than 35.9 KB | 
 | 11.3% have no downlink | 
 | Top 0.6% (by payload) account for 61.7% of total bytes | 
 | Top 5% (by payload size) | Payload >= 85.9 KB
 |  | 80.3% use HTTP
 |  | 74.4% video or audio

## Slide 12: TCP Flow Duration

## Slide 13: TCP Flow Duration
Flows | Duration
48.1% | < 5 seconds
6.8% | >= 3 minutes
2.8% | >= 10 minutes
Flows | Termination
86.2% | TCP FIN
5.4% | TCP RESET
8.5% | TCP SYN (did not connect properly)

## Slide 14: Tail Time
10 seconds between last transmission and the UE radio being turned off

## Slide 15: TCP Flow Rate
Larger flows send faster than smaller flows
Flow duration and rate are more negatively correlated than on Internet backbone
Better flow rate

## Slide 16: TCP Concurrency
72.1% of the time there is only one active TCP flow
Possibly higher for smartphones

## Slide 17: RTT
C-M = Client to monitor
M-P = Monitor to PEP
M-S = Monitor to server
C-S = Client to server
RTT Monitor to server > than client to monitor
Indicates wireless link is not largest delay factor
Better
RTT
RTT to M-S > C-M

## Slide 18: LTE Promotion Delay
Time to turn radio on
G(TSb - TSa) = RTT seen by UE
G – Inverse ticking frequency of UE’s clock
Percentile | Promotion Delay
25% | 319ms
50% | 435ms
75% | 558ms

## Slide 19: Queuing Delay

## Slide 20: Queuing Delay
10% of large flows have > 200 KB in-flight
Leads to
  Queue delay
  Longer RTT
  Created by long flows but impacts short flows

## Slide 21: TCP Retransmission Rate
38.1% of flows have no retransmission
0.06% is the median of flows with retransmission
Physical/MAC layer retransmission reduced transport layer retransmission
Study does not look at LTE RLC layer retransmissions

## Slide 22: Measurement History
LTE outperforms 3G, WiMAX and WiFi
4GTest LTE is higher than measurements
  Possibly due to rate limiting at remote server

## Slide 23: Outline
Introduction
LTE Data And Local Testbed
LTE Network Characteristics
Abnormal TCP Behavior
Bandwidth Estimation
Network Applications in LTE
Conclusions
Questions

## Slide 24: Duplicate ACKs
Medians
  17 Dup ACKs
  2 out of order packets
Over 29% of flows have > 100 Dup ACKs
Ratio Dup ACK / out of order
  24.7% of flows over 25
  Some up to 5,000
  1 out of order packet can cause many Dup ACKs
Notes: Large flows (down link)
  Longer than 5 sec
  Larger than 1MB
  0.3% of flows
  47.7% of data

## Slide 25: Undesired Slow Start
Undesired Slow Start – Large RTT triggers RTO
Author’s measure undesired slow start with
Where is average downlink throughput from t1 ms to t2 ms after last Dup ACK
Rss > 1.5 in slow start
  20.1% of large flows have >= 1 lost packet
  12.3% of all large flows have >= 1 lost packet

## Slide 26: Undesired Slow Start
Rss = 1.0
Rss = 3.5

## Slide 27: Mitigate Undesired Slow Start
Update RTO from duplicate ACKs with SACK
  Take difference between SACK window of two consecutive duplicate ACKs
  82.3% of flows used SACK in dataset
  < 1% of flows had packet reordering
Update RTO from duplicate ACKs without SACK
  Assume duplicate ACKs in response to data packets in order
Prevent > 95% of observed undesired slow starts

## Slide 28: Outline
Introduction
LTE Data And Local Testbed
LTE Network Characteristics
Abnormal TCP Behavior
Bandwidth Estimation
Network Applications in LTE
Conclusions
Questions

## Slide 29: TCP Transmission Rate
Sending Rate from Monitor
Receive Rate at UE

## Slide 30: TCP Timestamps
Replace t1 and t5 with t2 and t6
t2 and t6 originate at UE
Replace t2 and t6 with TCP Timestamps
Infer G

## Slide 31: Estimation Accuracy
For accurate G
  t7 – t3 >
Error rate of G drops as grows
At = 3 seconds error rate < 0.1%

## Slide 32: Estimation Accuracy
With = 3 seconds the error rate of inferred G < 0.1% for the majority of flows
If G is unknown it is estimated from its formula
Flows | G
5.9% | NA
57.3% | 1ms/tick
36.4% | 10ms/tick
0.4% | 100ms/tick

## Slide 33: Estimation Summary
G is known or inferred
Calculate Rsnd
If Rsnd >= C AND packets in order AND no duplicates AND last packet is not delayed ACK
  Rrcv calculated
If C too small – underestimate
If C too large – not enough samples
C = 30Mbps

## Slide 34: Validation
Compare server side estimate and UE trace
1 sec sample window average error rate is 7.9%
0.1 sec sample window average error rate has higher variation

## Slide 35: Validation
Actual throughput is UE perceived throughput
Used 1 sec sample window
Actual throughput varies around 10Mbps
Error varies by +- 1 Mbps

## Slide 36: Large Flow Utilization
Median ratio 19.8%
71.3% of large flows < 50% utilization
6.4% use more bandwidth than estimated
Average ratio 34.6%
Low utilization, flows last longer
  Higher radio usage
Notes: Bandwidth estimation ran on large TCP flows
  > 5 seconds, > 1 MB
  Flow split into 250ms windows
  1 bandwidth estimation per window

## Slide 37: LTE Bandwidth Variation
Two large flows
  Two different users
  Two different times
Bandwidth varies over time
  Condition of the wireless link
  Movement
  Resource scheduling

## Slide 38: RTT & Throughput
Experiments with modifiable RTT
  Used iptables to redirect packets to scheduler
  Scheduler changes available bandwidth similar to observed LTE
  Scheduler injects delays to impact RTT
Under small RTT TCP utilizes 95% of the bandwidth
RTT > 400ms utilization drops below 50%

## Slide 39: Outline
Introduction
LTE Data And Local Testbed
LTE Network Characteristics
Abnormal TCP Behavior
Bandwidth Estimation
Network Applications in LTE
Conclusions
Questions

## Slide 40: HTTP Characterization
12.9% of video content is octet-streams generated mostly by video players
HTTP Content | % of traffic
Video | 37.8%
Images | 19.5%
Text | 11.8%
Zip | 8.3%
Audio | 6.5%
Other | 5.6%
Unknown | 10.5%

## Slide 41: TCP Receive Window
Shazam app on iOS
30s, 1 MB audio
0s – 2s 3Mbps
Recv window full
2s – 9s < 300 Kbps
Download could have been done in 2.5s
Connection not closed until 30s
If receive window did not fill up

## Slide 42: TCP Receive Window
Receive Window around 131,712 +- 600 bytes
  True for > 90% of iOS, Android and Windows Phone flows
Applications not reading from receive buffer quickly enough
52.6% of downlink TCP flows experience full receive window
  91.2% of these bottleneck happens in initial 10% of the flow duration

## Slide 43: Application Design
Netflix on iOS
Multiple HTTP byte-range requests
Many short HTTP responses
  < 1s
  1 – 4MB
Periodic requests leaves radio idle

## Slide 44: Discussion
Manufactures reduce TCP receive window
  Decreases buffer bloat
  Underutilizes network
Use application buffers
  Relieves TCP buffers
  Allows radio interface to close sooner
Increase amount downloaded per request, decrease number of requests

## Slide 45: Conclusions
Not updating RTT from Dup ACKs causes performance issues with single packet loss
Bandwidth estimation algorithm
  71.3% of large flows have < 50% utilization
  High variation of network bandwidth
  cwnd too slow to adjust
TCP receive window throttles 52.6% of downlink flows
App design underutilizes bandwidth

## Slide 46: Questions

## Slide 47: References
Huan J. et all, An In-depth Study of LTE: Effect of Network Protocol and Application Behavior on Performance. SIGCOMM 2013.
Dahlman E. et all, 4G LTE/LTE-Advanced for Mobile Broadband. Academic Press, 2011.