## Slide 1: Characterization of 802.11 Wireless Networks in the Home
The First Workshop on Wireless Network Measurements (WiNMee) Trentino, Italy, April 2005
M. Yarvis. K. Papagiannaki and W. Conner
Intel Research
Presenter - Bob Kinicki
rek@cs.wpi.edu
Notes: Today, Prof Bob Kinicki and I are going to present our paper “Application, Network, and Linklayer measurements of Streaming video over a wireless Campus Network”.
Before I start the presentation, I want to introduce the people from WPI Wireless streaming research group.
They are our group members.
Prof Claypool, prof Kiniki, Mingzhe,Huahui, and Ashishi

## Slide 2: Outline
Introduction
Experimental Environment
Results
Conclusions

## Slide 3: Introduction
Little was known about the properties of home wireless networks in 2005.
Conjecture is that wireless home behavior will be similar to enterprise wireless network behavior.
The goal was to specifically examine the impact of transmission rate and transmission power on the quality of home wireless links.

## Slide 4: Experimental Environment
Experimental Setup
Methodology
Validation

## Slide 5: Experimental Setup
Measurements in Three Homes
Six wireless nodes inside each home
Ad Hoc communication (No AP)

## Slide 6: Experimental Methodology
DL layer retransmissions disabled.
300 1024-byte UDP probe packets sent every 500 ms (150 seconds).
No simultaneous transmissions.
Experiments run during the night to avoid interference from moving people.
Allows quantifying loss rate observed by each wireless link.

## Slide 7: ushome1 Experiments
Link asymmetry

## Slide 8: Methodology Validation
Duplicated results
Experimental length
Time of day variability

## Slide 9
Link performance does not change significantly.

## Slide 10: Experiment Length ?

## Slide 11: Time of Day Effect ?
Good link remains good, bad link remains bad.

## Slide 12: Results
Evaluates the home wireless environment along six dimensions:
Transmission rate (txrate)
Transmission power (txpower)
Node location
House type
External interference
Physical layer

## Slide 13: Overall Characteristics
Link loss rates were higher when the encoding rate was higher.
Link loss rates were lower when the power level increased.

## Slide 14: Overall Characteristics (cont.)
Wireless connectivity is NOT omnipresent.
Several asymmetric links were observed.
In most experiments, at least one node pair had 30% loss.

## Slide 15: ukhome1

## Slide 16: ushome1

## Slide 17: ushome2

## Slide 18: Figure 5 Loss Rates Layout1 ukhome1

## Slide 19: Figure 5 Loss Rates Layout1 ushome1

## Slide 20: Figure 5 Loss Rates Layout1 ushome2

## Slide 21: Small changes in antenna orientation and location
For layout2, layout1 nodes are translated a few inches and antennas are rotated to face another direction.
Conclusion:: exact node placement is a key contributor to performance.

## Slide 22
Figure 5a
ukhome1
Layout1
Figure 6a
ukhome1
layout2

## Slide 23: ukhome1

## Slide 24: Large changes in node placement
For ukhome1 nodes 2 and nodes 7 were moved to a different location within the same room from layout1 to produce layout3.
The other nodes were moved slightly from their layout1 positions.

## Slide 25: ukhome1

## Slide 26
Figure 5a
ukhome1
Layout1
Figure 8
ukhome1
layout3
More significant loss in links and quality

## Slide 27: Link quality and distance relationship
Results in Figure 9 for layout2 for all three homes show there is no correlation between physical distance and wireless link quality.
This result holds across homes and across txrate and txpower settings.

## Slide 28: Link quality and distance relationship layout2
Figure 9: ukhome1

## Slide 29: Link quality and distance relationship layout2
Figure 9: ushome1

## Slide 30: Link quality and distance relationship layout2
Figure 9: ushome2

## Slide 31: Microwave Oven Interference

## Slide 32: Between home comparisons
Small home (ukhome1) had better results sometimes (layout1), but worse performance under layout2.
Precise node location is more important than home size or distance.

## Slide 33: IEEE 802.11a Experiments
Results were quite similar to 802.11b results!
802.11a yielded slightly better performance.
802.11a results were more ‘binary’, namely either good or very bad.

## Slide 34: Layout1 ushome1
Figure 5b
802.11b
Figure 11a
802.11a

## Slide 35: IEEE 802.11a Experiments

## Slide 36: Conclusions
Wireless links inside homes tend to be stable over time, highly asymmetric and highly variable from one link to the next.
Precise node location is probably the single most important factor.
Distance has no impact on quality of the wireless links.
Small changes in antenna orientation and node location can dramatically change individual link performance.

## Slide 37: Conclusions (cont.)
802.11a performed slightly better in homes.
But for both 802.11a and 802.11b the highest allowable rate may not be possible due to high loss.
Home networks face similar problems to larger networks.
Results imply the location of the AP will have a significant impact on overall performance.

## Slide 38: Characterization of 802.11 Wireless Networks in the Home
Thank You!
Questions ??
Notes: Today, Prof Bob Kinicki and I are going to present our paper “Application, Network, and Linklayer measurements of Streaming video over a wireless Campus Network”.
Before I start the presentation, I want to introduce the people from WPI Wireless streaming research group.
They are our group members.
Prof Claypool, prof Kiniki, Mingzhe,Huahui, and Ashishi