## Slide 1: TCP Vegas
Lawrence s. Brakmo Sean W. O’Malley Larry l. Peterson Presented TCP Vegas in 1994
Presented by Chung Tran

## Slide 2: TCP Vegas VS TCP Reno
When TCP Vegas was research and presented in 1994 it stated that it have a better throughput than TCP Reno by 40 to 70 percent
Yet today most networking uses Reno instead of Vegas
I will attempt to explain the algorithms
What is a major problem with Vegas
Conclusion of why Reno is more widely accepted
Further research that been done for Vegas
Questions, Comments?

## Slide 3: Claimed and Unique idea
TCP Vegas is a congestion avoidance algorithm
Where Reno would have an aggressive retransmitting strategy and this would take away bandwidth from TCP connection
The claimed was Vegas achieved a more efficient uses of the allowed bandwidth
In the original paper they run it base on simulation using x-kernel where they implemented to simulate what they needed
They needed to trace the behavior of TCP so they wrote the trace data into memory ( 8 bytes) and than dump the data into a file when the test was over

## Slide 4: Algorithm
Congestion Avoidance
Expected = CWND (WindowSize)/BaseRTT
Actual = CWND ( WindowSize) / RTT
Diff = Expected – Actual
Threshold α < β
Diff < α increase CWND linearly on the next RTT
Diff > β decrease CWND linearly on the next RTT

## Slide 5: Known Issues
“Nice guys. Finish Last.” by Leo Durocher 1939
TCP Vegas is not uses widely instead they uses Reno even those the throughput of Vegas is 40-70 percent better than Reno
One of the major issues is that Reno is mostly uses and it will hog up all the buffer space available, Vegas is like the nice guy in a race it will back-off when it running with Reno and will consider this a Congestion and base on the algorithm I explain earlier this will cause it to not be useful

## Slide 6: Why Reno uses more than Vegas
The professor pointed out that Vegas came out about the time of RED and everyone thought RED was going to revolution the way network connection will be design
However, RED was not as great as suggested and so Reno was put into place and afterward running Vegas with Reno just cause more problems.
As stated Reno take up all of the buffer space and Vegas would consider this a congestion and would not work

## Slide 7: Research benefit
However, a lot of research had been done in improving TCP Vegas because the simple ideas and the amount of throughput and less retransmission make it beneficial to study
In 2003 there was a paper to propose an improvement to Vegas : An enhanced Congestion Avoidance Mechanism for TCP Vegas
In 2008 after the smartphone boom even more research into TCP Vegas for wireless was propose for example: Vegas-W: An Enhanced TCP-Vegas for wireless Ad Hoc networks
These are just a few examples of what researchers are doing with TCP-Vegas

## Slide 8: Questions & Comments
Before this PowerPoint come to a conclusion I would like to open this up for any questions of comments on this subject?
Final thoughts