## Slide 1: Framing and Stuffing
Computer Networks

## Slide 2: Framing & Stuffing Outline
Synchronous vs Asynchronous Transmissions
Asynchronous Character Transmissions
Framing – Identifying Synchronous Block Boundaries
Byte Stuffing
Bit Stuffing
PPP Byte Stuffing

## Slide 3: Synchronous versus Asynchronous Transmissions
There exists a hierarchy of synchronization tasks:
  Bit level : recognizing the start and end of each bit.
  Character or byte level : recognizing the start and end of each character (or small unit of data)
  Block or message level : recognize the start and end of each large unit of data (in networks this is a frame).

## Slide 4: Synchronous versus Asynchronous Transmissions [Halsall]
A fundamental requirement of digital data communications is that the receiver knows the starting time and the duration of each bit.
Asynchronous transmission :: each character (or byte) is treated independently for clock (bit) and character (byte) synchronization purposes and the receiver resynchronizes at the start of each character received.
Synchronous transmission :: the complete frame is transmitted as a contiguous string of bits and the receiver endeavors to keep in synchronism with the incoming bit stream for the duration of the frame.

## Slide 5: Byte Level Synchronization in Asynchronous Transmissions
Characters transmitted at random intervals (e.g., from keyboard)
Direction of transmission
Leon-Garcia & Widjaja:
Communication Networks

## Slide 6: Synchronous Transmissions
More efficient, i.e., less overhead
Blocks of characters are transmitted without start and stop codes.
The transmitted stream is suitably encoded so the receiver can stay ’in synch’ by:
  Using a separate clock line.
  Embedding clocking information into data (e.g. biphase coding).

## Slide 7: Methods to Identify Frames [Tanenbaum]
1. Byte counts
2. Starting/ending bytes [byte stuffing]
3. Starting/ending flags [bit stuffing]
4. Using physical layer coding violations (i.e., invalid physical codes, used in token rings)

## Slide 8: Framing
The contents of each frame are encapsulated between a pair of reserved characters or bytes for frame synchronization.
Preamble
Bit Pattern
Postamble
Bit Pattern
frame

## Slide 9: Byte Stuffing [HDLC Example]
Also referred to as character stuffing.
ASCII characters are used as framing delimiters (e.g. DLE STX and DLE ETX).
The problem occurs when these character patterns occur within the “transparent” data.
Solution: sender stuffs an extra DLE into the data stream just before each occurrence of an ‘accidental’ DLE in the data stream.
The data link layer on the receiving end unstuffs the DLE before giving the data to the network layer.

## Slide 10: HDLC Byte Stuffing
DLE
STX
DLE
ETX
Transparent Data
DLE
STX
DLE
ETX
A
B
DLE
H
W
DLE
STX
DLE
ETX
A
B
DLE
H
W
DLE
DLE
STX
DLE
ETX
A
B
DLE
H
W
Stuffed
Unstuffed
Before

## Slide 11: Bit Stuffing
Each frame begins and ends with a special bit pattern called a flag byte [01111110]. {Note this is 7E in hex.}
Whenever the sender data link layer encounters five consecutive ones in the data stream, it automatically stuffs a 0 bit into the outgoing stream.
When the receiver sees five consecutive incoming ones followed by a 0 bit, it automatically destuffs the 0 bit before sending the data to the network layer.

## Slide 12: Bit Stuffing
Input Stream
Stuffed Stream
Unstuffed Stream
0110111111100111110111111111100000
01101111101100111110011111011111000000
0110111111100111110111111111100000
Stuffed bits

## Slide 13: PPP (Point-to-Point Protocol) Frame Format
Flag
Flag
Address
Control
Information
CRC
Protocol
01111110
01111110
11111111
00000011
Unnumbered frame
Specifies what kind of packet is contained in the payload, e.g., LCP, NCP, IP, OSI CLNP, IPX
All stations are to
accept the frame
Leon-Garcia & Widjaja:
Communication Networks

## Slide 14: PPP Byte Stuffing
Flag
flag
Address
Control
Information
CRC
Protocol
01111110
11111111
00000011
01111110
7E
7E
7E
7D
5D
33
42
7E
7E
7E
7E
7D
7D
5D
33
33
7D
5E
42
42
7E
Input
Stuffed Stream
Unstuffed Stream
Flag
01111110
Flag
01111110

## Slide 15: Framing & Stuffing Summary
Synchronous vs Asynchronous Transmissions at different levels.
Character Transmissions {Asynchronous}
Synchronize bits (physical layer issue) to send blocks of characters as frames at data link layer.
Framing – identifying a frame.
HDLC and PPP Byte Stuffing
Bit Stuffing