## Slide 1: Sample Network Performance Problems

## Slide 2
12
1
11
8
4
7
2
6
9
10
14
5
13
15
3
Host
B
Host
C
Host
L
Host
D
Host
E
Host
G
Host
J
Host
A
Host
H
Host
F
Host
M
16
17
W
T
X
Y
Z
nodes
W2
W3
W4
AP
W1

## Slide 3
1. What is the end-to-end packet latency in this store-and-forward subnet from router 1 to router 6 ?
Assume: All links: 2.5 km; C = 100Mbps; propagation speed = 200m/microsec.
queuing delay = processing delay =0; packet size = 1000 bytes
Solution:
end-to-end packet delay = 4 (equal hops) x link delay
link delay = PROC +QD + TRANS + PROP = 0 + 0 + transmission time +
propagation delay
1000 bytes 8 x 103 bits
transmission time = ------------- = ----------------- = 8 x 10-5 = 80 microseconds.
100 Mbps 108 bps
2500 m
prop delay = ---------------------- = 12.5 microseconds
200 m/ microsec
link delay = 92.5 microseconds
end-to-end subnet delay = 4 x 92.5 = 370 microseconds
Host
A
Host
H
1
14
15
17
6

## Slide 4
2. What is the end-to-end packet delay in this store-and-forward subnet from router 1 to router 6 under the scenario that when a packet from router 1 arrives at router 15 there are three packets enqueued for the link to router 17?
Assume: All links: 2.5 km; C = 100Mbps; propagation speed = 200m/microsec.
processing delay =0; all packet sizes = 1000 bytes
Implied Assumption: queues at 1, 14, and 17 are empty when the packet arrives at node 15.
Required Insight: there will be no queuing delay at 17 even if all three queued packets are going to 6.
Solution:
end-to-end packet delay = 4 (equal hops) x link delay + queuing delay at node 15.
link delay = PROC +QD + TRANS + PROP = 0 + 0 + transmission time + propagation delay
1000 bytes 8 x 103 bits
transmission time = ------------- = ----------------- = 8 x 10-5 = 80 microseconds.
100 Mbps 108 bps
2500 m
prop delay = ---------------------- = 12.5 microseconds
200 m/ microsec
link delay = 92.5 microseconds
queueing delay at node 15 = 3 packets * transmission time = 3* 80 microseconds = 240 microseconds
end-to-end subnet delay = 4 x 92.5 + 240 = 610 microseconds
Host
A
Host
H
1
14
15
17
6

## Slide 5
What is the end-to-end packet delay in this store-and-forward subnet from router 1 to router 6 under the scenario that when a packet from router 1 arrives at router 15 there are three packets enqueued for the link to router 17?
3.a Assume Now All links: 2.5 km; C = 10Mbps;
propagation speed 200m/microsec.
processing delay = 0; all packet sizes = 1000 bytes
3.b Assume Now All links: 25 km; C = 100 Mbps;
propagation speed 200m/microsec.
processing delay = 0; all packet sizes = 1000 bytes
4.a Assume Now All links: 2.5 km; C = 100Mbps;
propagation speed 200m/microsec.
processing delay = 10 microsecs; all packet sizes = 1000 bytes
4.B Assume Now All links: 2.5 km; C = 100Mbps;
propagation speed 200m/microsec.
processing delay = 10 microsecs; all packet sizes = 3000 bytes
Host
A
Host
H
1
14
15
17
6

## Slide 6
Food for Thought
Host
E
9
13
15
17
4
AP
W1
Host
F
8
13
15
17
16
3
Host
L
Z
5. How does the end-to-end packet delay determination change when we send a packet from Host E to wireless Host W1?
6. How does the end-to-end packet delay determination change when we send a packet from Host F to Host Z that is on the Ethernet LAN?

## Slide 7: Happy Chinese New Year
The Year of the Snake