## Slide 1: Performance Evaluation of Computer Networks
Professor Bob Kinicki
Computer Science Department

## Slide 2: Outline
Performance Evaluation
Computer Network Performance Metrics
Performance Evaluation Techniques
  Workload Characterization
  Simulation Models
  Analytic Models
Empirical Measurement Studies
  What to measure?
  Choice of measurement tools
  The Design of Measurement Experiments

## Slide 3: Performance Evaluation
Historically, performance evaluation was initially concerned with computer systems.
During the 1970’s and 1980’s, computer system performance evaluation emerged as an essential component of Computer Science due to rapid and concurrent advancements in computer hardware and computer operating systems.
The resultant increased complexity of modern computer systems made understanding and evaluating computer systems more difficult.

## Slide 4: Performance Evaluation
Performance evaluation is the application of the scientific method to the study of computer systems.
Viewed as distinct from computer system design, the goal of performance evaluation is to determine the effectiveness and fairness of a computer system that is assumed to work correctly.
Performance evaluation techniques have been developed to accurately measure the effectiveness with which computer system resources are managed while striving to provide service that is fair to all customer classes.

## Slide 5: Outline
Performance Evaluation
Computer Network Performance Metrics
Performance Evaluation Techniques
  Workload Characterization
  Simulation Models
  Analytic Models
Empirical Measurement Studies
  What to measure?
  Choice of measurement tools
  The Design of Measurement Experiments

## Slide 6: Computer Network Performance Metrics
Metric :: a descriptor used to represent some aspect of a computer network’s performance.
The goal is objective performance indices.
For computer networks, metrics can capture performance at multiple layers of the protocol stack, e.g.,
  UDP throughput
  IP packet round trip time
  MAC layer channel utilization
Performance metrics can be positive and negative.
  e.g., goodput, packet loss rate, MAC layer retries

## Slide 7
12
1
11
8
4
7
2
6
9
10
14
5
13
15
3
Host
B
Host
C
Host
D
Host
E
Host
G
Host
J
Host
A
Host
H
Host
F
Host
N
16
17
routers
Host
L
Host
M
Wide Area Network (WAN)

## Slide 8
Wireless Local Area Network (WLAN)
AP
Clients
Server

## Slide 9: Sample Performance Measures
Category | Metric | Units
productivity | throughput effective capacity | Mbps
responsiveness | delay round trip time queue size | milliseconds packets
utilization | channel utilization | percentage of time busy
losses | packet loss rate frame retries | loss percentage
buffer problems | AP queue overflow playout buffer underflow | packet drops rebuffer events

## Slide 10
12
1
11
8
4
7
2
6
9
10
14
5
13
15
3
Host
B
Host
C
Host
D
Host
E
Host
G
Host
J
Host
A
Host
H
Host
F
Host
N
16
17
nodes
Host
L
Host
M
Wide Area Network (WAN)

## Slide 11
A
Z
X
C
Y
B
Local Area Network (LAN)

## Slide 12
Wireless Local Area Network (WLAN)
AP
Client
Server

## Slide 13: Outline
Performance Evaluation
Computer Network Performance Metrics
Performance Evaluation Techniques
  Workload Characterization
  Simulation Models
  Analytic Models
Empirical Measurement Studies
  What to measure?
  Choice of measurement tools
  The Design of Measurement Experiments

## Slide 14: Performance Evaluation Techniques
Workload characterization for computer networks involves the design and choice of traffic types that provide the inputs for computer network performance evaluation.
Performance measures of computer networks are all dependent to some extent on the input workload, the network topology and the choices in controlled parameters or network default settings.
An evaluation study of a computer network seeks to determine the values for network performance indices under a given traffic workload and network configuration.

## Slide 15: Typical Network Traffic Types
Web Traffic between a Browser and an Internet Server.
Long-Lived File Transfers
  FTP downloads.
Multimedia Streaming
  Video clip downloads (UDP and/or TCP)
  Audio VOIP (Voice Over IP)
Peer-to-Peer Exchanges
  Concurrent downloads and uploads
Telnet file edits

## Slide 16
Wireless Local Area Network (WLAN)
AP
Client
Server

## Slide 17: Performance Evaluation Techniques
Models
  Simulation Modeling
  Analytic Modeling
  Both modeling techniques tend to rely on queuing theory.
Measurement Studies
  Empirical measurement of real networks
  Measurements where some aspect of the network architecture or topology is emulated via software or hardware.
The primary focus of this presentation is on the design and techniques used in experiments to measure real computer networks.
Network evaluation utilizes the actual network, an emulated network or a model of the network.

## Slide 18: Conceptual Models
Researchers utilize knowledge about the interactions of network components to understand and explain the workings of a computer network via a conceptual model.
Models are partitioned into simulation models or analytic models. Both model types rely on simplifying assumptions that that enable the model to capture important characteristics of networks (usually in terms of networks of queues).

## Slide 19: Simple Queuing Model
Arrivals
Queue
Server

## Slide 20: Networks of Queues Model

## Slide 21: Simulation Models
Simulation attempts to reproduce the behavior of the network in the time domain.
Event-driven simulation defines a network in terms of states and transitions where events trigger transitions.
Simulation is essentially a numeric solution that utilizes systems of equations and data structures to capture the behavior of the simulated network in terms of logical conditions.

## Slide 22: Simulation Models
The three types of simulators are:
  Trace-driven
  Program-driven
  Distribution-driven
The choice of the duration of a simulation run is subject to the same issues of estimating variance and variance reduction as found in the design of empirical measurements.

## Slide 23: Analytic Models
Similar to simulation models, analytic models involve systems of equations.
Analytic models of computer networks usually start with a network of queues model and develop a system of equations that may or may yield a closed form solution.
Analytic models of computer networks tend to be stochastic models built on the theory of stochastic processes associated with independent random variables.

## Slide 24: Outline
Performance Evaluation
Computer Network Performance Metrics
Performance Evaluation Techniques
  Workload Characterization
  Simulation Models
  Analytic Models
Empirical Measurement Studies
  What to measure?
  Choice of measurement tools
  The Design of Measurement Experiments

## Slide 25: Empirical Measurement Studies
The planning phase objectives of an empirical measurement are:
  To decide what to measure.
  To choose the measurement tools
  To design the experiments.
Network measurements can be either active or passive.
Active measurement involves purposely adding traffic to the network workload specifically to facilitate the measurement (e.g., sending packet pair probes into the network to estimate the available bandwidth along a flow path).
An example of a passive measurement tool is a network sniffer running in promiscuous mode to collect information about all packets traversing a network channel.

## Slide 26: What to Measure?
The overall objective of the computer network measurement study guides the choice of performance indices to be measured.
Metrics are either direct or indirect indices. Indirect indices require some type of data reduction process to determine metric values.
Due to the large data volume associated with network traffic, measurement of computer networks often involves filtering of data or events (e.g., It is common for network measurement tools to only retain packet headers for off-line analysis).
When the measurement strategy involves probabilistic sampling, the duration of the experiments is determined using confidence interval techniques.

## Slide 27: Network Measurement Tools
While hardware probes provide the best quality measurements, they are expensive and not always available.
The availability of software tools for computer networks depends on the ability to get inside the components of the network protocol stack and the ability to access nodes of the network topology.
Network software measurement tools provide ‘hooks’ within the network layering software to capture and store network measurement data.

## Slide 28: Choice of Measurement Tools
Key issues in the usability of network measurement tools are:
  Tool location
  Interference or bias introduced by the tool.
  Accuracy of the tool.
  Tool resolution
    - This has become a problem with respect to the granularity of system clocks relative to the speed of modern high speed network links.

## Slide 29
Wireless Local Area Network (WLAN)
AP
Clients
Server

## Slide 30: The Design of Measurement Experiments
Measurement Experiments are divided into two major categories:
Live measurements
With live empirical studies, the objective is to measure the performance of the computer network while it is handling real traffic.
The advantage of this type of study is that the measurement involves a real workload.
One disadvantage of measuring live traffic is being convinced that this measurement involves ‘typical’ traffic for this network.
Another disadvantage of live traffic measurement is that reproducibility of the exact same traffic workload is usually not possible. This is problematic when the goal is to evaluate the impact of changing network components on overall performance.

## Slide 31
2. Controlled-traffic measurements
Traffic generator tools or traffic script files provide repeatable, controlled traffic workloads on the network being measured.
Controlled-traffic workloads are chosen when the goal of the performance study is to evaluate the impact of different versions of a network component, strategy or algorithm on network performance.
Controlled, repeatable traffic makes it easier to conduct cause-and-effect performance analysis.
One difficulty with controlled-traffic is being confident in the accuracy of the traffic generator tool and the ability to conduct measurement experiments where the traffic workload choices are adequately varied to provide representative, robust network performance evaluation.
The Design of Measurement Experiments

## Slide 32: Measurement Design Decisions
Understanding which network components (or independent variables) significantly impact network performance.
Deciding which network parameters are to be controlled and/or held fixed during experimental runs.
How long to run a single experiment?
How many times to repeat an experiment?

## Slide 33
Time (sec)
Throughput (Mbps)

## Slide 34
Time (sec)
RSSI (dB)

## Slide 35: Measurement Design Decisions
When to run experiments?
  Namely, to determine whether time of day or other temporal periods influence performance measurements.
How to control, minimize and/or understand physical phenomenon or other interference sources that can produce discrepancies and variability in the measurement results?

## Slide 36
Time (sec)
Throughput (Mbps)

## Slide 37
Time (sec)
RSSI (dB)

## Slide 38: Measurement Design Decisions
What data filters to use?
How and where to store experimental results?
Determining the best choices of graphical and tabular forms of data representation to facilitate network performance analysis while providing a clear view of the results of the computer network performance evaluation.

## Slide 39
Time (sec)
MAC Layer Retries

## Slide 40: Cumulative Distribution Function (CDF)

## Slide 41: Coming Attractions
Professor Claypool will discuss:
The Scientific Method applied to Computer Science
Statistical Techniques used in Experimental Measurement Design