## Slide 1: Routing in Vehicular Ad Hoc Networks: A Survey Fan Li, Yu Wang IEEE Vehicular Technology Magazine, June 2007
Speaker: Le Wang.

## Slide 2: Outline
1. Motivation and overview
2. Routing Protocols
  Ad Hoc Routing
  Position-Based Routing
  Cluster-Based Routing
  Broadcast Routing
  Geocast Routing
3. Mobility Model
4. Application
5. Summary

## Slide 3: Outline
1. Motivation and overview
2. Routing Protocols
  Ad Hoc Routing
  Position-Based Routing
  Cluster-Based Routing
  Broadcast Routing
  Geocast Routing
3. Mobility Model
4. Summary

## Slide 4: Motivation
Vehicular Ad Hoc Network (VANET):
  integrates ad hoc network, wireless LAN (WLAN) and cellular technology
  to achieve intelligent inter-vehicle communications
  to improve road traffic safety and efficiency
Distinguish from other kinds of ad hoc networks:
  Hybrid network architectures
  Node movement characteristics
  New application scenarios

## Slide 5: Major Application
Co-operative traffic monitor
Control of traffic flows
Real-time detour routes computation
Blind crossing prevention of collisions
Nearby information services
Internet connectivity to vehicular nodes while on the move, such as streaming video, email etc.

## Slide 6: Standards
The formal 802.11p standard is scheduled to be published in April, 2009 (this is a 2007 paper)
  IEEE Std 802.11p-2010, now incorporated in IEEE Std 802.11-2012
  Use 5.85 – 5.925 Ghz
  75 MHz of sprectrum
WAVE: Wireless Access in Vehicular Environments
  IEEE 1609 protocols suites
    IEEE 1609.2: Security
    IEEE 1609.3: Management Control
    IEEE 1609.4: Multichannel Operation

## Slide 7: Outline
1. Motivation and overview
2. Routing Protocols
  Ad Hoc Routing
  Position-Based Routing
  Cluster-Based Routing
  Broadcast Routing
  Geocast Routing
3. Mobility Model
4. Summary

## Slide 8: Routing Protocol for VANETs
Goal: to achieve minimal communication time with minimum consumption of network resources.
The performance of the existing routing protocols developed for MANETs (Mobile Ad Hoc Networks) suffer from poor performance due to:
  Fast vehicles movement
  Dynamic information exchange
  Relative high speed of mobile nodes

## Slide 9: VANET Architectures
(a) Vehicular to Infrastructure (V2I)
(b) Vehicular to Vehicular (V2V)
(c) Hybrid of V2I and V2V

## Slide 10: VANETs Characteristics
Highly dynamic topology
  High speed of movement between vehicles results in topology change.
  eg: Distance of two cars: 250m; Speed: 60 mph in opposite directions; Link will last only for 10 seconds.
Frequently disconnected network
  The connectivity of the VANETs could be changed frequently.
  One solution is to pre-deploy several relay nodes or AP along the road to keep the connectivity (V2I).
Sufficient energy and storage
  The nodes have ample energy and power
Geographical type of communication
  VANETs address geographical areas where packets need to be forwarded

## Slide 11: VANETs Characteristics
Mobility modelling and predication
  Mobility model and predication play an important role in VANETs protocol design.
Various communications environments
  In highway traffic scenarios, the environment is simple and straightforward;
  In city, direct communication is difficult because the streets are often separated by buildings, trees and other obstacles.
Hard delay constraints
  Delay has to be considered;
  eg: when brake event happens, the message should be transferred and arrived in a certain time to avoid car crash.
Interaction with on-board sensors
  On-board sensors is to provide information which can be used to form communication links and for routing purposes.

## Slide 12: Outline
1. Motivation and overview
2. Routing Protocols
  Ad Hoc Routing
  Position-Based Routing
  Cluster-Based Routing
  Broadcast Routing
  Geocast Routing
3. Mobility Model
4. Summary

## Slide 13: Ad Hoc Routing
AODV, PRAODV, PRAODVM
LAR

## Slide 14: Routing: Ad Hoc Routing
A.k.a. Topology-based routing
Similarities with MANET:
  not relying on fixed infrastructure; self-organization; self-management; low bandwidth and short radio transmission range.
  AODV: Ad-hoc On-demand Distance Vector
  DSR: Dynamic Source Routing
Differences from MANET:
  Highly dynamic topology
  AODV evaluation
  PRAODV
  PRAODVM
  ZOR and LAR

## Slide 15: Ad Hoc Routing
AODV (Ad-hoc On-demand Distance Vector) in VANET:
  Unable to quickly find, maintain and update long routes in a VANET.
  TCP is impossible because of the excessive lost of packets.
  Even when the scalability is not a problem with path lengths of only a few hops, AODV still breaks very quickly due to the dynamic nature.
PRAODV and PRAODVM:
  Prediction-based: predict the link lifetimes.
  PRAODV builds a new alternate route before the end of the predicted lifetime, while AODV does it when route failure happens.
  PRAODVM: select the max predicted lifetime instead of selecting the shortest path in AODV and PRAODV
  Results: Slightly improvement and heavily depend on the accuracy of the prediction method.

## Slide 16: Ad Hoc Routing
LAR (location-aided routing):
  AODV is modified to only forward the route requests within the Zone of Relevance (ZOR).
  ZOR can be rectangular or circular range determined by the application
  For example: ZOR covers the region behind the accident on the side of highway where the accident happens.

## Slide 17: Outline
1. Motivation and overview
2. Routing Protocols
  Ad Hoc Routing
  Position-Based Routing
  Cluster-Based Routing
  Broadcast Routing
  Geocast Routing
3. Mobility Model
4. Application
5. Summary

## Slide 18: Position-based Routing
GPSR
GSR
GPCR
A-STAR

## Slide 19: Routing: Position-Based Routing
Node movement in VANETs is usually restricted in bidirectional movements
Obtaining geographical location information from street maps, GPS is feasible.
More promising routing paradigm for VANETs.

## Slide 20: Position-Based Routing: GPSR
GPSR (Greedy Perimeter Stateless Routing)
  Greedy routing always forwards the packet to the node that is geographically closest to the destination.
  GPSR combines the greedy routing with face routing.
  Using face routing to get out of the local minimum where greedy routing failed.
  Suitable for free open space scenario with evenly distributed nodes.

## Slide 21: Position-Based Routing: GPSR
GPSR’s failure
a. The relative neighborhood graph (RNG) is a planar topology used by GPSR. A link uv will exist if the intersection of two circles centered at u and v does not contain any other nodes.
b. Link uv is removed by RNG since nodes a and b are inside the intersection of two circles centered at u and v. However, due to obstacles there is no direct link ua or ub. Thus the network is disconnected between u and v

## Slide 22: Position-Based Routing: GSR
GSR (Geographic Source Routing) assumes the aid of a street map in city environments.
Use Reactive Location Service (RLS) to get the global knowledge of the city topology.
Given the above information, the sender determines the junctions that have be traversed by the packet using the Dijkstra’s shortest path algorithm.
Forwarding between junctions is then done by position-based fashion.

## Slide 23: Position-Based Routing : GPCR
GPCR (Greedy Perimeter Coordinator Routing) does not use either source routing (DSR or GSR) or street map.
It utilizes the fact that the nodes at a junction follow a natural planar graph.
Thus a restricted greedy algorithm can be followed as long as the nodes are in a street.
Junctions are the only places where routing decisions are taken. Therefore packets should be forwarded on a junction rather than across the junction.
Restricted greedy routing
S wants to forward the packet to D.
For regular greedy forwarding, the packet will be forwarded to N1, then N3.
For greedy routing, the packet will be forwarded to C1, then N2,C2,D.

## Slide 24: Position-Based Routing: GPCR
GPCR also uses a repair strategy to get out of the local minimum, i.e., no neighbor exists which is closer to the destination than the intermediate node itself.
  1. decides, on each junction, which street the packet should follow next, by right hand rule.
  2. applies greedy routing, in between junctions, to reach the next junction.
S is the local minimum since no other nodes is closer to the destination D than itself.
The packet is routed to C1, which chooses the street that is the next one counter-clock wise from the street the packet has arrived on.
The packet is forwarded to C2 through N1.
Then C2 forward the packet to N2. Now, the distance from N2 to D is closer than at the beginning of the repair strategy at Node S.
GPCR switches back to modified greedy routing.
  GPCR has higher delivery rate than GPSR with large number of hops and slight increase in latency

## Slide 25: Position-Based Routing : A-STAR
Challenge:
  in a built-up city, vehicles are not evenly distributed;
  the constrained mobility by the road patterns;
  difficult signal reception due to radio obstacles such as high-rise buildings may lead VANETs unconnected.
A-STAR (Anchor-based Street and Traffic Aware Routing)
  Use street map to compute the sequence of junctions (anchors) through which a packet must pass to reach the destination.
  Unique:
    Use statistically rated maps by counting the number of city bus routes on each street to identify anchor paths.
    Or use Dynamically rated maps by monitoring the latest traffic condition to identify the best anchor paths.
    The packet is salvaged by traversing the new anchor path. To prevent other packets from traversing through the same void area, the street is marked as out of service temporarily.
Results: A-STAR shows the best performance compared to GSR and GPSR with traffic awareness.

## Slide 26: Outline
1. Motivation and overview
2. Routing Protocols
  Ad Hoc Routing
  Position-Based Routing
  Cluster-Based Routing
  Broadcast Routing
  Geocast Routing
3. Mobility Model
4. Application
5. Summary

## Slide 27: Cluster-based Routing
COIN
CORA_CBF

## Slide 28: Routing: Cluster-Based Routing
A virtual network infrastructure must be created through the clustering of nodes.
  Each cluster can have a cluster head, which is responsible for intra- and inter-cluster coordination in the network management function.
  Nodes inside a cluster communicate via direct links.
  Inter-cluster communication is performed via the cluster-heads.
Vehicles from multiple clusters in cluster-based routing

## Slide 29: Cluster-Based Routing: COIN
Current MANETs clustering techniques are unstable in VANET because the clusters are too short-lived to provide scalability with low communications overhead.
COIN (Clustering for Open IVC Networks)
  Cluster head election is based on vehicular dynamics and driver intentions, instead of ID or any classical clustering methods.
  Accommodate the oscillatory nature of inter-vehicle distances.
Results:
  COIN increases the average cluster lifetime by 192%;
  reduces number of cluster membership changes by 46%.

## Slide 30: Cluster-Based Routing: LORA_CBF
LORA_CBF Process:
  Each node can be the cluster head, gateway or cluster member.
  Each cluster has exactly one cluster-head.
  If a node is connected to more than one cluster, it is called a gateway.
  The cluster-head maintains information about its members and gateways.
  If the destination is unavailable, the source will send out the location request (LREQ) packets.
    It is similar to AODV, but only the cluster heads and gateways will disseminate the LREQ and LREP (Location Reply) messages.
Results: Network mobility and size affect the performance of AODV and DSR more significantly than LORA_CBF.

## Slide 31: Cluster-Based Routing
Cluster-based routing protocols can achieve good scalability for large networks
But a significant hurdle for them in fast-changing VANET systems is a delay and overhead involved in forming and maintaining these clusters.

## Slide 32: Outline
1. Motivation and overview
2. Routing Protocols
  Ad Hoc Routing
  Position-Based Routing
  Cluster-Based Routing
  Broadcast Routing
  Geocast Routing
3. Mobility Model
4. Application
5. Summary

## Slide 33: Broadcast Routing
Flooding
BROADCOMM
UMB
Others

## Slide 34: Routing: Broadcast Routing
Broadcast is frequently used in VANET
Flooding is the simplest routing way by using broadcast.
Advantages:
  Each node re-broadcasts messages to all of its neighbors except the one it got this message from.
  Flooding guarantees the message will eventually reach all nodes.
  Easy and suitable for small number of nodes.
Disadvantages:
  When network increases, the performance drops quickly and the bandwidth requested increase exponentially.
  Also cause contentions and collisions, broadcast storms.

## Slide 35: Broadcast Routing: BROADCOMM
BROADCOMM:
  The high way is divided into virtual cells, which moves as the vehicles move.
  The nodes are organized into two level of hierarchy:
    First level includes all the nodes in the same cell.
    Second level included cell reflectors, which are nodes located closed to the geographical center of the cell.
  Cell reflectors
    can act as a temporary base station (cluster head) to handle the emergency messages coming from neighbor cells.
    can also decides which message will be the first to be forwarded.
  Limitation: Only works with simple highway networks.

## Slide 36: Cluster Routing: UMB
UMB (Urban Multi-Hop Broadcast)
  Designed to overcome interference, packet collisions and designed to overcome interference, packet collisions and hidden nodes problems.
In UMB:
  The sender select the furthest node in the broadcast direction.
  At the intersection, repeaters are installed to forward the packets to all road segment.
Results:
  UMB has much higher success percentage at high packet loads and vehicle traffic densities than CSMA/CA.

## Slide 37: Cluster Routing: Others
Vector-based TRAcking Detection(V-TRADE), History-enhanced V-TRADE (HV-TRADE) are GPS based message broadcasting protocols.
Based on position and movement information, they classify the neighbors into different forwarding groups.
For each group, only a small subset of vehicles (border vehicles) is selected to rebroadcast the message.
Significant improvement of bandwidth utilization with slightly loss of reachability as fewer vehicles will rebroadcast themessage.

## Slide 38: Outline
1. Motivation and overview
2. Routing Protocols
  Ad Hoc Routing
  Position-Based Routing
  Cluster-Based Routing
  Broadcast Routing
  Geocast Routing
3. Mobility Model
4. Application
5. Summary

## Slide 39: Geocast Routing
Simple Geocast Routing
Cashed Geocast Routing
Abiding Geocast Routing

## Slide 40: Routing: Geocast Routing
Objective: to deliver the packet from a source node to all other nodes with a specified geographical region (Zone of Relevance, ZOR).
Different Communication Scenarios:
  Unicast routing
  Broadcast routing
  Geocast routing
Different Communication scenarios in VANETs

## Slide 41: Geocast Routing
Simple geocast scheme to avoid collision and reduce rebroadcast:
  When a node receives a packet, it does not rebroadcast it immediately but has to wait some time.
  The further the distance between this node and the sender, the shorter the waiting time is.
  Mainly nodes at the border of the reception area forward the packet quickly.
  When the waiting time is over, if it does not receive the same message form another node then it will rebroadcast this message.
By this way, broadcast storm can be avoided.

## Slide 42: Geocast Routing
Cashed Greedy Geocast:
  to deal with high velocities in VANET.
  Inside the ZOR, a small cache is added to the routing layer for holding packets that a node cannot forward instantly.
  When a new neighbor comes or old neighbors left, the cashed message can be possible forwarded to the newly discovered node.
  It chooses the closest node to destination instead of the node transmission range in the general greedy routing mode.
Results: can significantly improve the geocast delivery success ratio and significantly decrease network load and decreased end-to-end delivery delay.

## Slide 43: Geocast Routing
Abiding Geocast
  the packets need to delivered to all nodes that are sometime during the geocast lifetime inside the geocast destination region.
Solutions:
  a server is used to store the geocast messages
  an elected node inside the geocast region stores the messages
  each node stores all geocast packets destined for its location and keeps the neighbor information.

## Slide 44: Outline
1. Motivation and overview
2. Routing Protocols
  Ad Hoc Routing
  Position-Based Routing
  Cluster-Based Routing
  Broadcast Routing
  Geocast Routing
3. Mobility Model
4. Application
5. Summary

## Slide 45: Mobility Model
Realistic mobility models for VANETS need to be taken into account:
  Street conditions
  Urban conditions,
  Traffic speed
  Vehicle density
  Obstacles such as buildings

## Slide 46: Mobility Model: RWP
RWP (Random WayPoint Mobility) model
  Nodes randomly choose a destination and continue to move toward that destination at a uniform speed.
  When the destination is reached, another destination is chosen at random.
  Widely used in NS-2.
Saha, Johnson model
  Use TIGER (Topologically Integrated Geographic Encoding and Referencing) US road map, and convert the map into a graph.
  Assume each node starts at some random point on a road segment and moves toward a random destination following shortest path algorithm with a speed uniformly distributed within 5mph above and below the speed limit.
STRAW model
  Based on TIGER; Use a simple car-following model.
  Consider the interaction among cars, traffic congestion and traffic controls.
New trend of building mobility model using the realistic vehicular trace data

## Slide 47: Outline
1. Motivation and overview
2. Routing Protocols
  Ad Hoc Routing
  Position-Based Routing
  Cluster-Based Routing
  Broadcast Routing
  Geocast Routing
3. Mobility Model
4. Application
5. Summary

## Slide 48: Applications
Intelligent transportation applications
  On-board navigation;
  co-operative traffic monitoring;
  control of traffic flows;
  analysis of traffic congestion on the fly
  detour routes computation based on traffic conditions and destination.
Comfort applications
  allow the passenger to communicate either with other vehicles or with Internet hosts which improve passengers’ comfort.
    Download music, etc.

## Slide 49: Outline
1. Motivation and overview
2. Routing Protocols
  Ad Hoc Routing
  Position-Based Routing
  Cluster-Based Routing
  Broadcast Routing
  Geocast Routing
3. Mobility Model
4. Application
5. Summary

## Slide 50: Summary
Routing Protocols:
  Ad Hoc Routing:
  Position-Based Routing:
  Cluster-Based Routing:
  Broadcast Routing:
In general, position-based routing and geocasting are more promising because of the geographical constrains.
The performance of a routing protocol depends on mobility model, driving environment and vehicular density.
For certain VANETs application, we need to design specific routing protocol and mobility model to fulfill its requirements.

## Slide 51
Thank You!