## Slide 1: WAVE: A Tutorial
Roberto A. Uzcátegui
Guillermo Acosta-Marum
IEEE Communications Magazine ,May 2009
Presenter – Renato Iida

## Slide 2: Outline
Introduction
WAVE SYSTEM ARCHITECTURE
PHY and MAC Layers
Multichannel Operation
Networking Services
Resource Manager
Security Services
Concluding Remarks

## Slide 3: Introduction
Motivation and Standards

## Slide 4: Motivation
Intelligent Vehicle Highway Systems (IVHS) US,1991
  Increase safety
  Ameliorate congestion
  Reduce pollution
  Conserve fossil fuel
DOT advices with Intelligent Transportation Society of America (ITSA)
Created the intelligent transportation system [ITS] in 1996
  http://www.its.dot.gov/

## Slide 5: Standard of WAVE
2004, IEEE create the network layers based on ITSA
802.11p describe the PHY/MAC layer
  Based on 802.11a
  Uses 5.85-5.925 GHz
  75 Mhz of spectrum
1609 describe the other layer
  Divided in 4 parts
Wireless Access in Vehicular Environments (WAVE) is the solution using both standards

## Slide 6: WAVE SYSTEM ARCHITECTURE
Types and elements

## Slide 7: Types of Networks
Vehicle-to-Vehicle(V2V)
  Connect between two or Onboard units (OBUs)
Vehicle-to-Infrastructure(V2I)
  Connect between Onboard units (OBUs) and Roadside units (RSUs)
Traditional Internet Access

## Slide 8: Organization and Channels
Exchange information using control channel (CCH) and operates independently
WAVE basic service sets
  Small Network
  Similar to 802.11 service set
  Mix of OBU and RSU
  Service channels (SCHs)

## Slide 9: Examples
V2V
V2I
Internet

## Slide 10: PHY and MAC layers
802.11p

## Slide 11: Protocol Stack
802.11p

## Slide 12: Requirement
Longer ranges of operations (up to 1000m)
The high speed of vehicles
Extreme multipath environments
Multiple overlapping ad hoc with QoS
Special beacon frame

## Slide 13: Implementation
10 Mhz channels , half of the 802.11a
Control Channel and six service channel
Unique ad hoc mode
Random MAC
High accuracy of RSSI
16 QAM lower rate than 802.11a
Priority control
Power Control

## Slide 14: Multichannel Operation
Functional Description

## Slide 15: Protocol Stack
1609.4

## Slide 16: Elements of Multichannel Operation
Medium access using enhanced distributed channel access (EDCA) from 802.11e
Enhancement to IEEE 802.11 MAC
Manage channel coordination and to support MAC service data unit (MSDU)

## Slide 17: Services
Control channel data transfer
Service channel data transfer
Data transfer services
Control priority of data packet (WSMP or IP)

## Slide 18: Functional Description
Management Frames
  Wave announcement only in CCH
  Other IEEE management frames
Data Frames
  Wave short message can be on CCH and SCH
  IP data frames only on SCH
Channel Coordination using CCH
  For each WBSS

## Slide 19: Network Services

## Slide 20: Protocol Stack
1609.3

## Slide 21: Data Plane Services
IPv6
  TCP
  UDP
WSMP
  Capable of forward message
  Check integrity of the message

## Slide 22: Management-Plane Services
Application registration
WBSS management
Channel usage monitoring
IPv6 configuration
Received channel power indicator (RCPI) monitoring
Management information base (MIB) maintenance

## Slide 23: Application Registration
All applications need to register with WAVE management entity [WME]
Each application registers with a unique provider service identifier (PSID)
Three tables
  ProviderServiceInfo – info about applications that provide service
  UserServiceInfo -applications residing in the local unit
  ApplicationStatus – Info about the applications

## Slide 24: WBSS Management
Link establishment
Addition or removal of applications from dynamic WBSSs
Inclusion (provider side) and retrieval (user side) of security credentials
WBSS termination
Maintenance of the status of each application in the context of a particular WBSS

## Slide 25: Channel Usage Monitoring
Mandate that WME tracks SCH usage
The standard don’t define how but need to choose a less congested channel

## Slide 26: IPv6 Configuration
Controls the IPv6 connections

## Slide 27: RCPI Monitoring
Any application can query a remote device about the strength of the received signal
MLME that handle this request

## Slide 28: MIB Maintenance
The WME maintains a MIB that contains system-related and application-related information
Examples
  Network Information
  Addresses information
  Registration port
  And others

## Slide 29: Resource Manager

## Slide 30: Protocol Stack
1609.1

## Slide 31: Elements in the network
RM have a resource command processor (RCP)
RPC executes the command inside the RM on behalf of RMA

## Slide 32: Inside the OBU/RSU

## Slide 33: Security Services

## Slide 34: Protocol Stack
1609.2

## Slide 35: Symmetric Algorithms
How it can be used
  Encrypted-only
  Authenticated-only
  Both
Use Message Integrity Check (MIC)
Algorithm CBC AES-CCM

## Slide 36: Remaining Algorithms
Support Asymmetric Keys
User SHA1 for hash functions
Don’t guarantee anonymous header in the broadcast messages

## Slide 37: Hash Function
Use to create the MIC
Uses SHA-1

## Slide 38: Conclusions
Show how WAVE fit in a OSI model
Based on well-known solution of 802.11
Test of ITS were on going in California,Michigan, New York and Virginia

## Slide 39: Extra
https://www.udacity.com/course/applied-cryptography--cs387