## Slide 1: Distance Vector Routing
Computer Networks
A15

## Slide 2: DV Routing Outline
Internet Context
Network Layer Routing (**K&R slides)
Quick Routing Overview
Distance Vector Routing (my version)
  Adapted from Tanenbaum & Perlman Texts
Distance Vector Routing (K&R version)
Summary

## Slide 3: Internet Context
Computer Networks
Distance Vector Routing

## Slide 4: Metropolitan Area Network (MAN)
R
R
R
R
S
S
S
s
s
s
s
s
s
s
s
s
s
R
s
R
Backbone
To the Internet or wide area network
Organization Servers
Gateway
Departmental Server
Leon-Garcia & Widjaja:
Communication Networks

## Slide 5: Wide Area Network (WAN)
Interdomain level
Intradomain level
LAN level
Autonomous system
or domain
Border routers
Border routers
Internet service provider
Leon-Garcia & Widjaja:
Communication Networks

## Slide 6: Modern Internet Backbone
National service provider A
National service provider B
National service provider C
NAP
NAP
National Internet Service Providers
Network Access
Point
Leon-Garcia & Widjaja:
Communication Networks

## Slide 7: Network Access Point
Leon-Garcia & Widjaja:
Communication Networks
RA
RB
RC
Route server
NAP
LAN

## Slide 8: Network Layer Routing
Computer Networks
Distance Vector Routing

## Slide 9: Network Layer
transport segment from sending to receiving host.
on sending side, encapsulates segments into datagram packets.
on receiving side, delivers segments to transport layer.
network layer protocols in every host and router.
router examines header fields in all IP datagrams passing through it.
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
K & R

## Slide 10: Two Key Network Layer Functions
forwarding: move packets from router’s input to appropriate router output.
routing: determine route taken by packets from source to destination.
analogy:
routing: process of planning trip from source to destination
forwarding: process of getting through single interchange

## Slide 11: Interplay between Routing and Forwarding
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1

## Slide 12: Router Node
packet
node 15
17
Outgoing Link
Router Buffer
Server
packet
Incoming Link

## Slide 13: The Internet Network Layer
forwarding
table
Host, router network layer functions:
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport Layer: TCP, UDP
Data Link Layer
Physical Layer
Network
Layer

## Slide 14: Quick Routing Overview
Computer Networks
Distance Vector Routing

## Slide 15: Routing
Routing algorithm:: that part of the Network Layer responsible for deciding on which output line to transmit an incoming packet.
Remember: For virtual circuit subnets the routing decision is made ONLY at set up.
Algorithm properties:: correctness, simplicity, robustness, stability, fairness, optimality, and scalability.

## Slide 16: Routing Classification
Adaptive Routing
based on current measurements
of traffic and/or topology.
1. centralized
2. isolated
3. distributed
Non-Adaptive Routing
routing computed in advance and off-line
1. flooding
2. static routing using shortest path algorithms

## Slide 17: Internetwork Routing [Halsall]
Adaptive Routing
Centralized
Distributed
Intradomain routing
Interdomain routing
Distance Vector routing
Link State routing
[IGP]
[EGP]
[BGP,IDRP]
[OSPF,IS-IS,PNNI]
[RIP]
[RCC]
Interior
Gateway Protocols
Exterior
Gateway Protocols
Isolated

## Slide 18: Adaptive Routing Design
Design Issues:
How much overhead is incurred due to gathering the routing information and sending routing packets?
What is the time frame (i.e, the frequency) for sending routing packets in support of adaptive routing?
What is the complexity of the routing strategy?

## Slide 19: Adaptive Routing
Basic functions:
1. Measurement of pertinent network data.
2. Forwarding of information to where the routing computation will be done.
3. Compute the routing tables.
4. Convert the routing table information into a routing decision and then dispatch the data packet.

## Slide 20: Centralized Routing
RCC
A
Z
W
B

## Slide 21: Distance Vector Routing {Tanenbaum & Perlman version}
Computer Networks
Distance Vector Routing

## Slide 22: Distance Vector Routing
Historically known as the old ARPANET routing algorithm {or known as Bellman-Ford (BF) algorithm}.
BF Basic idea: each router maintains a Distance Vector table containing the distance between itself and ALL possible destination nodes.
Distances,based on a chosen metric, are computed using information from the neighbors’ distance vectors.
Distance Metric: usually hops or delay

## Slide 23: Distance Vector Routing
Information kept by DV router
each router has an ID
associated with each link connected to a router, there is a link cost (static or dynamic).
Distance Vector Table Initialization
Distance to itself = 0
Distance to ALL other routers = infinity number

## Slide 24: Distance Vector Algorithm [Perlman]
A router transmits its distance vector to each of its neighbors in a routing packet.
Each router receives and saves the most recently received distance vector from each of its neighbors.
A router recalculates its distance vector when:
  It receives a distance vector from a neighbor containing different information than before.
  It discovers that a link to a neighbor has gone down (i.e., a topology change).
The DV calculation is based on minimizing the cost to each destination.

## Slide 25: Distance Vector Example
Tanenbaum
Figure 5-9.(a) A subnet. (b) Input from A, I, H, K, and the new routing table for J.

## Slide 26: Distance Vector Routing {Kurose & Ross version}
Computer Networks
Distance Vector Routing

## Slide 27: Distance Vector Algorithm
Bellman-Ford Equation (dynamic programming)
Define
dx(y) := cost of least-cost path from x to y
Then
dx(y) = min {c(x,v) + dv (y)}
where min is taken over all neighbors v of x.
v

## Slide 28: Bellman-Ford Example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
The node that achieves minimum is next
hop in shortest path ➜ forwarding table.
Namely, packets from u destined for z are
forwarded out link between u and x.
B-F equation says:

## Slide 29: Distance Vector Algorithm (3)
Dx(y) = estimate of least cost from x to y
Node x knows cost to each neighbor v: c(x,v)
Node x maintains distance vector
Dx = [Dx(y): y є N ]
Node x also maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 30: Distance Vector Algorithm (4)
DV Basic idea:
From time-to-time, each node sends its own distance vector estimate to neighbors.
Asynchronous
When a node x receives a new DV estimate from any neighbor v, it saves v’s distance vector and it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Under minor, natural conditions, the estimate Dx(y) converges to the actual least cost dx(y).

## Slide 31: Distance Vector Algorithm (5)
Iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
Distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary.
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any destination has changed, notify neighbors
Each node:

## Slide 32
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
7
1
0
cost to
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
∞
∞

## Slide 33
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
7
1
0
cost to
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
∞
∞
∞

## Slide 34: Distance Vector: Link Cost Changes
Link cost changes:
node detects local link cost change.
updates routing info, recalculates distance vector.
if DV changes, it notifies neighbors .
At time t0, y detects the link-cost change, updates its DV, and informs its neighbors.
“good
news
travels
fast”
At time t1, z receives the update from y and updates its table.
It computes a new least cost to x and sends its neighbors its DV.
At time t2, y receives z’s update and updates its distance table.
y’s least costs do not change and hence y does not send any
message to z.
x
z
1
4
50
y
1

## Slide 35
Link cost changes:
good news travels fast
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm stabilizes: see text!
Poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?
x
z
1
4
50
y
60
Distance Vector: Link Cost Changes

## Slide 36: Distance Vector Summary
The Network Layer is responsible for routing and forwarding.
The routing process is used to build forwarding lookup tables.
Forwarding uses the lookup table to move an incoming packet to the correct outgoing link queue.
Routing algorithms use link cost metrics such as hops or delay.
Distance Vector (DV) is an intradomain adaptive routing algorithm that does not scale well.

## Slide 37: Distance Vector Summary
DV (originally the old ARPA algorithm) employs the Bellman-Ford shortest path algorithm and currently is used in the RIP, RIP-2, BGP, ISO IDRP and Novell IPX protocols.
DV routers:
keep distances to ALL intranet routers in a distance vector which is periodically updated and transmitted to each of its neighbors.
reacts to changes in its neighbors’ distance vectors and to topology changes (i.e., nodes and/or links coming up or going down).
In distance vector routing “bad news travels slowly and good news travels quickly”.