## Slide 1: Network Architecture and the OSI Reference Model
Computer Networks
B14

## Slide 2: Architecture Outline
The Internet and IP
Network Architecture
  Protocols and Layers
  Encapsulation
The OSI Reference Model
  The Seven OSI Layers
The TCP/IP Internet Stack
Layering Example
Tiered Internet Architecture

## Slide 3: The Internet versus an internet
An internet :: involves the interconnection of multiple networks into a single large networks. [LG&W]
The Internet :: refers to the successor to ARPANET. The modern Internet is multi-tiered and includes commercial participation.
IP (the Internet Protocol) :: provides connectionless transfer of packets across an internet.

## Slide 4: The Internet
Provides a name space to refer to machines connected to the Internet (e.g. chablis.cs.wpi.edu).
The name space is hierarchical, but it is only administrative and not used in network routing operations.
DNS (Domain Name Service) provides automatic translation of names to addresses.

## Slide 5: IP
Currently IP provides best-effort service.
  packets may be lost (i.e., IP is unreliable).
General IP design philosophy
  Keep internal operations simple by relegating complex functions to the edge of the subnet.
  IP can operate over any network.
  This design allows IP to scale!!!
  The end-to-end mechanisms are responsible for recovery of packet losses and congestion control.

## Slide 6: IPv4
Network ID
Host ID
4 bytes
Uses 32 bit hierarchical address space with location information embedded in the structure.
IPv4 address is usually expressed in dotted-decimal notation
e.g.,
128.100.11.56

## Slide 7: IPv6
IPv6 addresses are 128 bits long.
16 bytes of IPv6 address are represented as a group of hexadecimal digits, separated by colons. e.g.
[D&C]
2000:fdb8:0000:0000:0001:00ab:853c:39a1
Shorthand – leave out groups of zeros and leading zeros.
2000:fdb8:::1:ab:853c:39a1

## Slide 8: Layering and Abstraction
Layering accommodates incremental changes.
It is possible to have alternative abstractions at each layer.
Figure 1.9 Layered system with alternate abstractions available at a given layer.
P&D

## Slide 9: Applications and Layered Architectures
In the 1970’s vendor companies (IBM and DEC) developed proprietary networks with the common feature of grouping communication functions into related and manageable sets called layers.
network architecture :: a set of protocols that specify how every layer is to function and the defined interfaces between the layers. [LG&W]

## Slide 10: Protocols
Protocols are the building blocks of a network architecture.
Each protocol object has two different interfaces:
  service interface :: operations on this protocol
  peer-to-peer interface :: messages exchanged with peer

## Slide 11: Interfaces
Figure 1.10 Service interfaces and peer interfaces
P&D

## Slide 12: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
All communication activity in the Internet is governed by protocols.
Protocols define: the format, the order of msgs sent and received among network entities, and the actions taken on message transmission and receipt.
K & R

## Slide 13: What’s a protocol?
a human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
TCP connection
request
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
K & R

## Slide 14: International Standards Organization Open Systems Interconnect (OSI) Reference Model
Network Architecture

## Slide 15: ISO Architecture
Figure 1.13 The OSI seven-layer model
P&D

## Slide 16: The OSI Model
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Network
Layer
Electrical and/or Optical Signals
Application A
Application B
Data Link
Layer
Physical
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Communication Network
Figure 2.6
Copyright ©2000 The McGraw Hill Companies
Leon-Garcia
& Widjaja:
Communication
Networks

## Slide 17: OSI Layer Encapsulation
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application A
Application B
data
data
data
data
data
data
data
ah
ph
sh
th
nh
dh
bits
dt
Leon-Garcia
& Widjaja:
Communication
Networks

## Slide 18: Seven Layer OSI Model
Application Layer
Provides users access to the OSI environment and distributed information services.
Presentation Layer
Provides application processes independence from differences in data representations.
Session Layer
Provides the control structure for communicating between applications.
Establishes, manages and terminates session connections between cooperating applications.
Transport Layer
Provides reliable transparent transfer of data between end points.
Provides end-to-end flow control and error recovery.
Network Layer
Provides independence from the data transmission, routing/switching technologies used
to connect systems. Responsible for establishing, managing and terminating connections.
Data Link Layer
Provides for reliable transfer of information across the physical layer. Sends
and receives frames with the necessary synchronization, flow control and error control.
Physical Layer
Concerned with transmission of unstructured bit stream over a physical medium. Deals with
mechanical, electrical, functional and procedural characteristics to access the physical medium.

## Slide 19: ISO/OSI Reference Model
Presentation layer: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
Session layer: synchronization, check-pointing, recovery of data exchange
The TCP/IP Internet stack is “missing” these two layers!
  these services, if needed, must be implemented in an application.
  needed?
application
presentation
session
transport
network
data link
physical
K & R

## Slide 20: Advantages of Layering Design
An explicit structure for dealing with a complex system:
  allows identification and structures the relationship of complex system’s pieces.
  layered reference model for discussion.
Provides an abstraction for functional locality.
Simplifies the design process.

## Slide 21: Advantages of Layering Design
Modularity of layers eases maintenance and updating of system components:
  change in implementation of a layer’s service is transparent to rest of the system.
  Led to flexibility in modifying and developing network architectures.
  Accommodates incremental changes.

## Slide 22: TCP/IP Architectural Model
DCC 6th Ed., W. Stallings

## Slide 23: OSI versus TCP/IP
Figure 1-21. [old] The TCP/IP reference model.
Tanenbaum

## Slide 24: Internet Protocol Stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  PPP, Ethernet
application
transport
network
link
physical
physical: bits “on the wire” or in the air
K & R

## Slide 25
HTTP
SMTP
RTP
TCP
UDP
IP
Network
Interface 1
Network
Interface 3
Network
Interface 2
DNS
Leon-Garcia & Widjaja:
Communication Networks
TCP/IP Protocols

## Slide 26: Alternate View
Figure 1.15 Alternate view of the Internet architecture
P&D

## Slide 27: Layering Example
Client/server relationship
  Server process waits for incoming requests by listening to a port.
  Client process makes requests as required.
  Server process provides responses to these requests.
  The server process usually runs in the background as a daemon (e.g. httpd is the server daemon). for HTTP).

## Slide 28: HTTP Example
HTTP (HyperText Transfer Protocol) specifies rules by which the client and the server interact so as to retrieve a document.
The protocol assumes the client and the server can exchange messages directly.
The client software needs to set up a two-way connection prior to the HTTP request.

## Slide 29: HTTP Client/Server Interaction
HTTP
server
HTTP
client
Request
Response
Figure 2.1
Leon-Garcia & Widjaja: Communication Networks
Copyright ©2000 The McGraw Hill Companies
Leon-Garcia & Widjaja:
Communication Networks

## Slide 30
HTTP
server
HTTP
client
TCP
TCP
GET 80, #
#, 80 STATUS
Port 80
Ephemeral
Port #
HTTP/TCP Layering Interface
Leon-Garcia & Widjaja:
Communication Networks

## Slide 31
HTTP Request
TCP Header
Header contains source and destination port numbers
Header contains source and destination IP addresses; transport protocol type
IP Header
Header contains source and destination physical addresses; network protocol type
Frame Check Sequence
Ethernet Header
HTTP Encapsulation Example
Leon-Garcia & Widjaja:
Communication Networks

## Slide 32: Encapsulation Animation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
packet
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
K & R

## Slide 33: Internet Structure: Network of Networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., Verizon, Sprint, AT&T, Cable and Wireless), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
K & R

## Slide 34: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
….
…
…
…
POP: point-of-presence

## Slide 35: Internet Structure: Network of Networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other.
K & R

## Slide 36: Internet Structure: Network of Networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet
K & R

## Slide 37: Internet Structure: Network of Networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
K & R

## Slide 38: Internet Structure: Network of Networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP B
ISP A
ISP C
IXP
IXP
peering link
Internet exchange point
K & R

## Slide 39
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPS
ISP B
ISP A
ISP C
IXP
IXP
regional net
Internet Structure: Network of Networks
K & R

## Slide 40
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network
Internet Structure: Network of Networks
K & R

## Slide 41
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP
Internet Structure: Network of Networks
K & R

## Slide 42: Architecture Summary
The Internet and IP
Network Architecture
  Protocols and Layers
  Encapsulation
The OSI Reference Model
  The Seven OSI Layers
The TCP/IP Internet Stack
Layering Example
Tiered Internet Architecture