## Slide 1: Introduction
Computer Networks
B14

## Slide 2: Introduction Outline
Preliminary Definitions
Internet Components
Network Application Paradigms
Classifying Networks
  by transmission technology
  by size/scale
  by topology
Summary

## Slide 3: Definitions
computer network ::
[Tan] a collection of autonomous computers interconnected by a single technology.
[LG&W] communications network ::a set of equipment and facilities that provide a service.
[P&D] a network provides connectivity among a set of computers.
Initially, computers were directly connected over a physical medium such as copper, coaxial cable or optical fiber.
Selecting the set of computers involves security and scalability issues.

## Slide 4: Physical Connectivity
Figure 1.2 Direct links:
(a) point-to-point
(b) multiple access (MA)
P&D

## Slide 5: Other Forms of Connectivity
Indirect connectivity through a set of cooperating nodes.
Wireless connectivity:
  WiFi (IEEE802.11)
  Cellular (3G, 4G LTE)
  Bluetooth
  Zigbee (part of IEEE802.15.4)
  WiMAX

## Slide 6: Switched Network
Figure 1.3 Switched network
P&D

## Slide 7: An internet
Figure 1.4 Interconnection of Networks
P&D

## Slide 8: Definitions
In a distributed system::
the collection of independent computers appears to its users as a single coherent system.
Namely, the distinction between a computer network and a distribution system lies in the transparency in assigning tasks to computers.
Examples:
1. NFS is a distributed files system.
2. Computer networks provide host-to-host connectivity by assigning an address to each node.

## Slide 9: Application Communication
Figure 1.7 Processes communicating over
an abstract channel
P&D

## Slide 10: Internet Access and Flows
12
1
11
8
4
7
2
6
9
10
14
5
13
15
3
Host
B
Host
C
Host
L
Host
D
Host
E
Host
G
Host
J
Host
A
Host
H
Host
F
Host
M
16
17
W
T
X
Y
Z
nodes
AP
W1
W2
W3
W4

## Slide 11: The Internet: “nuts and bolts” view
billions of connected computing devices: hosts = end systems
  running network apps
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
router
PC
server
wireless
laptop
cellular
handheld
wired
links
access
points
communication links
  fiber, copper, radio, satellite
  transmission rate = capacity
routers*: forward packets (chunks of data)
* Also referred to as switches or gateways.
K & R

## Slide 12
K & R

## Slide 13: Student Perspectives
Application Programmer
  List the services that an application needs with QoS (Quality of Service) delivery targets.
Network Designer
  Design a cost-effective network with fair resource sharing.
Network Provider/Operator
  List the characteristics of a system that is easy to administer and manage. Concerns include: quick fault diagnosis, correct configurability, and easy growth.

## Slide 14: Networking Application Paradigms
Introduction

## Slide 15: Client-Server Applications
Figure 1.1 A network with two clients and one server.
Tanenbaum

## Slide 16: Client-Server Model
Figure 1-2. The client-server model involves requests and replies.
Tanenbaum

## Slide 17: Peer-to-Peer Applications
Figure 1.3 In a peer-to-peer system there are no fixed clients and servers.
Tanenbaum

## Slide 18: A Closer Look at Network Structure
network edge: applications and hosts
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
K & R

## Slide 19: The Network Edge
end systems (hosts)
  run application programs
  e.g. Web, email
  at “edge of network”
client/server
peer-peer
client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
peer-peer model
  minimal (or no) use of dedicated servers
  e.g. Skype, BitTorrent
K & R

## Slide 20: Wireless versus Mobile Applications
Wireless involves transmissions through the air (type depends on frequency).
  Residential access networks
    Residential access points
  Institutional access networks
    Institutional and corporate access points or mesh networks
  Public access networks
    e.g., Cities, towns, libraries and coffee shops
  Cellular networks
    2.5G, 3G and 4G LTE

## Slide 21: Wireless versus Mobile Applications
Mobile can refer to the Hosts.
  Laptops can be moveable and wired.
  Laptops can be moveable and wireless.
  Cell phones, smart phones and devices in vehicles are mobile and wireless.
Mobile Ad Hoc NETworks (MANETs)::
  wireless devices are both Hosts and subnet nodes (routers).
  The distinction is that MANET nodes may relay traffic intended for other nodes (multi-hop traffic).

## Slide 22: Network Classifications
Introduction

## Slide 23: Classifying by Transmission Technology
broadcast :: a single communications channel shared
by all machines (addresses) on the network.
Broadcast can be both a logical or a physical concept
(e.g. Media Access Control (MAC) sublayer ).
multicast :: communications to a specified group.
This requires a group address (e.g. – multimedia multicast).
unicast :: a communication involving a single sender and a single receiver.
point-to-point :: connections made via links between pairs of nodes.

## Slide 24: Classification by Size
Figure 1-6. Classification of interconnected processors by scale.
Tanenbaum
(PAN)
(LAN)
(MAN)
(WAN)

## Slide 25: Classification by Size
PANS {Personal Area Networks}
  Used for communication among computer devices, including smart phones and PDA’s in proximity to an individual's body. [Wikipedia].
  Reach up to meters.
  Includes ‘wearable’ devices and protocols such as Bluetooth, Zigbee and UWB (Ultra Wide Band) and BANs (Body Area Networks).
  IEEE 802.15 Working Group for Wireless PANs (WPANs).

## Slide 26: PANs
[Brunell University West London]

## Slide 27: Classification by Size
LANs {Local Area Networks}
  Wired LANs: typically physically broadcast at the MAC layer (e.g., Ethernet, Token Ring)
  Wireless LANs (WLANs)
  Wireless Sensor Networks (WSNs)
MANs {Metropolitan Area Networks}
  campus networks connecting LANs logically or physically.
  often have a backbone (e.g., FDDI, ATM or a mesh) to connect campus networks.

## Slide 28: Wired LANs
Ethernet bus
Ethernet hub
transceivers
     
Leon-Garcia & Widjaja:
Communication Networks

## Slide 29: Wireless LANs (WLANs)
Figure 1-35. (a) Wireless networking with a base station. (b) Ad hoc networking.
Tanenbaum

## Slide 30: Wireless Sensor Networks (WSNs)
WSNs can have mobile or fixed nodes but require a routing algorithm and normally have power concerns.
N. Chohan

## Slide 31: Metropolitan Area Networks (MANs)
Figure 1-8. A metropolitan area network based on cable TV.
Tanenbaum

## Slide 32
Metropolitan network A consists of access subnetworks: a, b, c, d.
National network consists of regional subnetworks: a, b, g.
Metropolitan network A is part of regional subnetwork .
A
A
Hierarchical Network Topology
1*
a
c
b
d
g
2
3
4


MANs within a Hierarchical Topology
Leon-Garcia & Widjaja:
Communication Networks

## Slide 33: Network Classification by Size
WANs {Wide Area Networks}
  also referred to as “point-to-point” networks.
  ARPANET  Internet
  usually hierarchical with a backbone.
  Enterprise Networks, Autonomous Systems (ASs)
  VPNs (Virtual Private Networks).

## Slide 34: ARPAnet circa 1972
A point-to-point network
UCLA
RAND
TINKER
USC
NBS
UCSB
HARV
SCD
BBN
STAN
AMES
AMES
McCLELLAN
UTAH
BOULDER
GWC
CASE
CARN
MITRE
ETAC
MIT
ILL
LINC
RADC
Leon-Garcia & Widjaja:
Communication Networks

## Slide 35: Wide Area Networks (WANs)
Figure 1-10.A stream of packets from sender to receiver.
Tanenbaum

## Slide 36: internet
A network of networks
G
G
G
G
G
net 1
net 2
net 3
net 4
net 5
G = gateway
G
Leon-Garcia & Widjaja:
Communication Networks

## Slide 37: Network Classification by Topology
flow of data
Repeater
Bus Topology
Bidirectional flow
Default is baseband
cabling

## Slide 38: Network Classification by Topology
Repeater
Repeater
Ring Topology
Note - A ring implies unidirectional flow.

## Slide 39: Network Classification by Topology
Headend
Tree Topology
Computer Networks Introduction

## Slide 40: Tree Topology
WSN end-to-end routing often employs a spanning tree for routing.
N. Chohan

## Slide 41: Network Classification by Topology
hub, switch
or repeater
Star Topology

## Slide 42: Network Classification by Topology
AP
W1
W2
W3
W4
Wireless Infrastructure
Star Topology

## Slide 43: Wireless Mesh Network

## Slide 44: Introduction Summary
Define: network, distributed system, subnet, host, node, flow, channel and link.
Paradigms: Client-Server, Peer-to-Peer, Wireless and Mobile.
Classifications and Acronyms:
  Broadcast, multicast, unicast
  PAN, LAN, MAN, WAN, WLAN, WSN
  The Internet versus an internet
  Hierarchical, bus, ring, tree, star and mesh topology