## Slide 1: Transport Layer
Computer Networks
Term B14

## Slide 2: Kurose’s Chapter 3 Outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 3: Transport Services and Protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 4: Internet Transport Layer Protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 5: Kurose’s Chapter 3 Outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing [Brief Look]
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 6: Connection-Oriented Demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
receiving host uses all four values to direct segment to appropriate socket.
Server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client.
  non-persistent HTTP will have different socket for each request.

## Slide 7: Connection-Oriented Demux
Client
IP:B
P1
client
IP: A
P1
P2
P4
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P5
P6
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B

## Slide 8: Connection-Oriented Demux
Client
IP:B
P1
client
IP: A
P1
P2
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B
P4
Threaded Web Server

## Slide 9: Kurose’s Chapter 3 Outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 10: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others.
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header
no congestion control: UDP can blast away as fast as desired.

## Slide 11: UDP Details
often used for streaming multimedia apps
  loss tolerant
  rate sensitive
other UDP uses
  DNS
  SNMP
reliable transfer over UDP: add reliability at application layer
  application-specific error recovery!
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header

## Slide 12: UDP Checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 13: Internet Checksum Example
Note
  When adding numbers, a carryout from the most significant bit needs to be added to the result
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit

## Slide 14: Kurose’s Chapter 3 Outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control
We will use Tanenbaum’s Data Link Layer Treatment to study this in place of K&R’s Transport Layer Discussion.

## Slide 15: Principles of Reliable Data Transfer
important in application, transport, and data link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 16: Principles of Reliable Data Transfer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
important in application, transport, and data link layers
top-10 list of important networking topics!

## Slide 17: Principles of Reliable Data Transfer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt).
important in application, transport, and data link layers
top-10 list of important networking topics!

## Slide 18: Reliable Data Transfer: Getting Started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 19: TCP Segment Structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)
{needed now
for error
detection}

## Slide 20: WARNING
Explanation of
Reliable Data Transport
will now be explained using the
Data Link Layer

## Slide 21: Reliable data transfer: getting started
We’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 22: Rdt1.0: Reliable Transfer over a Reliable Channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver read data from underlying channel
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)
sender
receiver

## Slide 23: Rdt2.0: Channel with Bit Errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK.
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors.
  sender retransmits pkt on receipt of NAK.
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) rcvr->sender

## Slide 24: rdt3.0: Channels with Errors and Loss
New assumption: underlying channel can also lose packets (data or ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help, but not enough
Approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but use of seq. #’s already handles this
  receiver must specify seq # of pkt being ACKed
requires countdown timer

## Slide 25: rdt3.0 Sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
udt_send(sndpkt)
start_timer
timeout
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L

## Slide 26: Pipelining and Sliding Windows
Lecture returns back to this point after Data Link Layer.
Diagrams from textbook!!

## Slide 27: Pipelined Protocols
Pipelining:: sender allows multiple, “in-flight”, yet-to-be-acknowledged packets.
  range of sequence numbers must be increased
  buffering at sender and/or receiver
Two generic forms of pipelined protocols: Go-Back-N and Selective Repeat

## Slide 28: Pipelining increases Utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
Increase utilization
by a factor of 3!

## Slide 29: Pipelining Protocols
Go-back-N: overview
sender: up to N unACKed pkts in pipeline
receiver: only sends cumulative ACKs
  doesn’t ACK pkt if there’s a gap
sender: has timer for oldest unACKed pkt
  if timer expires: retransmit all unACKed packets
Selective Repeat: overview
sender: up to N unACKed packets in pipeline
receiver: ACKs individual pkts
sender: maintains timer for each unACKed pkt
  if timer expires: retransmit only unACKed packet.

## Slide 30: Go-Back-N
Sender:
k-bit seq # in pkt header
“window” of up to N, consecutive unACKed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  may receive duplicate ACKs (see receiver)
timer for each in-flight pkt
timeout(n): retransmit pkt n and all higher seq # pkts in window.

## Slide 31: GBN: Sender Extended FSM
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum)
start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1
If (base == nextseqnum)
stop_timer
else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1
nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L

## Slide 32: GBN: Receiver Extended FSM
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order pkt:
  discard (don’t buffer) -> no receiver buffering!
  Re-ACK pkt with highest in-order seq #
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L

## Slide 33: Selective Repeat
receiver individually acknowledges all correctly received packets.
  buffers packets, as needed, for eventual in-order delivery to upper layer.
sender only resends packets for which ACK not received.
  sender timer for each unACKed packet
sender window
  N consecutive sequence #’s
  again limits sequence #s of sent, unACKed packets

## Slide 34: Selective Repeat Sender, Receiver Windows

## Slide 35: Selective Repeat
data from above :
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver

## Slide 36: Selective Repeat in Action
sliding
window

## Slide 37: Selective Repeat Dilemma
Example:
seq #’s: 0, 1, 2, 3
window size=3
receiver sees no difference in two scenarios!
incorrectly passes duplicate data as new in (a)
Q: What is the required relationship between seq # size and window size?

## Slide 38: Kurose’s Chapter 3 Outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 39: TCP Flow Control
receive side of TCP connection has a receive buffer:
speed-matching service: matching send rate to receiving application’s drain rate.
app process may be slow at reading from buffer.
sender won’t overflow
receiver’s buffer by
transmitting too much,
too fast
flow control
IP
datagrams
TCP data
(in buffer)
(currently)
unused buffer
space
application
process

## Slide 40: TCP Flow Control: how it works
(suppose TCP receiver discards out-of-order segments)
unused buffer space:
= rwnd
= RcvBuffer-[LastByteRcvd - LastByteRead]
receiver: advertises unused buffer space by including rwnd value in segment header
sender: limits # of unACKed bytes to rwnd
  guarantees receiver’s buffer doesn’t overflow.
rwnd known as the receiver’s advertised window.
IP
datagrams
TCP data
(in buffer)
(currently)
unused buffer
space
application
process
rwnd
RcvBuffer

## Slide 41: Kurose’s Chapter 3 Outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control