## Slide 1: TinyOS Introduction
Advanced Computer Networks

## Slide 2: TinyOS Outline
Introduction to the Architecture of TinyOS and nesC
Component Model
  Components, interfaces, wiring
  Commands and events; user and provider;
  Modules and configurations
  Wiring and callbacks
Concurrency Model
  Tasks and event handlers

## Slide 3: TinyOS Outline (cont)
Components
  Signatures and implementation blocks
Interfaces
  Commands and events
  Generic and bidirectional
Configurations
  Wiring
Generic components
Split-Phase Operation
  Read Interface; Send Interface

## Slide 4: TinyOS
TinyOS:: a general, embedded, lightweight operating system designed for low-power wireless sensors developed at UC Berkeley.
It provides a set of services and abstractions to make building sensor network applications easier.
It defines a concurrency execution model that emphasizes building applications from reusable services and components while avoiding unforeseen interactions.

## Slide 5: Application Architecture
Application
Timer
Sensors
Routing
Radio
Figure 1.3 Example application architecture. Application code uses a timer to act periodically, sensors to collect data, and a routing layer to deliver data to a sink.
Levis & Gay

## Slide 6: nesC
The TinyOS system, libraries and applications are written in nesC.
nesC, a dialect of C, has features to reduce RAM use and help prevent race conditions.
nesC applications are built from components with well-defined bidirectional interfaces linked together to form an executable.

## Slide 7: TinyOS
Provides three features to make writing systems and applications easier:
  a component model which defines how to write small, reusable pieces of code and compose them into larger abstractions.
  a concurrent execution model which defines how components interleave their computations and how interrupt and non-interrupt code interact.
  application program interfaces (APIs), services, component libraries and an overall component structure that simplifies writing new applications and services.

## Slide 8: A Operating System for Tiny Devices?
Main Concept
  HURRY UP AND SLEEP!!
    Sleep as often as possible to save power.
  provide framework for concurrency and modularity.
    Commands, events, tasks
  interleaving flows, events - never poll, never block.
Separation of construction and composition.
Programs are built out of components.
  Libraries and components are written in nesC.
  Applications are too -- just additional components composed with the OS components.
Each component is specified by an interface.
  Provides “hooks” for wiring components together.
Components are statically wired together based on their interfaces.
  Increases runtime efficiency.
Comnet TinyOS Tutorial

## Slide 9: Components and Interfaces
A component provides and uses interfaces.
  These interfaces are the only point of access to the component and are bidirectional.
An interface declares a set of functions called commands and events.
The interface’s user makes requests (calls commands) on the interface’s provider.
The provider makes callbacks (signals events) to the interface’s user.

## Slide 10: Programming in TinyOS
An interface defines a logically related set of commands and events.
Components implement the events they use and the commands they provide:
Commands and events themselves are like regular functions (they contain arbitrary C code).
Calling a command or signaling an event is just a function call.
Component | Commands | Events
Use | Can call | Must implement
Provide | Must implement | Can signal
Comnet TinyOS Tutorial

## Slide 11: PowerupC module
module PowerupC {
uses interface Boot;
uses interface Leds;
}
implementation {
event void Boot.booted ( ) {
call Leds.led0On ( );
}
}

## Slide 12: Components
There are two types of components in nesC: modules and configurations.
modules provide application code, implementing one or more interfaces.
module code declares variables and functions,calls functions and compiles to assembly code. module implementation sections consist of nesC code that looks like C.

## Slide 13: Configurations
Configurations are used to assemble other components together, connecting interfaces used by components to interfaces provided by other components. This is called wiring.
  Every nesC application is described by a top-level configuration that wires together the components inside.
nesC uses the filename extension “.nc” for all source files – interfaces, modules and configurations.

## Slide 14: PowerupAppC configuration
configuration PowerupAppC { }
implementation {
components MainC, LedsC, PowerupC;
MainC.Boot <- PowerupC.Boot;
PowerupC.Leds -> LedsC.Leds;
}

## Slide 15: Wiring and Callbacks
Wiring leaves the component connection decision to the programmer.
It also provides an efficient mechanism for supporting callbacks.
TinyOS provides a variable number of periodic or deadline timers.
Associated with each timer is a callback to a function that is executed each time the timer fires.

## Slide 16: Powerup with blinking LED [List 2.6]
module BlinkC {
uses interface Boot;
uses interface Timer;
uses interface Leds;
}
implementation {
event void Boot.booted ( ) {
call Timer.startPeriodic (250); /* start the 250ms timer when it boots */
}
event void Timer.fired ( ) {
call Leds.led0Toggle ( );
}
}

## Slide 17: Timer interface
interface Timer {
command void startPeriodic (uint32_t interval);
event void fired ( );
…
}
The connection between the startPeriodic command that starts the timer and the fired event which blinks the LED is implicitly specified by having the command and the event in the same interface.

## Slide 18: Powerup with blinking LED configuration [List 2.7]
configuration BlinkAppC { }
implementation {
components MainC, LedsC,
new TimerC ( ) as MyTimer, BlinkC;
BlinkC.Boot -> MainC.Boot;
BlinkC.Leds -> LedsC.Leds;
BlinkC.Timer -> MyTimer.Timer;
}
The Timer must be connected to a component that provides the actual timer. BlinkAppC wires BlinkC.Timer to a newly allocated MyTimer.

## Slide 19: Concurrency Model
TinyOS executes only one program consisting of selected system components and custom components needed for a single application.
TinyOS has two threads of execution: tasks and hardware event handlers.
Tasks are functions whose execution is deferred.
Once scheduled, tasks run to completion and do not preempt each other.

## Slide 20: Event Handlers
Hardware event handlers execute in response to hardware interrupts.
They run to completion, but event handlers may preempt execution of a task or other event handlers.
Commands and events executed as part of a hardware event handler must be declared with the async keyword.

## Slide 21: Components and Interfaces
All components have two code blocks.
The first block describes its signature and the second block describes its implementation.
A component signature declares whether it provides or uses an interface.

## Slide 22: Signature and Implementation Blocks [List 3.1]
module PowerupC { configuration LedsC {
// signature // signature
} }
implementation { implementation {
//implementation //implementation
} }
All components have two code blocks.

## Slide 23: MainC’s signature [List 3.8]
configuration MainC {
provides interface Boot;
uses interface Init as SoftwareInit;
}
MainC is a configuration that implements the boot sequence of a node and provides the Boot interface so that components, such as PowerupC, can be notified when a node has fully booted.

## Slide 24: MainC’s signature [List 3.8]
configuration MainC {
provides interface Boot;
uses interface Init as SoftwareInit;
}
The as keyword lets a signature provide an alternate name for an interface for clarity or to distinguish multiple instances of the same interface (see LedsP Module).

## Slide 25: Interfaces
Interfaces define a functional relationship between two or more components.
Like components, interfaces have a one-to-one mapping between names and files and exist in global namespace.
  e.g., the file Boot.nc contains the interface Boot.

## Slide 26: Init and Boot Interfaces [List 3.7]
An interface declaration has one or more functions in it.
The two kinds of functions are: commands and events.
interface Init { interface Boot {
command error_t init ( ); event void booted ( );
} }
Remember – While users call commands and providers can signal events, users implement events while providers implement commands.

## Slide 27: Interfaces
User
Provider
Commands
Events
Interface
Figure 3.2 Interfaces have commands and events.

## Slide 28: PowerupC module
module PowerupC {
uses interface Boot;
uses interface Leds;
}
implementation {
event void Boot.booted ( ) {
call Leds.led0On ( );
}
}
implementation of event
call command

## Slide 29: Event Implementation
As a user of the Boot interface which has a single event booted, PowerupC must provide an implementation.
{An event implementation is essentially an event handler.}
As the provider of the single event Boot.booted, MainC signals the event when a node has booted successfully.

## Slide 30: Command Call
As the user of the interface Leds, PowerupC calls the command Leds.led0On which is implemented by the provider Leds.
Boot, Init and Leds are type-free interfaces.

## Slide 31: Generic Interfaces [List 3.9]
Take one or more types as parameters.
Interface Queue <t> {
command bool empty ( );
command uint8_t size ( );
command uint8_t maxsize ( );
command t head ( );
command t dequeue ( );
command error_t enqueue (t newVal);
command t element (uint8_t idx):
}

## Slide 32: Generic Interfaces [List 3.10]
When a component declares a generic interface, it must specify its parameters.
Example:
Module QueueUserC {
uses interface Queue<uint32_t>;
}
Note – when connecting users to providers, interface types must match.

## Slide 33: Bidirectional Interfaces [List 3.12]
Declare both commands from a user to a provider as well as events from a provider to a user.
interface Notify <val_t> {
command error_t enable ( );
command error_t disable ( );
event void notify (val_t val);
}

## Slide 34: Notify Interface
The Notify interface has two commands. If notifications are enabled, the provider of the interface signals notify events.
Bidirectional interfaces enable components to register callbacks without needing function pointers.

## Slide 35: PowerupToggleC module [List 3.16]
Module PowerupToggleC {
uses interface Boot;
uses interface Leds;
}
implementation {
event void Boot.booted ( ) {
while (1) {
call Leds.led0Toggle ( );
call Leds.led1Toggle ( );
call Leds.led2Toggle ( );
}
} /* modules allocate state and implement executable logic */
}

## Slide 36: PowerupToggleAppC configuration [List 3.17]
configuration PowerupToggleAppC { }
implementation {
components MainC, Leds, PowerupToggleC;
PowerupToggleC.Boot -> MainC.Boot;
PowerupToggleC.Leds -> LedsC.Leds;
}
The configuration ‘wires’ components by mapping names in one component’s signatures to a set of names in another component’s signature.
interface user
interface provider

## Slide 37: Get interface [List 3.19]
interface Get <val_t> {
command val_t get ( );
}
All module variables are private.
The interface part of UserButtonC, demonstrates that interfaces are the only way to access to a variable.
configuration UserButtonC {
provides interface Get <button_state_t>;
}

## Slide 38: CountingGetC module [List 3.20]
module CountingGetC {
provides interface Get <uint8_t>;
}
implementation {
uint8_t count;
command uint8_t Get.get ( );
return count++
}
}
This component implements a Get interface that
returns the number of times Get has been called.

## Slide 39: Singleton Components
Components in TinyOS are singletons: only one exists by default.
Every configuration that names a component names the same component.
Example
If two components wire to LedsC, they are wiring to the same code that accesses the same variables.
A singleton component introduces a component name in global name space.

## Slide 40: Generic Components
Can have multiple instances unlike hardware singletons.
Generic components have the keyword generic before their signature:
generic configuration TimerMilliC ( ) {
provides interface Timer <TMilli>;
}
Configurations must instantiate using new :
…
components new TimerMilliC ( ) as Timer0;

## Slide 41: Split-phase Interfaces
Hardware is almost always split-phase rather than blocking.
In split-phase operations, the request that initiates an operation completes immediately.
Actual completion of the operation is signaled by a separate callback.
To save RAM space, TinyOS does not use multiple threads, but rather uses bidirectional split-phase software interfaces:
  A command starts the operation.
  An event signals the operation is complete.

## Slide 42: Read Interface
The Read interface is the basic TinyOS interface for split-phase data acquisition.
Most sensor drivers provide Read which is generic:
interface Read <val_t> {
command error_t read ( );
event void readDone (error_t, val_t val );
}
If the provider of Read returns SUCCESS to a call to Read, it will
signal readDone in the future, passing Read’s result parameter back as
the val parameter to the event handler.

## Slide 43: Send Interface
The basic TinyOS packet transmission interface, Send, is also a split-phase operation.
It is more complex because it requires passing a pointer for a packet to transmit.

## Slide 44: Split-Phase Send Interface [List 3.26]
interface Send {
command error_t send (message_t* msg, unint8_t len);
event void sendDone (message_t* msg, error_t error);
command error_t cancel (message_t* msg);
command void* getPayload (message_t* msg);
command uint8_t maxPayloadLength (message_t* msg);
}
passes a pointer for
message transmission

## Slide 45: Split-Phase Send Interface
A provider of Send defines the send and cancel functions and can signal the sendDone event.
A user of Send needs to define the sendDone event and can call the send and cancel commands.
When a send call returns SUCCESS, the msg parameter has been passed to the provider which tries to send the packet.
When the send completes, the provider signals sendDone, passing the pointer back to the user.

## Slide 46: Introduction to TinyOS Summary
Introduction to TinyOS and nesC
Component Model
  Components, interfaces, wiring
  Commands and events; user and provider;
  Modules and configurations
  Wiring and callbacks
Concurrency Model
  Tasks and event handlers

## Slide 47: Introduction to TinyOS Summary
Components
  Signatures and implementation blocks
Interfaces
  Commands and events
  Generic and bidirectional (as)
Configurations
  Wiring
Generic components (new)
Split-Phase Operation
  Read and Send