## Slide 1: Physical Layer (Part 2) Data Encoding Techniques
Advanced Computer Networks

## Slide 2: Data Encoding Techniques
Digital Data, Analog Signals [modem]
Digital Data, Digital Signals [wired LAN]
Analog Data, Digital Signals [codec]
  Frequency Division Multiplexing (FDM)
  Wave Division Multiplexing (WDM) [fiber]
  Time Division Multiplexing (TDM)
  Pulse Code Modulation (PCM) [T1]
  Delta Modulation

## Slide 3: Analog and Digital Transmissions
Figure 2-23.The use of both analog and digital transmissions for a computer-to-computer call. Conversion is done by the modems and codecs.
Tanenbaum

## Slide 4: Digital Data, Analog Signals [Example – modem]
Basis for analog signaling constant-frequency is a continuous, signal known as the carrier frequency.
Digital data is encoded by modulating one of the three characteristics of the carrier: amplitude, frequency, or phase or some combination of these.

## Slide 5: Signal Modulation
A binary signal
Frequency
modulation
Amplitude
modulation
Phase modulation
Figure 2-24.
Tanenbaum

## Slide 6: Modems
All advanced modems use a combination of modulation techniques to transmit multiple bits per baud.
Multiple amplitude and multiple phase shifts are combined to transmit several bits per symbol.
QPSK (Quadrature Phase Shift Keying) uses multiple phase shifts per symbol.
Modems actually use Quadrature Amplitude Modulation (QAM).
These concepts are explained using constellation points where a point determines a specific amplitude and phase.

## Slide 7: Constellation Diagrams
(a) QPSK. (b) QAM-16. (c) QAM-64.
Figure 2-25.
V = 64
v = log2 V = 6
Tanenbaum

## Slide 8: Digital Data, Digital Signals [the technique is used in a number of LANs]
Digital signal – is a sequence of discrete, discontinuous voltage pulses.
Bit duration :: the time it takes for the transmitter to emit the bit.
Issues
  Bit timing (sender/receiver clock drift)
  Recovery from signal
  Noise immunity

## Slide 9: NRZ ( Non-Return-to-Zero) Codes
Uses two different voltage levels (one positive and one negative) as the signal elements for the two binary digits.
NRZ-L ( Non-Return-to-Zero-Level)
The voltage is constant during the bit interval.
NRZ-L is used for short distances between a terminal and modem or terminal and computer.
1  negative voltage
0  positive voltage

## Slide 10: NRZ ( Non-Return-to-Zero) Codes
NRZ-I ( Non-Return-to-Zero-Invert on ones)
The voltage is constant during the bit interval.
NRZI is a differential encoding scheme (i.e., the signal is decoded by comparing the polarity of adjacent signal elements.)
1  existence of a signal transition at the beginning of the bit time
(either a low-to-high or a high-to-low transition)
0  no signal transition at the beginning of the bit time

## Slide 11: Bi–Phase Codes
Bi-phase codes – require at least one transition per bit time and may have as many as two transitions.
 the maximum modulation rate is twice that of NRZ
 greater transmission bandwidth is required.
Advantages:
Synchronization – with a predictable transition per bit time the receiver can “synch” on the transition [self-clocking].
No d.c. component
Error detection – the absence of an expected transition can be used to detect errors.

## Slide 12: Manchester Encoding
There is always a mid-bit transition {which is used as a clocking mechanism}.
The direction of the mid-bit transition represents the digital data.
Consequently, there may be a second transition at the beginning of the bit interval.
Used in 802.3 baseband coaxial cable and CSMA/CD twisted pair.
1  low-to-high transition
0  high-to-low transition
Some
textbooks
disagree
on this
definition!!

## Slide 13: Differential Manchester Encoding
mid-bit transition is ONLY for clocking.
Differential Manchester is both differential and bi-phase.
Note – the coding convention for Differential Manchester is the opposite convention from NRZI.
Used in 802.5 (token ring) with twisted pair.
* Modulation rate for Manchester and Differential Manchester is twice the data rate  inefficient encoding for long-distance applications.
1  absence of transition at the beginning of the bit interval
0  presence of transition at the beginning of the bit interval

## Slide 14: Bi-Polar Encoding
Has the same issues as NRZI for a long string of 0’s.
A systemic problem with polar is the polarity can be backwards.
1  alternating +1/2 , -1/2 voltage
0  0 voltage

## Slide 15: Digital Encoding Techniques
1
0
1
0
1
1
0
0
1
Unipolar
NRZ
NRZ-Inverted
(Differential
Encoding)
Bipolar
Encoding
Differential
Manchester
Encoding
Polar NRZ
Manchester
Encoding
Leon-Garcia & Widjaja:
Communication Networks

## Slide 16: Analog Data, Digital Signals [Example – PCM (Pulse Code Modulation)]
The most common technique for using digital signals to encode analog data is PCM.
Example: To transfer analog voice signals off a local loop to digital end office within the phone system, one uses a codec.
Because voice data limited to frequencies below 4000 HZ, a codec makes 8000 samples/sec. (i.e., 125 microsec/sample).

## Slide 17: Multiplexing
MUX
MUX
(a)
(b)
Trunk
group
A
A
A
A
B
B
B
B
C
C
C
C
Leon-Garcia & Widjaja:
Communication Networks
Multiplexing {general definition} ::
Sharing a resource over time.

## Slide 18: Frequency Division Multiplexing (FDM) vs Time Division Multiplexing (TDM)
FDM
frequency
time
TDM
frequency
time
4 users
Example:
K & R
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 19: Frequency Division Multiplexing
A
C
B
f
C
f
B
f
A
f
H
H
H
0
0
0
(a) Individual signals occupy H Hz
(b) Combined signal fits into channel bandwidth
Leon-Garcia & Widjaja:
Communication Networks

## Slide 20: Frequency Division Multiplexing
Figure 2-31. (a) The original bandwidths. (b) The bandwidths raised in frequency. (c) The multiplexed channel.
Tanenbaum

## Slide 21: Wavelength Division Multiplexing
Wavelength division multiplexing.
Figure 2-32.
Tanenbaum

## Slide 22: Time Division Multiplexing

## Slide 23: Concentrator [Statistical Multiplexing]

## Slide 24: T1 System
MUX
MUX
24
b
1
2
. . .
b
23
22
frame
24
A
B
C
A
B
C
Leon-Garcia & Widjaja:
Communication Networks

## Slide 25: T1 - TDM Link
The T1 carrier (1.544 Mbps).
Figure 2-33.T1 Carrier (1.544Mbps)
Tanenbaum

## Slide 26: Pulse Code Modulation (PCM)
T1 example for voice-grade input lines:
implies both codex conversion of analog to digital signals (PCM) and TDM.

## Slide 27: Pulse Code Modulation Stages
DCC 8th Ed.
Stallings

## Slide 28: Pulse Code Modulation (PCM)
Analog signal is sampled.
Converted to discrete-time continuous-amplitude signal (Pulse Amplitude Modulation)
Pulses are quantized and assigned a digital value.
  A 7-bit sample allows 128 quantizing levels.

## Slide 29: Pulse Code Modulation (PCM)
PCM uses non-linear encoding, i.e., amplitude spacing of levels is non-linear.
  There is a greater number of quantizing steps for low amplitude.
  This reduces overall signal distortion.
This introduces quantizing error (or noise).
PCM pulses are then encoded into a digital bit stream.
8000 samples/sec x 7 bits/sample = 56 Kbps for a single voice channel.

## Slide 30: PCM Stages
DCC 8th Ed.
Stallings

## Slide 31: PCM Nonlinear Quantization
DCC 8th Ed.
Stallings

## Slide 32: Delta Modulation (DM)
The basic idea in delta modulation is to approximate the derivative of analog signal rather than its amplitude.
The analog data is approximated by a staircase function that moves up or down by one quantization level at each sampling time.  output of DM is a single bit.
PCM preferred because of better SNR characteristics.

## Slide 33: Delta Modulation
DCC 8th Ed.
Stallings

## Slide 34: Data Encoding Summary
Digital Data, Analog Signals [modem]
  Three forms of modulation (amplitude, frequency and phase) used in combination to increase the data rate.
  Constellation diagrams (QPSK and QAM)
Digital Data, Digital Signals [wired LANs]
  Tradeoffs between self clocking and required frequency.
  Biphase, differential, NRZL, NRZI, Manchester, differential Manchester, bipolar.

## Slide 35: Data Encoding Summary
Analog Data, Digital Signals [codec]
  Multiplexing Detour:
    Frequency Division Multiplexing (FDM)
    Wave Division Multiplexing (WDM) [fiber]
    Time Division Multiplexing (TDM)
    Statistical TDM (Concentrator)
Codex functionality:
  Pulse Code Modulation (PCM)
  T1 line {classic voice-grade TDM}
  PCM Stages (PAM, quantizier, encoder)
  Delta Modulation