## Slide 1: Ethernet
Advanced
Computer Networks

## Slide 2: Ethernet Outline
Ethernet
  Binary Exponential Backoff
Ethernet versus IEEE 802.3
Ethernet Evolution
  10BASE5, 1OBASE2, 1BASE5, 10BASE-T
Switched Ethernet
Switching Hub

## Slide 3: Ethernet [DEC, Intel, Xerox]
1-persistent, CSMA-CD with Binary Exponential Backoff.
Manchester encoding.

## Slide 4: Ethernet [operational in 1974]
Initially 3 Mbps baseband coaxial cable (thick Ethernet).
Operational Description
Ethernet stations sense the channel (CS).
When the channel is free, the station transmits a frame (1-persistent).
The stations monitor the ‘ether’ during the transmission (MA).
If a collision is detected by any station (CD), the transmission is terminated immediately and a jam signal is sent.
Upon collision, transmitting stations backoff using a local counter and then retransmit (BEB).

## Slide 5: Worst Case Collision Scenario
A transmits at t = 0
Distance d meters
A
B
B transmits before t = tprop and detects collision shortly
thereafter
A
B
A
B
A detects
collision at
t = 2 tprop
tprop = d /  seconds
Leon-Garcia & Widjaja:
Communication Networks

## Slide 6: Ethernet
frame
contention
frame
A frame seizes the channel after 2 tprop
On 1 km Ethernet, tprop is approximately 5 microseconds.
Contention interval = 2 tprop
Interframe gap = 9.6 microseconds
Modeled as slotted scheme with
slot = 2 tprop

## Slide 7: Binary Exponental Backoff (BEB)
Upon a collision, the sending stations increment a local counter K. The backoff interval is randomly selected using a uniform distribution over the
L = 2K slots.
K is initially set to 0.
Thus upon collision, the value of L is doubled locally for each sending station.

## Slide 8: Binary Exponental Backoff (BEB)
Slotted ALOHA has been shown to be unstable when
p > 1/n
Since Ethernet permits up to 1024 stations, backoff continues until K = 10, L = 210, and p = 1/210
Normally K is incremented up to 10, but BEB is set for 16 retries. After 16 retries, MAC gives up trying to send the frame.
{The IP packet is now considered lost}.

## Slide 9
Preamble
SD
Destination
Address
Source
Address
Length
Information
Pad
FCS
7
1
2 or 6
2 or 6
2
4
64 to 1518 bytes
Synch
Start
frame
0
Single address
1
Group address
Destination address is either single address
or group address (broadcast = 111...111)
Addresses are defined on local or universal basis
246 possible global addresses
0
Local address
1
Global address
802.3 MAC Frame
IEEE 802.3 Frame Format
Leon-Garcia & Widjaja:
Communication Networks

## Slide 10
Preamble
SD
Destination
Address
Source
Address
Type
Information
Pad
FCS
7
1
2 or 6
2 or 6
2
4
64 to 1518 bytes
Synch
Start
frame
Ethernet Frame
Ethernet Frame Format
Leon-Garcia & Widjaja:
Communication Networks

## Slide 11
AA AA 03
Information
MAC Header
FCS
802.3 Frame
LLC PDU
SNAP Header
Type
ORG
SNAP PDU
3
2
1
1
1
Leon-Garcia & Widjaja:
Communication Networks
Ethernet Encapsulation

## Slide 13: Ethernet Evolution
10BASE5 {1983}
10 Mbps
500 meter segment length
Signal-regenerating repeaters
Thick Coax
  Advantages: Low attenuation, excellent noise immunity, superior mechanical strength
  Disadvantages: Bulky, difficult to pull, transceiver boxes too expensive
Wiring represented a significant part of total installed cost.

## Slide 14
MAU device is physically hooked on main cable.
50 meter AUI cable from MAU to station.
10BASE5

## Slide 15: Ethernet Evolution
10BASE2 ‘Cheapernet’ {1985}
10 Mbps
185 meter segment length
Signal-regenerating repeaters
Transceiver was integrated onto the adapter
Thin Coax (coax thinner and lighter)
  Advantages: Easier to install, reduced hardware cost, BNC connectors widely deployed  lower installation costs.
  Disadvantages: Attenuation not as good, could not support as many stations due to signal reflection caused by BNC Tee Connector.

## Slide 16
10Base2 Cheapernet

## Slide 17
(a)
(b)
transceivers
Thick Ethernet Cable
Thin Ethernet Cable
Leon-Garcia & Widjaja:
Communication Networks

## Slide 18: Ethernet Evolution
1BASE5 StarLAN {1987}
1 Mbps
250 meter segment length
Signal-regenerating repeaters
Transceiver integrated onto the adapter
Hub-and-Spoke topology (star topology)
Two pairs of unshielded twisted pair
  Advantages: Since four or more UTP are ubiquitous in buildings, it is easier to use installed wiring in the walls. Telephone wiring is hierarchical  can use wiring closets.

## Slide 19: Ethernet Evolution
10BASE-T {1990} **Most popular
10 Mbps
100 meter segment length
Signal-regenerating repeaters
Transceiver integrated onto adapter
Two pairs of UTP
Hub-and-spoke topology {Hub in the closet}
  Advantages: could be done without pulling new wires. Each hub amplifies and restores incoming signal.

## Slide 20: The Hub Concept
Separate transmit and receive pair of wires.
The repeater in the hub retransmits the signal received from any input pair onto ALL output pairs.
Essentially the hub emulates a broadcast channel with collisions detected by receiving nodes.

## Slide 21
10Base-T Hub Concept

## Slide 22
(a)
(b)
     
   
High-Speed Backplane or Interconnection fabric
Single collision domain
hub
switch
Leon-Garcia & Widjaja:
Communication Networks
Twisted Pair Ethernet

## Slide 23: 10Mbps Specification (Ethernet)
Notes: The IEEE 802.3 committee has defined a number of alternative physical configurations. This is both good and bad. On the good side, the standard has been responsive to evolving technology. On the bad side, the customer, not to mention the potential vendor, is faced with a bewildering array of options. However, the committee has been at pains to ensure that the various options can be easily integrated into a configuration that satisfies a variety of needs. Thus, the user that has a complex set of requirements may find the flexibility and variety of the 802.3 standard to be an asset.
To distinguish the various implementations that are available, the committee has developed a concise notation:
<data rate in Mbps> <signaling method><maximum segment length in hundreds of meters>
The defined alternatives for 10-Mbps are:
10BASE5: Specifies the use of 50-ohm coaxial cable and Manchester digital signaling. The maximum length of a cable segment is set at 500 meters. The length of the network can be extended by the use of repeaters. A repeater is transparent to the MAC level; as it does no buffering, it does not isolate one segment from another. So, for example, if two stations on different segments attempt to transmit at the same time, their transmissions will collide. To avoid looping, only one path of segments and repeaters is allowed between any two stations. The standard allows a maximum of four repeaters in the path between any two stations, extending the effective length of the medium to 2.5 kilometers.
10BASE2: Similar to 10BASE5 but uses a thinner cable, which supports fewer taps over a shorter distance than the 10BASE5 cable. This is a lower-cost alternative to 10BASE5.
10BASE-T: Uses unshielded twisted pair in a star-shaped topology. Because of the high data rate and the poor transmission qualities of unshielded twisted pair, the length of a link is limited to 100 meters. As an alternative, an optical fiber link may be used. In this case, the maximum length is 500 m.
10BASE-F: Contains three specifications: a passive-star topology for interconnecting stations and repeaters with up to 1 km per segment; a point-to-point link that can be used to connect stations or repeaters at up to 2 km; a point-to-point link that can be used to connect repeaters at up to 2 km.

## Slide 24: Switched Ethernet
Basic idea: improve on the Hub concept
The switch learns destination locations by remembering the ports of the associated source address in a table.
The switch may not have to broadcast to all output ports. It may be able to send the frame only to the destination port.
 a big performance advantage over a hub, if more than one frame transfer can go through the switch concurrently.

## Slide 26: Switches
link-layer devices: smarter than hubs, take active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment.
transparent
  hosts are unaware of presence of switches.
plug-and-play, self-learning
  switches do not need to be configured.

## Slide 27: Switches allows multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ simultaneously, without collisions
  not possible with dumb hub!!
A
A’
B
B’
C
C’
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 28: Switch Table
Q: how does switch know that A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?
A
A’
B
B’
C
C’
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 29: Switch: Self-Learning
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 30: Switch: Frame Filtering/Forwarding
When frame received:
1. record link associated with sending host
2. index switch table using MAC dest address
3. if entry found for destination then {
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 31: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination unknown:
flood
A’ A
destination A location known:
A’
4
60
selective send

## Slide 32: Interconnecting Switches
switches can be connected together
A
B
Q: sending from A to G - how does S1 know to forward frame destined to F via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 33: Self-learning Multi-switch
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
1
2

## Slide 34: Switched Ethernet
The advantage comes when the switched Ethernet backplane is able to repeat more than one frame in parallel (a separate backplane bus line for each node).
  The frame is relayed onto the required output port via the port’s own backplane bus line.
Under this scheme collisions are still possible when two concurrently arriving frames are destined for the same station.
Note – each parallel transmission can take place at 10 Mbps!!

## Slide 35: Switched Ethernet
Figure 4-20.A simple example of switched Ethernet.
Tanenbaum’s discussion
considers a more powerful switch
that reduces collisions even
further!!
Tanenbaum

## Slide 36: Switched Ethernet Hub
Since servers are often shared by multiple nodes, one can employ a switching hub with a port which operates at a higher rate than the other ports.
This requires extra buffering inside the hub to handle speed mismatches.
Can be further enhanced by higher rated port full-duplex.

## Slide 37: Switching Hierarchy
Ethernet Switch
Ethernet Switch
Server
100 Mbps links
10 Mbps links
Fast Ethernet
Switch
Leon-Garcia & Widjaja:
Communication Networks

## Slide 38: Ethernet Summary
Ethernet
  Binary Exponential Backoff
Ethernet versus IEEE 802.3
Ethernet Evolution
  10BASE5, 1OBASE2, 1BASE5, 10BASE-T
Switched Ethernet
Switching Hub