## Slide 1: Physical Layer (Part 1)
Advanced Computer Networks

## Slide 2: Physical Layer Outline (Part 1)
Definitions
Nyquist Theorem - noiseless
Shannon’s Result – with noise
Analog versus Digital
Amplifier versus Repeater
Advantages/Disadvantages of Analog vs Digital Transmissions

## Slide 3: A Very Simple Abstraction
Receiver
Communication channel
Transmitter
Leon-Garcia & Widjaja:
Communication Networks
The Physical Layer is concerned with physical considerations and limitations.

## Slide 4: Physical Layer Definitions
The time required to transmit a character depends on both the encoding method and the signaling speed (i.e., the modulation rate - the number of times/sec the signal changes its voltage).
baud (D) - the number of changes per second.
bandwidth (H) - the range of frequencies that is passed by a channel. The transmitted signal is constrained by the transmitter and the nature of the transmission medium in cycles/sec (hertz).
channel capacity (C) – the rate at which data can be transmitted over a given channel under given conditions.{This is also referred to as data rate (R).}

## Slide 5: Modulation Rate
DCC 6th Ed.
Stallings
modulation rate
is doubled

## Slide 6: Nyquist Theorem {assume a noiseless channel}
If an arbitrary signal is run through a low-pass filter of bandwidth H, the filtered signal can be completely reconstructed by making 2H samples/sec.
This implies for a signal of V discrete levels,
Note – a higher sampling rate is pointless because higher frequency signals have been filtered out.
Max. data rate :: C = 2H log 2 (V) bits/sec.

## Slide 7: Physical Transmission Issues
f
0
H
A(f)
(b) Maximum pulse transmission rate is 2H pulses/second
0
H
f
A(f)
1
Channel
t
t
Leon-Garcia & Widjaja:
Communication Networks

## Slide 8: Voice-grade Phone Line
Example 1. {sampling rate}
H = 4000 Hz
2H = 8000 samples/sec.
 sample every 125 microseconds!!
Example 2. {noiseless capacity}
D = 2400 baud {note D = 2H}
V = each pulse encodes 16 levels
C = 2H log 2 (V) = D x log 2 (V)
= 2400 x 4 = 9600 bps.

## Slide 9: Signal Constellations
Ak
Bk
4 “levels”/ pulse
2 bits / pulse
2D bits per second
Ak
Bk
16 “levels”/ pulse
4 bits / pulse
4D bits per second
Leon-Garcia & Widjaja:
Communication Networks

## Slide 10: Constellation Diagrams
(a) QPSK. (b) QAM-16. (c) QAM-64.
Figure 2-25.
Tanenbaum

## Slide 11: Signal to Noise Ratio (SNR)
signal
noise
signal + noise
signal
noise
signal + noise
High
SNR
Low
SNR
SNR =
Average Signal Power
Average Noise Power
SNR (dB) = 10 log10 SNR
t
t
t
t
t
t
Leon-Garcia & Widjaja:
Communication Networks

## Slide 12: Shannon’s Channel Capacity Result {assuming only thermal noise}
For a noisy channel of bandwidth H Hz. and a signal-to-noise ratio SNR, the max. data rate::
Regardless of the number of signal levels used and the frequency of the sampling.
C = H log 2 (1 + SNR)

## Slide 13: Shannon Example – Noisy Channel
Telephone channel (3400 Hz) at 40 dB SNR
C = H log 2 (1+SNR) b/s
SNR (dB) = 40 dB
40 dB =10 log 10 (SNR)
4 = log 10 (SNR)
SNR =10,000
C = 3400 log 2 (10001) = 44.8 kbps
Leon-Garcia & Widjaja:
Communication Networks

## Slide 14: Data Communications Concepts
Analog and Digital correspond roughly to continuous and discrete , respectively.
These two terms can be used in three contexts: data, signals, transmissions.
1. data:: entities that convey meaning.
analog – voice and video are continuously
varying patterns of intensity.
digital - take on discrete values (e.g., integers, ASCII text).
Data are propagated from one point to another by means of electrical signals.
DCC 6th Ed.
Stallings

## Slide 15: Analog vs Digital (three contexts)
DCC 6th Ed.
Stallings

## Slide 16: Analog and Digital Signaling
signals:: electric or electromagnetic encoding of data.
2. signaling :: is the act of propagating the signal along a suitable medium.
  Analog signal – a continuously varying electromagnetic wave that may be propagated over a variety of medium depending on the spectrum (e.g., wire, twisted pair, coaxial cable, fiber optic cable and atmosphere or space propagation).

## Slide 17: Analog and Digital Signaling
digital signal – a sequence of voltage pulses that may be transmitted over a wire medium.
Note – analog signals to represent analog data and digital signals to represent digital data are not the only possibilities.

## Slide 18: Analog and Digital Signals
DCC 9th Ed.
Stallings
Notes: Stallings DCC9e Figure 3.1 shows an example of both analog or digital signals. The continuous signal might represent speech, and the discrete signal might represent binary 1s and 0s.

## Slide 19: Signals Details
Means by which data are propagated.
Analog Signals
  Continuously variable
  Various media
    wire, fiber optic, space
  Speech bandwidth 100Hz to 7kHz
  Telephone bandwidth 300Hz to 3400Hz
  Video bandwidth 4MHz
Digital Signals
  Use two DC components
DCC 6th Ed.
Stallings

## Slide 20: Analog and Digital Signaling
Digital data can be represented by analog signals using a modem (modulator/demodulator).
The digital data is encoded on a carrier frequency.
Analog data can be represented by digital signals using a codec (coder-decoder).

## Slide 21: PC Input Converted to Digital Signal
DCC 9th Ed.
Stallings
Notes: Finally, the third example described is the general case of binary data. Binary data is generated by terminals, computers, and other data processing equipment and then converted into digital voltage pulses for transmission, as illustrated in Stallings DCC9e Figure 3.13. A commonly used signal for such data uses two constant (dc) voltage levels, one level for binary 1 and one level for binary 0. (In Chapter 5, we shall see that this is but one alternative, referred to as NRZ.) Again, we are interested in the bandwidth of such a signal. This will depend, in any specific case, on the exact shape of the waveform and the sequence of 1s and 0s. We can obtain some understanding by considering Stallings DCC9e Figure 3.8 (compare Figure 3.7). As can be seen, the greater the bandwidth of the signal, the more faithfully it approximates a digital pulse stream.

## Slide 22: Analog Signals
Notes: Analog and Digital Signals
Stallings DCC9e Figure 3.14a shows a communications system, data are propagated from one point to another by means of electromagnetic signals. An analog signal is a continuously varying electromagnetic wave that may be propagated over a variety of media, depending on spectrum; examples are wire media, such as twisted pair and coaxial cable; fiber optic cable; and unguided media, such as atmosphere or space propagation

## Slide 23: Digital Signals
Notes: Data and Signals
In the foregoing discussion, we have looked at analog signals used to represent analog data and digital signals used to represent digital data. Generally, analog data are a function of time and occupy a limited frequency spectrum; such data can be represented by an electromagnetic signal occupying the same spectrum. Digital data can be represented by digital signals, with a different voltage level for each of the two binary digits.
As Stallings DCC9e Figure 3.14 illustrates, these are not the only possibilities. Digital data can also be represented by analog signals by use of a modem (modulator/demodulator). The modem converts a series of binary (two-valued) voltage pulses into an analog signal by encoding the digital data onto a carrier frequency. The resulting signal occupies a certain spectrum of frequency centered about the carrier and may be propagated across a medium suitable for that carrier. The most common modems represent digital data in the voice spectrum and hence allow those data to be propagated over ordinary voice-grade telephone lines. At the other end of the line, another modem demodulates the signal to recover the original data.
In an operation very similar to that performed by a modem, analog data can be represented by digital signals. The device that performs this function for voice data is a codec (coder-decoder). In essence, the codec takes an analog signal that directly represents the voice data and approximates that signal by a bit stream. At the receiving end, the bit stream is used to reconstruct the analog data.
Thus, Stallings DCC9e Figure 3.14 suggests that data may be encoded into signals in a variety of ways. We will return to this topic in Chapter 5.

## Slide 24: Analog and Digital Transmission
DCC 9th Ed.
Stallings
Notes: Analog and Digital Transmission
Both analog and digital signals may be transmitted on suitable transmission media. The way these signals are treated is a function of the transmission system. Stallings DCC9e Table 3.1 summarizes the methods of data transmission. Analog transmission is a means of transmitting analog signals without regard to their content; the signals may represent analog data (e.g., voice) or digital data (e.g., binary data that pass through a modem). In either case, the analog signal will become weaker (attenuate) after a certain distance. To achieve longer distances, the analog transmission system includes amplifiers that boost the energy in the signal. Unfortunately, the amplifier also boosts the noise components. With amplifiers cascaded to achieve long distances, the signal becomes more and more distorted. For analog data, such as voice, quite a bit of distortion can be tolerated and the data remain intelligible. However, for digital data, cascaded amplifiers will introduce errors.
Digital transmission, in contrast, assumes a binary content to the signal. A digital signal can be transmitted only a limited distance before attenuation, noise, and other impairments endanger the integrity of the data. To achieve greater distances, repeaters are used. A repeater receives the digital signal, recovers the pattern of 1s and 0s, and retransmits a new signal. Thus the attenuation is overcome.
The same technique may be used with an analog signal if it is assumed that the signal carries digital data. At appropriately spaced points, the transmission system has repeaters rather than amplifiers. The repeater recovers the digital data from the analog signal and generates a new, clean analog signal. Thus noise is not cumulative.
The question naturally arises as to which is the preferred method of transmission. The answer being supplied by the telecommunications industry and its customers is digital. Both long-haul telecommunications facilities and intrabuilding services have moved to digital transmission and, where possible, digital signaling techniques. The most important reasons:
Digital technology: The advent of large-scale integration (LSI) and very-large-scale integration (VLSI) technology has caused a continuing drop in the cost and size of digital circuitry. Analog equipment has not shown a similar drop.
Data integrity: With the use of repeaters rather than amplifiers, the effects of noise and other signal impairments are not cumulative. Thus it is possible to transmit data longer distances and over lower quality lines by digital means while maintaining the integrity of the data.
Capacity utilization: It has become economical to build transmission links of very high bandwidth, including satellite channels and optical fiber. A high degree of multiplexing is needed to utilize such capacity effectively, and this is more easily and cheaply achieved with digital (time division) rather than analog (frequency division) techniques. This is explored in Chapter 8.
Security and privacy: Encryption techniques can be readily applied to digital data and to analog data that have been digitized.
Integration: By treating both analog and digital data digitally, all signals have the same form and can be treated similarly. Thus economies of scale and convenience can be achieved by integrating voice, video, and digital data.

## Slide 25: Analog vs Digital Signaling
Digital signaling is:
Cheaper
Less susceptible to noise interference
Suffers more attenuation.

## Slide 26: Attenuation
Attenuation of a signal::
the reduction or loss of signal strength (power) as it is transferred across a system.
Attenuation is an increasing function of frequency.
The strength of the received signal must be strong enough for detection and must be higher than the noise to be received without error.

## Slide 27: Attenuation

## Slide 28: Attenuation vs Frequency
Attenuation (dB/mi)
f (kHz)
19 gauge
22 gauge
24 gauge
26 gauge
6
12
3
9
15
18
21
24
27
30
1
10
100
1000
Leon-Garcia & Widjaja:
Communication Networks

## Slide 29: Analog and Digital Transmissions
{Stalling’s third context}
3. Transmissions :: communication of data by the propagation and processing of signals.
Both analog and digital signals may be transmitted on suitable transmission media.
[Stalling’s argument] The way the signals are “treated” is a function of the transmission system and here lies the crux of the distinction between transmission types.

## Slide 30: Analog vs Digital Transmission
(a) Analog transmission: all details must be reproduced accurately
Sent
Sent
Received
Received
  e.g digital telephone, CD Audio
(b) Digital transmission: only discrete levels need to be reproduced
  e.g. AM, FM, TV transmission
Leon-Garcia & Widjaja:
Communication Networks

## Slide 31: Analog Transmissions
Analog transmission:: a means of transmitting analog signals without regard to their content (i.e., the signals may represent analog data or digital data).
  Transmissions are attenuated over distance.
Analog signal – the analog transmission system uses amplifiers to boost the energy in the signal.

## Slide 32: Analog Transmissions
Amplifiers boost the energy  this
amplifies the signal and amplifies the noise.
The cascading of amplifiers distorts the signal.
Note – voice (analog data) can tolerate much distortion but with digital data, distortion introduces errors.

## Slide 33: Digital Transmissions
Digital transmissions:: are concerned with the content of the signal. Attenuation is overcome without amplifying the noise.
1. Analog signals {assumes digital data}:
With retransmission devices [analog repeater] at appropriate points the device recovers the digital data from the analog signal and generates a new clean analog signal.
the noise is not cumulative!!

## Slide 34: Digital Transmissions
2. digital signals - digital repeaters are used to attain greater distances.
The digital repeater receives the digital signal, recovers the patterns of 0’s and 1’s and retransmits a new digital signal.
The treatment is the same for analog and digital data.

## Slide 35: Analog vs Digital Transmission
Source
Amplifier
Amplifier
Analog Transmission
Source
Digital Transmission
Destination
Destination
Repeater
Repeater
Leon-Garcia & Widjaja:
Communication Networks

## Slide 36: Analog Transmissions
Equalizer
Recovered signal
+
residual noise
Amplifier
Amp.
Attenuated &
distorted signal
+
noise
Leon-Garcia & Widjaja:
Communication Networks

## Slide 37: Digital Transmissions
Amplifier
Equalizer
Timing
Recovery
Decision Circuit.
& Signal
Regenerator
Repeater (digital signal)
Leon-Garcia & Widjaja:
Communication Networks

## Slide 38: Digital vs Analog Transmissions
Digital transmission advantages
Superior cost of digital technology
  Low cost LSI/VLSI technology
  Repeaters versus amplifiers costs
Superior quality {Data integrity}
  Longer distances over lines with lower error rates
Capacity utilization
  Economical to build high bandwidth links
  High degree of multiplexing easier with digital techniques
    TDM (Time Division Multiplexing) is easier and
    cheaper than FDM (Frequency Division Multiplexing).
DCC 6th Ed.
Stallings

## Slide 39: Digital vs Analog Transmissions
Digital transmission advantages
Security & Privacy
  Encryption techniques readily applied to digitized data.
Integration
  Can treat analog and digital data similarly.
  Economies of scale come from integrating voice, video and data.
Analog transmission advantages
  Digital signaling not as versatile or practical (digital impossible for satellite and microwave systems).
  LAN star topology reduces the severity of the noise and attenuation problems.
DCC 6th Ed.
Stallings

## Slide 40: Physical Layer Summary (Part 1)
Definitions of bandwidth, capacity and modulation rate.
Nyquist Theorem
  noiseless channel, sampling rate
Shannon’s Result
  Channel with thermal noise, voice-grade line, SNR, constellations

## Slide 41: Physical Layer Summary (Part 1)
Analog versus Digital
  Data, signals, transmissions
  Attenuation of the signal as a function of transmission frequency.
Amplifier versus Repeater
  Effect of cascading amplifiers
  Analog and digital repeaters
Advantages/Disadvantages of Analog vs Digital Transmissions