## Slide 1: TinyOS Applications
Advanced Computer Networks

## Slide 2: TinyOS Applications Outline
AntiTheft Example
  LEDs, timer, booting
Sensing Example
  Light Sensor
  Wiring to AntiTheft
Single Hop Networks
  Active Messages interface
  Sending packets
  Receiving packets

## Slide 3: AntiTheft Example [List 6.1]
module AntiTheftC {
uses {
interface Boot;
interface Timer <Tmilli> as WarningTimer;
interface Leds;
}
}
implementation {
enum { WARN_INTERVAL = 4096, WARN_DURATION = 64 };
can only declare integer constants

## Slide 4: AntiTheft Example [List 6.1]
event void WarningTimer.fired ( ) {
if (call Leds.get ( ) & LEDS_LED0)
{ /* Red LED is on. Turn it off, will switch on again in 4096 – 64 ms. */
call Leds.led0Off ( );
call WarningTimer.startOneShot (WARN_INTERVAL –
WARN_DURATION);
}
else
{ // Red LED is off. Turn it on for 64 ms.
call Leds.led0On ( );
call WarningTimer.startOneShot (WARN_DURATION);
}
}

## Slide 5: AntiTheft Example [List 6.1]
event void Boot.booted ( ) {
/* We just booted. Perform first
LED transition */
signal WarningTimer.fired ( );
}
}
interface Leds { [List 6.2]
…
async command void led0On ( );
async command void led0Off ( );
async command uint8_t get ( );
}
software signal

## Slide 6: AntiTheft configuration [List 6.6]
configuration AntiTheftAppC { }
implementation {
components AntiTheftC, MainC, LedsC;
components new TimerMilliC ( ) as WTimer;
AntiTheftC.Boot -> MainC;
AntiTheftC.Leds -> LedsC;
AntiTheftC.WarningTimer -> WTimer;
}

## Slide 7: Sensing Example
TinyOS provides two standard interfaces for reading sensor samples
  Read :: acquire a single sample
  ReadStream :: sample at a fixed rate.
interface Read <val_t> {
command error_t read ( );
event void readDone (error_t, val_t val );
}

## Slide 8: Sensing Example [List 6.8]
module DarkC {
uses {
interface Boot;
interface Leds;
interface Timer<TMilli> as TheftTimer;
interface Read<uint16_t> as Light;
}
}

## Slide 9: Sensing Example [List 6.8]
implementation {
enum { DARK_INTERVAL = 256, DARK_THRESHOLD = 200};
event void Boot.booted ( ) {
call TheftTimer.startPeriodic (DARK_INTERVAL);
}
event void TheftTimer.fired ( ) {
call Light.read ( ); //Initiate split-phase light sampling
}

## Slide 10: Sensing Example [List 6.8]
/* Light sample completed. Check if it is a theft. */
event void Light.readDone (error_t ok,uint16_t val) {
if (ok == SUCCESS && val < DARK_THRESHOLD)
call Leds.led2On ( ); /* Alert! Alert! */
else
call Leds.led2Off( ); /* Don’t leave LED on */
}
}

## Slide 11: Sensor Components
Sensors are represented in TinyOS by generic components, e.g., PhotoC for the light sensor on the mts310 board.
generic configuration PhotoC ( ) {
provides interface Read<uint16_t>;
}

## Slide 12: AntiTheft Light Sensor Wiring [List 6.9]
configuration AntiTheftAppC { }
implementation {
… /* the wiring for the blinking Red LED */
components DarkC;
components new TimerMilliC ( ) as TTimer;
components new PhotoC ( );
DarkC.Boot -> MainC;
DarkC.Leds -> LedsC;
DarkC.TheftTimer -> TTimer;
DarkC.Light -> PhotoC;
}

## Slide 13: Single Hop Networks
TinyOS uses a layered network structure where each layer defines a header and footer layout.
The lowest exposed network layer in TinyOS is called active messages (AM).
AM is typically implemented directly over a mote’s radio providing unreliable, single hop packet transmission and reception.

## Slide 14: Single Hop Networks
Packets are identified by an AM type, an 8-bit packet type.
‘Active Messages’ indicates the type is used automatically to dispatch received packets to an appropriate handler.
Each packet holds a user-specified payload of up to TOSH_DATA_LENGTH bytes (normally 28 bytes)**.
A variable of type message_t holds a single AM packet.
** changeable at compile time.

## Slide 15: Platform-Independent Types
TinyOS has traditionally used structs to define message formats and directly access messages.
Platform-independent structs are declared with nx_struct and every field of a platform-independent struct must be a platform-independent type.
nx_uint16_t val ; // A big-endian 16-bit value
nxle_uint32_t otherval; // A litte-endian 32-bit value

## Slide 16: TinyOS 2.0 CC2420 Header [List 3.32]
typedef nx_struct cc2420_header_t ** {
nxle_uint8_t length;
nxle_uint16_t fcf;
nxle_uint8_t dsn;
nxle_uint16_t destpan;
nxle_uint16_t dest;
nxle_uint16_t src;
nxle_uint8_t type;
} cc2420_header_t;
The CC2420 expects all fields to be little-endian.

## Slide 17: Theft Report Payload
Platform-independent struct in the antitheft.h header file:
#ifndef ANTITHEFT_H
#define ANTITHEFT_H
typedef nx_struct theft {
nx_uint16_t who;
} theft_t;
…
#endif
struct to define payload

## Slide 18: AMSend Interface [List 6.12]
Contains all the commands needed to fill in and send packets:
interface AMSend {
command error_t send (am_addr_t addr, message_t* msg, uint8_t len);
event void sendDone (message_t* msg, error_t error);
command error_t cancel (message_t* msg);
command uint8_t maxPayLoadLength ( );
command void* getPayLoad (message_t* msg, uint8_t len);
}

## Slide 19: Sending Report-Theft Packets [List 6.13]
uses interface AMSend as Theft;
…
message_t reportMsg;
bool sending;
void reportTheft ( ) {
theft_t* payload = call Theft.getPayload (&reportMsg,
sizeof (theft_t) );
if (payload && !sending)
{ //Payload fits and we are idle – Send packet
payload->who = TOS_NODE_ID; //Report being stolen!
//Broadcast the report packet to everyone
if (call Theft.send(TOS_BCAST_ADDR, &reportMsg,
sizeof (theft_t) ) == SUCCESS)
}
}

## Slide 20: Sending Report-Theft Packets [List 6.13]
event void Theft.sendDone (message_t *msg,
error_t error) {
sending = FALSE; //Our send completed
}

## Slide 21: Generic AMSenderC configuration
generic configuration AMSenderC (am_id_t AMId) {
provides {
interface AMSend;
interface Packet;
interface AMPacket;
interface PacketAcknowledgements as Acks;
}
}

## Slide 22: Communication Stack
Cannot switch itself on and off on-demand, and needs the SplitControl interface to start and stop the radio:
interface SplitControl { [List 6.14]
command error_t start ( );
event void startDone (error_t error);
command error_t stop ( );
event void stopDone (error_t error);
}

## Slide 23: MovingC using SplitControl
uses interface SplitControl as CommControl;
…
event void Boot.booted ( ) {
call CommControl.start ( ) ;
}
event void CommControl.startDone (error_t ok) {
//Start checks once communication stack is ready
call TheftTimer.startPeriodic (ACCEL_INTERVAL);
}
event void CommControl.stopDone (error_t ok) { }

## Slide 24: Moving C Receiving Packet
MovingC receives a packet payload (defined as a struct contained in a header file) that contains acceleration settings for detecting movement of the mote:
typedef nx_struct settings {
nx_uint16_t accerVariance;
nx_uint16_t accelInterval;
} settings_t;
struct to define payload

## Slide 25: AM Packet Reception
Provided by the TinyOS Receive interface:
interface Receive {
event message_t* receive(message_t* msg,
void* payload, uint8_t len);
}
Receive.receive, as a receive “handler”, receives a packet buffer which it can simply return or return as a different buffer if the handler wants to hold onto buffer.

## Slide 26: MovingC Receiving Packet [List 6.16]
uses interface Receive as Setting;
…
uint16_t accelVariance = ACCEL_VARIANCE;
event message_t *Settings.receive (message_t *msg,
void *payload, uint8_t len) {
if (len >= sizeof (settings_t)) //Check for valid packet
{ /* Read settings by casting payload to settings_t,
reset check interval */
settings_t *settings = payload;
accelVariance = setting->accelVariance;
call TheftTimer.startPeriodic (setting->accelInterval);
}
return msg;
}

## Slide 27: TinyOS Applications Summary
AntiTheft Example
  LEDs, Timer, Boot
  get, enum
Sensing Example
  Light Sensor
  Read (split-phase)
  Wiring to AntiTheft
  Two Timer instances

## Slide 28: TinyOS Applications Summary
Single Hop Networks
  Active Messages, typed messages
  Platform-independent types
Sending packets
  AMSenderC generic configuration
  SplitControl of Radio Stack
  Structs for packet payloads
Receiving packets
  Implemented as a receive event handler.